| Stuart Petroleum Limited | BAZZARD-1 |
| --- | --- |
| Report Date: | 02 October 2008 | Bit Diameter: | 311.1 mm (12.25”) |
| Report Number: | 10 | Last Casing: | 399 mm (13-3/8”) @ 841 m |
| Spud Date: | 20 September 2008 | LOT: | 15.06 ppg at 853m |
| Days from Spud: | 11 | Mud Weight: | 9.5 |
| Current Activity (06:00 hours): | POOH BHA | ECD: | 9.9 |
| Water Depth: | 68 m | Mud Type: | KCl / PHPA |
| Rotary Table: | 38.5 m above AHD. | Last Survey: | 2846.49m incl 0.04° azim 239.3° |

| Time / Date | m MDRT | m TVDRT | Previous, m | Progress, m | Drill rate m/hr |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Minimum | Maximum | Average |
| 06:00 hrs, 02/10/08 | 2859 | 2858.4 | 2712 | 147 | 3.0 | 59.7 | 17.5 |

| Depth m MDRT | Description | Gas Data (total gas in %; C1, C2, C3, iC4, nC4, iC5, nC5 in ppm), C1/2/3/4/5/ ratios indicated below. |
| --- | --- | --- |
| 2705-2730 | KINGFISH FORMATION (cont.): SILTSTONE (60-75%): pale to moderate olive brown to medium grey, firm to hard, argillaceous to carbonaceous, non calcareous, trace coal fragments, minor pyrite. Trace pale grey firm slightly sandy siltstone, trace mica flakes. SANDSTONE (20-35%): Very light grey to light to medium brownish grey, firm to moderately hard, very fine lower to upper sandstone, well sorted subangular quartz and trace mica in silty matrix, weakly silica cemented, common carbonaceous laminae. Common white to pale grey loose very fine to medium sand, dominantly fine, moderately sorted, subrounded quartz. CLAYSTONE (5%): light to medium grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. COAL (10% at 2720m): dark brown to black, blocky, firm. | 0.12, 501/26/54/8/8/3/1.3 83/4/9/3/1 |
| 2730-2745 | SILTSTONE (50-75%): moderate olive brown to medium grey, firm to hard, argillaceous to carbonaceous, non calcareous, trace coal fragments, minor pyrite. Trace pale grey firm slightly sandy siltstone, trace mica flakes, trace carbonaceous laminae. SANDSTONE (10-30%): very light grey to light to medium brownish grey, firm to moderately hard, very fine lower to upper sandstone, well sorted subangular quartz and trace mica in silty matrix, weakly silica cemented, common carbonaceous laminae. With minor loose very fine to medium sand, trace quartz granules. CLAYSTONE (5%): light to medium grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. COAL (Tr to 30% at 2735m): dark brown to black, hackly to conchoidal fracture, dull to brightly banded. | 0.13, 530/38/54/9/11/3/1.3 82/6/8/3/1 |
| 2745-2760 | SILTSTONE (45-55%): pale to moderate olive brown to medium grey, firm to hard, argillaceous to carbonaceous, non calcareous, trace coal fragments, minor pyrite. Trace pale grey firm slightly sandy siltstone, trace mica flakes. SANDSTONE (40-50%): White to pale grey loose very fine to coarse sand, dominantly medium, moderately sorted, subrounded quartz. Common very light grey to light to medium brownish grey, firm to moderately hard, very fine lower to upper sandstone, well sorted subangular quartz and trace mica in silty matrix, weakly silica cemented, common carbonaceous laminae. CLAYSTONE (5%): light to medium grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. | 0.13, 517/11/59/10/10/3/1.4 85/2/9/3/1 |
| 2760-2790 | SILTSTONE (35-85%): moderate olive brown to medium grey, firm to hard, argillaceous to carbonaceous, non calcareous, trace coal fragments, minor pyrite. Trace pale grey firm slightly sandy siltstone, trace mica flakes, trace carbonaceous laminae. SANDSTONE (5-35%): very light grey to light to medium brownish grey, firm to moderately hard, very fine lower to upper sandstone, well sorted subangular quartz and trace mica in silty matrix, weakly silica cemented, common carbonaceous laminae. With minor loose very fine to medium sand, trace quartz granules. CLAYSTONE (5-35%): light to medium grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. COAL (Tr-10% at 2775m): dark brown to black, hackly to conchoidal fracture, dull to brightly banded. | 0.14, 563/37/64/11/8/3/1.4 82/6/9/3/21 |
| 2790-2800 Drill break at 2789m 10-60m/hr | SANDSTONE (90-95%): very light grey to light to medium brownish grey, loose fine to granule sand, predominantly medium to lower coarse, moderately sorted, subangular to subrounded, subspherical quartz. ~10% aggregates of yellowish-grey, moderately firm, moderately silica cemented fine sand. Trace pyrite, trace coal. SILTSTONE (5-10%): moderate olive brown to medium grey, firm to hard, argillaceous to carbonaceous, non calcareous, trace coal fragments, minor pyrite. Trace pale grey firm slightly sandy siltstone, trace mica flakes, trace carbonaceous laminae. Trace claystone. | 0.13, 552/16/67/10/12/3/1.7 84/10/2/3/1 |
| 2800-2859 | SILTSTONE (45-95%): moderate olive brown to medium grey, firm to hard, argillaceous to carbonaceous, non calcareous, trace coal fragments, minor pyrite. Trace pale grey firm slightly sandy siltstone, trace mica flakes, trace carbonaceous laminae. SANDSTONE (0-45%): very light grey to light to medium brownish grey, firm to moderately hard, very fine lower to upper sandstone, well sorted subangular quartz and trace mica in silty matrix, weakly silica cemented, common carbonaceous laminae. With minor loose very fine to medium sand, trace subangular quartz granules. CLAYSTONE (5-35%): light to medium grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. COAL (10-20% at 2810-2825m, 5% at 2835-2840m): dark brown to black, hackly to conchoidal fracture, dull to brightly banded. | 0.13, 599/15/65/10/13/3/2 85/2/9/3/1 |

| Depth m MDRT | Fluorescence | Cut | Residue ring / film |
| --- | --- | --- | --- |
| 2735-2740, 2770-2785 | Trace yellow-green fluorescence associated with coal resin. | Very slow blooming, blue-white cut fluorescence. | Dull pale blue-white fluorescing residual ring, nil visible residue. |
| 2825-2830 | Trace yellow green pinpoint fluorescence in medium grey siltstone. | Very slow blooming white-blue cut fluorescence. | Dull white blue fluorescing residual ring, nil visible residue. |

| (m MDRT) | Total Gas (%) | Methane (ppm) | Ethane (ppm) | Propane (ppm) | i-Butane (ppm) | n-Butane (ppm) | i-Pentane (ppm) | n-Pentane (ppm) | % Ratios (C1/2/3/4/5) | Type |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2712-2859 | 0.13 | 573 | 24 | 63 | 10 | 11 | 3 | 2 | 84/3/9/3/1 | BG |
| 2839.5 | 0.59 | 4108 | 18 | 293 | 34 | 34 | 7 | 3 | 91/0/7/2/0 | FMG |

KEY: BG Background gas, CG Connection gas,   POG Pumps-off gas, TG Trip gas, STG Short trip gas, FMG Formation gas

| From m MDRT | To m MDRT | Total or Rate (bbl) | Remarks |
| --- | --- | --- | --- |
|  |  |  | Normal surface losses plus intermittent high losses on solid control equipment. No downhole losses. |

Run 2 MWD / LWD string as follows: Resistivity: 3.98m, ARC Gamma 4.03m, D&I (survey) 11.54m, Sonic 21.01m, SADN Density 25.51m, SADN Porosity 28.37m LWD RT data quality good for gamma, resistivity. No RT data for other tools. Sonic tool operating on batteries. No recording on SADN anticipated.

| Formation (Unit) | Prognosed MDRT SS, m | Actual MDRT TVDSS, m | Actual Thickness | Difference to Prog (TVDSS) | Basis Of Pick |
| --- | --- | --- | --- | --- | --- |
| Gippsland Limestone | 106 | -68 | 106.5 | -68 | 1803.4 | 0 | Sea-floor |
| Lakes Entrance | 1918.5 | -1880 | 1910 | -1871.4 | 189.8 | -8.6 | Slight increase in gamma, subtle change in cuttings |
| Latrobe Group: |  |  |  |  |  |  |  |
| Gurnard Formation | 2097.5 | -2059 | 2010 | -2061.2 | 27 | +2.2 | Greensand in cuttings |
| Kingfish Formation | 2132.5 | -2094 | 2127 | -2088.2 |  | -5.8 | Drill break, coarse quartz sand in cuttings |
| 54-5 Sand | 2513.5 | -2475 | 2537? | -2497.9 |  | +22.9 | Drill break, low gamma interval |
| 62 Sand | 2798.5 | -2760 | 2789? | -2749.9 |  | -10.1 | Drill break, coarse quartz sand in cuttings |
| Volador Fm 66.5 Sand | 2978.5 | -2940 |  |  |  |  |  |
| 67 Sand | 3218.5 | -3180 |  |  |  |  |  |
| 70 Sand | 3438.5 | -3400 |  |  |  |  |  |
| TD | 3501.5 | -3463 |  |  |  |  |  |

Drill to 2859m at 22:30 hrs 01/10/08, POOH for new bit and LWD tools. Tops for Kingfish Formation Sands are wellsite picks subject to verification by Operations Geologist.

Geologists:  Simon Ward / Roman Leslie

# Text boxes

Lithology Summary:

Drilling Summary:

Oil Fluorescence Summary:

Gas Summary:

Fluid Loss:

MWD Summary:

Wellsite Formation Picks:

Comments: