| Stuart Petroleum Limited | BAZZARD-1 |
| --- | --- |
| Report Date: | 04 October 2008 | Bit Diameter: | 311.1 mm (12.25”) |
| Report Number: | 12 | Last Casing: | 399 mm (13-3/8”) @ 841 m |
| Spud Date: | 20 September 2008 | LOT: | 15.06 ppg at 853m |
| Days from Spud: | 13 | Mud Weight: | 10.1 |
| Current Activity (06:00 hours): | Drill ahead 311 mm (12-1/4”) hole | ECD: | 10.5 |
| Water Depth: | 68 m | Mud Type: | KCl / PHPA |
| Rotary Table: | 38.5 m above AHD. | Last Survey: | 2878.15m incl 0.10° azim 323.43° |

| Time / Date | m MDRT | m TVDRT | Previous, m | Progress, m | Drill rate m/hr |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Minimum | Maximum | Average |
| 06:00 hrs, 02/10/08 | 2960 | 2959.4 | 2859 | 101 | 7.7 | 49.8 | 21.4 |

| Depth m MDRT | Description | Gas Data (total gas in %; C1, C2, C3, iC4, nC4, iC5, nC5 in ppm), C1/2/3/4/5/ ratios indicated below. |
| --- | --- | --- |
| 2859-2885 | Kingfish Formation (cont.) SANDSTONE (20-70%): loose medium to granule dominantly medium poorly to moderately sorted subrounded quartz grains, trace muscovite flakes, trace calcareous fragments, trace to common loose pyrite crystals, with minor to abundant white to pale grey to yellowish grey fine to coarse (dom medium) aggregates, moderately sorted, subangular to subrounded quartz in minor silty matrix, minor silica cement, friable to firm, trace pyrite cement, trace carbonaceous fragments, nil visible porosity. SILTSTONE (30-80%): moderate olive brown to medium grey, firm to hard, argillaceous to carbonaceous, non calcareous, trace coal fragments. Trace pale grey firm slightly sandy siltstone, trace mica flakes. | 0.09, 447/37/35/3/5/1/1 84/7/7/2/0 |
| 2885-2895 | SILTSTONE (90%): medium to dark brownish grey, medium greenish grey in parts, firm to moderately hard, argillaceous, non-calcareous, glauconitic in parts with patchy to nodular glauconite, trace to common pyrite (trace to common disseminated, common microcrystalline clusters, trace cubic crystal clusters and trace pyrite cemented glauconite) SANDSTONE (10%): loose fine to granular quartz, minor very fine to fine sandstone. | 0.09, 338/31/39/4/6/1/1 89/7/9/2/1 |
| 2895-2905 | SANDSTONE (80-90%): loose medium to granule dominantly medium upper moderately sorted subrounded quartz grains, trace muscovite flakes, trace calcareous fragments, trace pyrite crystals, with minor white to pale grey to yellowish grey fine to coarse (dom medium) aggregates, moderately sorted, subangular to subrounded quartz in minor silty matrix, minor silica cement, friable to firm, trace pyrite cement, trace carbonaceous fragments, nil visible porosity. SILTSTONE (10-20%): moderate olive brown to medium grey, firm to hard, argillaceous to carbonaceous, non calcareous, trace coal fragments. Trace pale grey firm slightly sandy siltstone, trace mica flakes. | 0.09, 455/25/29/3/5/1/1 88/5/6/1/0 |
| 2905-2910 | SILTSTONE (90%): olive brown to medium brownish grey, firm to hard, argillaceous to carbonaceous, non calcareous. Trace pale grey firm slightly sandy siltstone, trace mica flakes. COAL (10%): dark brown to black, firm, blocky, conchoidal fracture. | 0.15, 544/40/41/5/7/1/1 85/6/6/2/1 |
| 2910-2920 | SILTSTONE (70-80%): light olive brown to medium brownish grey, firm to hard, argillaceous to carbonaceous, non calcareous, minor pyrite. Trace pale grey firm slightly sandy siltstone, trace mica flakes. SANDSTONE (20-30%): light grey, blocky, firm to hard, very fine to fine, moderately sorted, subangular to subrounded quartz and trace mica in minor silty matrix, weakly silica cemented, non-calcareous, trace carbonaceous fragments, poor visible porosity. Minor loose very fine to fine sand. | 0.19, 938/99/96/10/12/2/1 81/9/8/2/0 |
| 2920-2940 | SANDSTONE (75-90%, 50% at 2935m): loose fine to medium well sorted subrounded quartz grains, trace feldspar, trace muscovite flakes, trace pyrite crystals, with common white to pale grey medium sandstone aggregates, well sorted, subangular to subrounded quartz in minor silty matrix, minor silica cement, friable to firm, trace pyrite cement, trace carbonaceous fragments, poor to visible porosity. Minor soft white rock flour inferred to be from sandstone. SILTSTONE (10-25%, 45% at 2935m): moderate olive brown to medium grey, firm to hard, argillaceous to carbonaceous, non calcareous, trace coal fragments. Trace pale grey firm slightly sandy siltstone, trace mica flakes. COAL (5% below 2930m): black, firm to hard. | 0.15, 755/71/75/10/11/2/1 82/8/8/2/0 |
| 2940-2950 | SILTSTONE (70%): moderate olive brown to medium grey, firm to hard, argillaceous to carbonaceous, non calcareous, trace coal fragments. Common pale grey firm slightly sandy siltstone, trace mica flakes. SANDSTONE (30%): white to pale grey aggregates, very fine, well sorted, subangular to subrounded quartz in common silty matrix, minor silica cement, firm to hard, trace pyrite cement, trace carbonaceous fragments, poor visible porosity. Trace loose fine to medium sand. | 0.11, 520/41/58/8/9/2/1 81/6/9/3/1 |
| 2950-2955 | SILTSTONE (60%): light to moderate olive brown to medium grey, firm to hard, argillaceous to carbonaceous, non calcareous. Common pale grey firm slightly sandy siltstone, trace mica flakes. COAL (40%): black, firm to hard, bright banded, conchoidal to planar fractures. | See below for gas peak. |

| Depth m MDRT | Fluorescence | Cut | Residue ring / film |
| --- | --- | --- | --- |
| 2910-2915 | Trace dull greenish yellow pinpoint fluorescence in silty very fine sandstone | Slow blooming moderately bright blue-white cut fluorescence | Moderately thick bright blue-white fluorescing residual ring, nil visible residue. |

| (m MDRT) | Total Gas (%) | Methane (ppm) | Ethane (ppm) | Propane (ppm) | i-Butane (ppm) | n-Butane (ppm) | i-Pentane (ppm) | n-Pentane (ppm) | % Ratios (C1/2/3/4/5) | Type |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2909 | 0.64 | 1089 | 110 | 80 | 9 | 12 | 2 | 1 | 84/8/6/2/0 | FMG |
| 2952 | 0.79 | 3239 | 352 | 172 | 20 | 15 | 4 | 2 | 85/9/5/1/0 | FMG |
| 2859-2960 | 0.13 | 736 | 64 | 61 | 7 | 8 | 1 | 1 | 84/7/7/2/0 | BG |

KEY: BG Background gas, CG Connection gas,   POG Pumps-off gas, TG Trip gas, STG Short trip gas, FMG Formation gas

| From m MDRT | To m MDRT | Total or Rate (bbl) | Remarks |
| --- | --- | --- | --- |
|  |  |  | No losses recorded during tripping. Surface losses while reaming and drilling. Minor seepage losses noted while drilling sandstone sections. |

Run 3 MWD / LWD string as follows: Resistivity: 3.97m, ARC Gamma 4.02m, D&I (survey) 11.53m, Sonic 20.98m, SADN Density 26.92m, SADN Porosity 28.90m Using Powerpulse MWD. No RT SADN data available, other tools fully functional. RT sonic data noisy due to stick-slip. SADN battery anticipated to last approximately 24 hours from 07:00 4th October.

| Formation (Unit) | Prognosed MDRT SS, m | Actual MDRT TVDSS, m | Actual Thickness | Difference to Prog (TVDSS) | Basis Of Pick |
| --- | --- | --- | --- | --- | --- |
| Gippsland Limestone | 106 | -68 | 106.5 | -68 | 1803.4 | 0 | Sea-floor |
| Lakes Entrance | 1918.5 | -1880 | 1910 | -1871.4 | 189.8 | -8.6 | Slight increase in gamma, subtle change in cuttings |
| Latrobe Group: |  |  |  |  |  |  |  |
| Gurnard Formation | 2097.5 | -2059 | 2099.2 | -2061.2 | 27.8 | +2.2 | Greensand in cuttings |
| Kingfish Formation | 2132.5 | -2094 | 2127 | -2088.2 |  | -5.8 | Drill break, coarse quartz sand in cuttings |
| 54-5 Sand | 2513.5 | -2475 | 2537? | -2497.9 |  | +22.9 | Drill break, low gamma interval |
| 62 Sand | 2798.5 | -2760 | 2789? | -2749.9 |  | -10.1 | Drill break, coarse quartz sand in cuttings |
| Volador Fm 66.5 Sand | 2978.5 | -2940 |  |  |  |  |  |
| 67 Sand | 3218.5 | -3180 |  |  |  |  |  |
| 70 Sand | 3438.5 | -3400 |  |  |  |  |  |
| TD | 3501.5 | -3463 |  |  |  |  |  |

Continue washing and reaming to TD from 2200m. Commence drilling 22:40 hrs. No Trip Gas recorded. Gas peak at 2909m likely from thin coal at base of sandy interval 2892-2907m, very brief peak interrupted by connection, not sampled by chromatograph. Minor gas increases observed correlate with thin intervals of higher resistivity which may represent thin coal intervals. Gas peak at 2952m from coal 2949-2952m on gamma log.

Geologists:  Simon Ward / Roman Leslie

# Text boxes

Lithology Summary:

Drilling Summary:

Oil Fluorescence Summary:

Gas Summary:

Fluid Loss:

MWD Summary:

Wellsite Formation Picks:

Comments: