| Stuart Petroleum Limited | BAZZARD-1 |
| --- | --- |
| Report Date: | 05 October 2008 | Bit Diameter: | 311.1 mm (12.25”) |
| Report Number: | 13 | Last Casing: | 399 mm (13-3/8”) @ 841 m |
| Spud Date: | 20 September 2008 | LOT: | 15.06 ppg at 853m |
| Days from Spud: | 14 | Mud Weight: | 10.0 |
| Current Activity (06:00 hours): | Drill ahead 311 mm (12-1/4”) hole | ECD: | 10.4 |
| Water Depth: | 68 m | Mud Type: | KCl / PHPA |
| Rotary Table: | 38.5 m above AHD. | Last Survey: | 3203.64m incl 0.67° azim 322.06° |

| Time / Date | m MDRT | m TVDRT | Previous, m | Progress, m | Drill rate m/hr |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Minimum | Maximum | Average |
| 06:00 hrs, 05/10/08 | 3215 | 3214.4 | 2960 | 255 | 3.2 | 58.1 | 15.7 |

| Depth m MDRT | Description | Gas Data (total gas in %; C1, C2, C3, iC4, nC4, iC5, nC5 in ppm), C1/2/3/4/5/ ratios indicated below. |
| --- | --- | --- |
| 2955-2960 | SILTSTONE (95%): dark brown to brownish black, firm to hard, blocky, argillaceous to carbonaceous, non calcareous, trace very fine sand in parts, trace coal fragments, minor pyrite. COAL (5%): black, flakey. | 0.47, 3073/244/184/21/11/3/1 87/7/5/1/0 |
| 2960-3005 | SILTSTONE (30-80%): dark brown to brownish black, firm to hard, blocky, argillaceous to carbonaceous, non calcareous, trace very fine sand in parts, trace coal fragments, minor pyrite. SANDSTONE (20-70%): white to pale grey aggregates, very fine to fine, well sorted, subangular to subrounded quartz in common silty matrix, minor silica cement, firm to hard, trace pyrite cement, trace carbonaceous fragments, poor visible porosity. Trace loose fine to medium sand. Minor rock flour inferred to be derived from sandstone. Trace coal. | 0.97, 1159/104/96/13/13/3/1.7 83/8/7/2/0 |
| 3005-3010 | COAL (70%): black, flakey, planar to conchoidal fracture, bright. SILTSTONE (30%): dark brown to brownish black, firm to hard, blocky, argillaceous to carbonaceous, non calcareous, trace very fine sand in parts, minor pyrite. | 0.23, 1222/120/107/12/14/3/2 83/8/7/2/0 |
| 3010-3015 | SANDSTONE (60%): loose very fine to fine moderately sorted subrounded quartz grains, trace feldspar, trace muscovite flakes, trace pyrite crystals, with adundant white to pale grey fine sandstone aggregates, well sorted, subangular to subrounded quartz in common silty matrix, minor silica cement, friable to firm, trace pyrite cement, trace carbonaceous fragments, poor visible porosity. Minor soft white rock flour inferred to be from sandstone. SILTSTONE (35%): dark brown to brownish black, firm to hard, blocky, argillaceous to carbonaceous, trace very fine sand in parts, trace coal fragments, minor pyrite. COAL (5%): black, flakey, planar to conchoidal fracture, bright. | 0.72, 5850/604/223/22/19/4/2.4 87/9/3/1/0 |
| 3015-3025 | SILTSTONE (80-100%): medium brown to brownish black, firm to hard, blocky, argillaceous to carbonaceous, non calcareous, trace very fine sand in parts, trace coal fragments, minor pyrite. Trace loose fine to medium sand. COAL (0-20%): dark brown to black, firm, blocky, conchoidal fracture. | 0.43, 1596/154/133/16/20/4/2 83/8/7/2/0 |
| 3025-3090 | SANDSTONE (0-90%): loose fine to coarse, moderately sorted subrounded quartz grains, trace feldspar, trace muscovite flakes, trace pyrite crystals and white to pale grey fine to medium sandstone aggregates, moderately to well sorted, subangular to subrounded quartz in common silty matrix, weak to moderate silica cement with dolomite (?) cement at 3070m, friable to firm, trace pyrite cement, trace carbonaceous fragments, poor visible porosity. Minor soft white rock flour inferred to be from sandstone. SILTSTONE (5-100%): dark brown to brownish black, firm to hard, blocky, argillaceous to carbonaceous, trace very fine sand in parts, trace coal fragments, minor pyrite. COAL (Tr-90% at 3085m): black, flakey, planar to conchoidal fracture, bright banded. | 0.33, 2035/209/126/15/18/4/2.7 85/9/5/1/0 |
| 3090-3120 | SANDSTONE (70-80%): loose fine to coarse dominantly medium (upper), moderately sorted subrounded quartz grains, trace feldspar, trace muscovite flakes, trace pyrite crystals and white to pale grey fine to medium sandstone aggregates, well sorted, subangular to subrounded quartz in common silty matrix, minor silica cement, friable to firm, trace pyrite cement, trace carbonaceous fragments, poor visible porosity. Minor soft white rock flour inferred to be from sandstone. Trace coal. SILTSTONE (5-25%): dark brown to brownish black, firm to hard, blocky, argillaceous to carbonaceous, trace very fine sand in parts, trace coal fragments, minor pyrite. CLAYSTONE (5-20%): light to medium grey, moderately soft, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. | 0.19, 1245/68/73/9/16/4/3 88/5/5/2/0 |
| 3120-3190 | SANDSTONE (35-90%): loose fine to granule dominantly medium lower, common to abundant granules, poorly sorted subanglular quartz grains, trace feldspar, trace muscovite flakes, rare white to pale medium sandstone aggregates, moderately sorted, subangular to subrounded quartz in common silty matrix, moderate silica cement, friable to firm, trace carbonaceous fragments, poor visible porosity. Minor to common soft white rock flour inferred to be from sandstone. Trace coal. SILTSTONE (5-40%): dark brown to brownish black, firm to hard, blocky, argillaceous to carbonaceous, trace very fine sand in parts, trace coal fragments, trace to common pyrite. CLAYSTONE (5-35% to 3140m, then nil): light to medium grey, moderately soft, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. | 0.15, 910/24/36/4/9/2/2 92/2/4/2/0 |
| 3190-3210 | SILTSTONE (90%, decreasing to 25%): dark brownish grey, firm to hard, blocky, argillaceous, trace very fine sand, trace carbonaceous fragments, minor to common pyrite. SANDSTONE (10-75%): pale grey to white loose fine to medium sand, well sorted, subangular to subrounded quartz, trace feldspar, trace mica, trace coaly fragments. Minor aggregates with soft silty matrix. | 0.15, 832/24/46/2/6/1/1 91/3/5/1/0 |

| Depth m MDRT | Fluorescence | Cut | Residue ring / film |
| --- | --- | --- | --- |
| 3005-3010 | Trace moderately bright yellow pinpoint fluorescence in siltstone and coal | Moderately fast blooming moderately bright blue white cut fluorescence | Thin to wide moderately bright to bright green blue fluorescing residual ring, nil visible residue. |
| 3065-3070 | 5% very dull greenish yellow pinpoint fluorescence in fine sandstone. | Very slow blooming very dull blue white cut fluorescence. | Thin moderately dull blue white fluorescing residual ring, nil visible residue. |
| 3125-3130 | Trace very dull greenish yellow pinpoint fluorescence in fine siltstone. | Very slow blooming very dull blue white cut fluorescence. | Thin moderately bright blue white fluorescing residual ring, nil visible residue. |
| 3185-3190 | Trace bright greenish yellow pinpoint fluorescence in fine siltstone. | Slow blooming moderately bright blue white cut fluorescence. | Wide moderately bright blue white fluorescing residual ring, very pale yellow visible residue. |

| (m MDRT) | Total Gas (%) | Methane (ppm) | Ethane (ppm) | Propane (ppm) | i-Butane (ppm) | n-Butane (ppm) | i-Pentane (ppm) | n-Pentane (ppm) | % Ratios (C1/2/3/4/5) | Type |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2969 | 0.97 | 5003 | 513 | 232 | 30 | 18 | 4 | 2 | 86/9/4/1/0 | FMG |
| 3009.5 | 1.13* | 8963 | 954 | 304 | 24 | 22 | 7 | 3 | 88/9/3/0/0 | FMG |
| 3013 | 1.53 | 10423 | 1071 | 349 | 33 | 24 | 5 | 3 | 87/9/3/1/0 | FMG |
| 3024.5 | 2.24* | 10131 | 928 | 407 | 36 | 35 | 6 | 3 | 88/8/3/1/0 | FMG |
| 3036.5 | 1.95 | 10910 | 1192 | 412 | 38 | 37 | 7 | 4 | 87/9/3/1/0 | FMG |
| 3050.5 | 1.32 | 9363 | 1021 | 387 | 30 | 33 | 6 | 4 | 86/9/4/1/0 | FMG |
| 3088 | 1.88 | 11303 | 1013 | 481 | 46 | 69 | 12 | 10 | 87/8/4/1/0 | FMG |
| 2960-3215 | 0.24 | 1440 | 113 | 15 | 10 | 13 | 3 | 2 | 86/7/5/2/0 | BG |

KEY: BG Background gas, CG Connection gas,   POG Pumps-off gas, TG Trip gas, STG Short trip gas, FMG Formation gas

* = isotube gas samples taken.

| From m MDRT | To m MDRT | Total or Rate (bbl) | Remarks |
| --- | --- | --- | --- |
|  |  |  | Normal surface losses while drilling. Minor seepage losses noted while drilling sandstone sections. |

Run 3 MWD / LWD string as follows: Resistivity: 3.97m, ARC Gamma 4.02m, D&I (survey) 11.53m, Sonic 20.98m, SADN Density 26.92m, SADN Porosity 28.90m Using Powerpulse MWD. No RT SADN data available, other tools fully functional. RT sonic data noisy due to stick-slip. SADN battery anticipated to last approximately until 08:00 5th October.

| Formation (Unit) | Prognosed MDRT SS, m | Actual MDRT TVDSS, m | Actual Thickness | Difference to Prog (TVDSS) | Basis Of Pick |
| --- | --- | --- | --- | --- | --- |
| Gippsland Limestone | 106 | -68 | 106.5 | -68 | 1803.4 | 0 | Sea-floor |
| Lakes Entrance | 1918.5 | -1880 | 1910 | -1871.4 | 189.8 | -8.6 | Slight increase in gamma, subtle change in cuttings |
| Latrobe Group: |  |  |  |  |  |  |  |
| Gurnard Formation | 2097.5 | -2059 | 2100 | -2061.2 | 27 | +2.2 | Greensand in cuttings |
| Kingfish Formation | 2132.5 | -2094 | 2127 | -2088.2 |  | -5.8 | Drill break, coarse quartz sand in cuttings |
| 54-5 Sand | 2513.5 | -2475 | 2537? | -2497.9 |  | +22.9 | Drill break, low gamma interval |
| 62 Sand | 2798.5 | -2760 | 2789? | -2749.9 |  | -10.1 | Drill break, coarse quartz sand in cuttings |
| Volador Fm 66.5 Sand | 2978.5 | -2940 |  |  |  |  |  |
| 67 Sand | 3218.5 | -3180 |  |  |  |  |  |
| 70 Sand | 3438.5 | -3400 |  |  |  |  |  |
| TD | 3501.5 | -3463 |  |  |  |  |  |

Daylight saving correction to time during reporting period, therefore this report covers 23 hours drilling. Data acquisition computers remaining on EST until end of well. Good correspondence seen between gamma curve and cuttings lithology.

Geologists:  Simon Ward / Roman Leslie

# Text boxes

Lithology Summary:

Drilling Summary:

Oil Fluorescence Summary:

Gas Summary:

Fluid Loss:

MWD Summary:

Wellsite Formation Picks:

Comments: