| Stuart Petroleum Limited | BAZZARD-1 |
| --- | --- |
| Report Date: | 06 October 2008 | Bit Diameter: | 311.1 mm (12.25”) |
| Report Number: | 14 | Last Casing: | 399 mm (13-3/8”) @ 841 m |
| Spud Date: | 20 September 2008 | LOT: | 15.06 ppg at 853m |
| Days from Spud: | 15 | Mud Weight: | 10.0 |
| Current Activity (06:00 hours): | POOH | ECD: | 10.6 |
| Water Depth: | 68 m | Mud Type: | KCl / PHPA |
| Rotary Table: | 38.5 m above AHD. | Last Survey: | 3262.74m incl 1.13° azim 324.09° |

| Time / Date | m MDRT | m TVDRT | Previous, m | Progress, m | Drill rate m/hr |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Minimum | Maximum | Average |
| 06:00 hrs, 06/10/08 | 3287 | 3286.2 | 3215 | 72 | 1.7 | 23.7 | 6.9 |

| Depth m MDRT | Description | Gas Data (total gas in %; C1, C2, C3, iC4, nC4, iC5, nC5 in ppm), C1/2/3/4/5/ ratios indicated below. |
| --- | --- | --- |
| 3210-3240 | SILTSTONE (40-95%): dark brownish grey, firm to hard, blocky, argillaceous, trace very fine sand, trace carbonaceous fragments, minor to common pyrite. SANDSTONE (5-60%): pale grey to white loose fine sand, well sorted, subangular to subrounded quartz, trace feldspar, trace mica, trace coaly fragments. Minor firm to hard aggregates with silty matrix. Common white to pale grey rock flour interpreted to be derived from sandstone. | 0.17, 1038/43/59/3/11/1/1 90/4/5/1/0 |
| 3240-3250 | SANDSTONE (20-80%): pale grey to white loose fine to coarse, dominantly medium lower sand, moderately to well sorted, subangular to subrounded quartz, trace feldspar, trace mica, trace titanite (sphene), trace coaly fragments. Moderately abundant firm to hard medium sand aggregates with silty matrix, moderate silica cement. Minor white to pale grey rock flour interpreted to be derived from sandstone. SILTSTONE (15-70%): dark brownish grey, firm to hard, blocky, argillaceous, trace very fine sand, trace carbonaceous fragments, minor pyrite. COAL (5-10%): dark brown to black, firm, blocky, conchoidal fracture. | 0.26, 1672/42/81/4/17/1/1 92/2/5/1/0 |
| 3250-3270 | SILTSTONE (45-95%): dark brownish grey and yellowish-olive grey, firm to hard, blocky, argillaceous, trace very fine sand, yellowish olive -grey siltstones strongly calcite cemented, trace carbonaceous fragments, minor pyrite. SANDSTONE (5-45%): pale grey to white loose fine to coarse, dominantly medium lower sand, moderately to well sorted, subangular to subrounded quartz, trace feldspar, trace mica, trace coaly fragments, trace quartz granules. Moderately abundant firm to hard medium sand aggregates with silty matrix, moderate silica cement. Minor white to pale grey rock flour interpreted to be derived from sandstone. CLAYSTONE (10% at 3270m): light to medium grey, moderately soft, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. | 0.32, 2089/86/126/8/27/3/3 89/4/5/2/0 |
| 3270-3287 | SANDSTONE (70% decr to 20%): pale grey to white loose very fine to coarse, dominantly medium lower sand, moderately to well sorted, subangular to subrounded quartz, trace feldspar, trace mica, trace coaly fragments, trace quartz granules. Moderately abundant firm to hard medium sand aggregates with silty matrix, moderate silica cement. Minor white to pale grey rock flour interpreted to be derived from sandstone. SILTSTONE (15% incr to 70%): dark brownish grey and yellowish-olive grey, firm to hard, blocky, argillaceous, trace very fine sand, yellowish olive -grey silts strongly calcite cemented, trace carbonaceous fragments, minor pyrite. CLAYSTONE (5-10%): light to medium grey to light brown, moderately soft to soft, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous. COAL (tr-10%): dark brown to black, firm, blocky to fissile, conchoidal fracture. | 0.25, 1476/74/113/11/29/5/3 86/4/7/2/1 |

| Depth m MDRT | Fluorescence | Cut | Residue ring / film |
| --- | --- | --- | --- |
| 3255-3265 | Trace to 2% moderately bright yellow-green (sandstone) to white green (rock flour). | Very slow to moderately fast blooming dull blue-white, dull blue-wt cut fluorescence. | Dull and patchy blue-white to moderately bright greenish blue fluorescing residual ring. |
| 3265-3270 | 5% moderately bright yellow-green (sandstone) to white green (rock flour). | Very slow to moderately slow blooming dull blue-white cut fluorescence. | Dull and patchy blue-white fluorescing residual ring. |
| 3270-3280 | Trace moderately bright yellow-green fluorescence associated with weakly cemented and slightly stained (honey brown) medium sandstone. | Moderately fast to fast blooming bright blue cut fluorescence. | Well developed, thick, moderately wide, bright blue residual ring. |

| (m MDRT) | Total Gas (%) | Methane (ppm) | Ethane (ppm) | Propane (ppm) | i-Butane (ppm) | n-Butane (ppm) | i-Pentane (ppm) | n-Pentane (ppm) | % Ratios (C1/2/3/4/5) | Type |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 3244.5 | 1.00 | 8233 | 351 | 208 | 15 | 31 | 4 | 4 | 93/4/2/1/0 | FMG |
| 3256 | 0.97 | 6648 | 331 | 387 | 32 | 73 | 10 | 9 | 89/5/5/1/0 | FMG |
| 3261* | 0.96 | 7726 | 416 | 329 | 24 | 55 | 7 | 7 | 90/5/4/1/0 | FMG |
| 3271* | 1.19 | 9007 | 530 | 514 | 54 | 97 | 18 | 16 | 88/5/5/2/0 | FMG |
| 3210-3287 | 0.24 | 1486 | 60 | 91 | 6 | 20 | 2 | 2 | 89/4/5/2/0 | BG |

KEY: BG Background gas, CG Connection gas,   POG Pumps-off gas, TG Trip gas, STG Short trip gas, FMG Formation gas

* = isotube gas samples taken.

| From m MDRT | To m MDRT | Total or Rate (bbl) | Remarks |
| --- | --- | --- | --- |
|  |  |  | Normal surface losses while drilling. Minor seepage losses noted while drilling sandstone sections. |

Run 3 MWD / LWD string as follows: Resistivity: 3.97m, ARC Gamma 4.02m, D&I (survey) 11.53m, Sonic 20.98m, SADN Density 26.92m, SADN Porosity 28.90m Using Powerpulse MWD. No RT SADN data available, other tools fully functional. RT sonic data noisy due to stick-slip. SADN battery anticipated to have failed yesterday morning.

| Formation (Unit) | Prognosed MDRT SS, m | Actual MDRT TVDSS, m | Actual Thickness | Difference to Prog (TVDSS) | Basis Of Pick |
| --- | --- | --- | --- | --- | --- |
| Gippsland Limestone | 106 | -68 | 106.5 | -68 | 1803.4 | 0 | Sea-floor |
| Lakes Entrance | 1918.5 | -1880 | 1910 | -1871.4 | 189.8 | -8.6 | Slight increase in gamma, subtle change in cuttings |
| Latrobe Group: |  |  |  |  |  |  |  |
| Gurnard Formation | 2097.5 | -2059 | 2100 | -2061.2 | 27 | +2.2 | Greensand in cuttings |
| Kingfish Formation | 2132.5 | -2094 | 2127 | -2088.2 |  | -5.8 | Drill break, coarse quartz sand in cuttings |
| 54-5 Sand | 2513.5 | -2475 | 2537? | -2497.9 |  | +22.9 | Drill break, low gamma interval |
| 62 Sand | 2798.5 | -2760 | 2789? | -2749.9 |  | -10.1 | Drill break, coarse quartz sand in cuttings |
| Volador Fm 66.5 Sand | 2978.5 | -2940 | 3000? | -2960.9 |  | -20.9 | Change in cuttings |
| 67 Sand | 3218.5 | -3180 |  |  |  |  |  |
| 70 Sand | 3438.5 | -3400 |  |  |  |  |  |
| TD | 3501.5 | -3463 |  |  |  |  |  |

Data acquisition computers remaining on EST until end of well. Good correspondence seen between gamma curve and cuttings lithology. Increasing resistivity correlates well with Veilfin-1 suggesting Bazzard-1 is running c.100m deep to prognosis. 67 Sand now anticipated at around 3320m. POOH at 22:40 hrs due to low ROP.

Geologists:  Simon Ward / Roman Leslie

# Text boxes

Lithology Summary:

Drilling Summary:

Oil Fluorescence Summary:

Gas Summary:

Fluid Loss:

MWD Summary:

Wellsite Formation Picks:

Comments: