| Stuart Petroleum Limited | BAZZARD-1 |
| --- | --- |
| Report Date: | 07 October 2008 | Bit Diameter: | 311.1 mm (12.25”) |
| Report Number: | 15 | Last Casing: | 399 mm (13-3/8”) @ 841 m |
| Spud Date: | 20 September 2008 | LOT: | 15.06 ppg at 853m |
| Days from Spud: | 16 | Mud Weight: | 10.0 |
| Current Activity (06:00 hours): | Reaming 311 mm (12-1/4”) hole | ECD: | - |
| Water Depth: | 68 m | Mud Type: | KCl / PHPA |
| Rotary Table: | 38.5 m above AHD. | Last Survey: | 3262.74m incl 1.13° azim 324.09° |

| Time / Date | m MDRT | m TVDRT | Previous, m | Progress, m | Drill rate m/hr |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Minimum | Maximum | Average |
| 06:00 hrs, 07/10/08 | 3287 | 3286.2 | 3287 | 0 | - | - | - |

| Depth m MDRT | Description | Gas Data (total gas in %; C1, C2, C3, iC4, nC4, iC5, nC5 in ppm), C1/2/3/4/5/ ratios indicated below. |
| --- | --- | --- |
|  | No new formation drilled. |  |

| Depth m MDRT | Fluorescence | Cut | Residue ring / film |
| --- | --- | --- | --- |

| (m MDRT) | Total Gas (%) | Methane (ppm) | Ethane (ppm) | Propane (ppm) | i-Butane (ppm) | n-Butane (ppm) | i-Pentane (ppm) | n-Pentane (ppm) | % Ratios (C1/2/3/4/5) | Type |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

KEY: BG Background gas, CG Connection gas,   POG Pumps-off gas, TG Trip gas, STG Short trip gas, FMG Formation gas

* = isotube gas samples taken.

| From m MDRT | To m MDRT | Total or Rate (bbl) | Remarks |
| --- | --- | --- | --- |
|  |  |  | No losses while tripping. Normal surface losses while reaming. |

Run 3 complete at 09:00 RM data from ARC and Sonic downloaded on rig floor. SADN laid down. RM ARC data good (2840-3283m), Sonic data (2844-3266m) transmitted to DCS for processing, SADN data collected to 2298m (batteries exhausted). Pick up SADN as used in Run 2, reloaded with partially used batteries. Tool delay set to activate at 21:00 hrs. Loaded sources at 11.15-11.45 hrs. Shallow LWD test at 13.45hrs – tool good. RIH at 14:00hrs Run 4 MWD / LWD string as follows: Resistivity: 3.97m, ARC Gamma 4.02m, D&I (survey) 11.53m, Sonic 20.98m, SADN Density 26.93m, SADN Porosity 28.91m Using Powerpulse MWD. No RT SADN data available, other tools fully functional. Limited battery life in SADN and Sonic tools.

| Formation (Unit) | Prognosed MDRT SS, m | Actual MDRT TVDSS, m | Actual Thickness | Difference to Prog (TVDSS) | Basis Of Pick |
| --- | --- | --- | --- | --- | --- |
| Gippsland Limestone | 106 | -68 | 106.5 | -68 | 1803.4 | 0 | Sea-floor |
| Lakes Entrance | 1918.5 | -1880 | 1910 | -1871.4 | 189.8 | -8.6 | Slight increase in gamma, subtle change in cuttings |
| Latrobe Group: |  |  |  |  |  |  |  |
| Gurnard Formation | 2097.5 | -2059 | 2100 | -2061.2 | 27 | +2.2 | Greensand in cuttings |
| Kingfish Formation | 2132.5 | -2094 | 2127 | -2088.2 |  | -5.8 | Drill break, coarse quartz sand in cuttings |
| 54-5 Sand | 2513.5 | -2475 | 2537? | -2497.9 |  | +22.9 | Drill break, low gamma interval |
| 62 Sand | 2798.5 | -2760 | 2789? | -2749.9 |  | -10.1 | Drill break, coarse quartz sand in cuttings |
| Volador Fm 66.5 Sand | 2978.5 | -2940 | 3000? | -2960.9 |  | -20.9 | Change in cuttings |
| 67 Sand | 3218.5 | -3180 |  |  |  |  |  |
| 70 Sand | 3438.5 | -3400 |  |  |  |  |  |
| TD | 3501.5 | -3463 |  |  |  |  |  |

Wash and ream from 2771m at 19:30 hrs, bit at 3241m at report time.

Geologists:  Simon Ward / Roman Leslie

# Text boxes

Lithology Summary:

Drilling Summary:

Oil Fluorescence Summary:

Gas Summary:

Fluid Loss:

MWD Summary:

Wellsite Formation Picks:

Comments: