| Stuart Petroleum Limited | BAZZARD-1 |
| --- | --- |
| Report Date: | 08 October 2008 | Bit Diameter: | 311.1 mm (12.25”) |
| Report Number: | 16 | Last Casing: | 399 mm (13-3/8”) @ 841 m |
| Spud Date: | 20 September 2008 | LOT: | 15.06 ppg at 853m |
| Days from Spud: | 17 | Mud Weight: | 10.0 |
| Current Activity (06:00 hours): | Drilling 311 mm (12-1/4”) hole | ECD: | 10.5 |
| Water Depth: | 68 m | Mud Type: | KCl / PHPA |
| Rotary Table: | 38.5 m above AHD. | Last Survey: | 3348.68m incl 1.03° azim 306.14° |

| Time / Date | m MDRT | m TVDRT | Previous, m | Progress, m | Drill rate m/hr |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Minimum | Maximum | Average |
| 06:00 hrs, 08/10/08 | 3406 | 3405.3 | 3287 | 119 | 1.7 | 29.6 | 8.2 |

| Depth m MDRT | Description | Gas Data (total gas in %; C1, C2, C3, iC4, nC4, iC5, nC5 in ppm), C1/2/3/4/5/ ratios indicated below. |
| --- | --- | --- |
| 3287-3295 | SILTSTONE (70-80%): medium to dark grey to brownish grey, firm to hard, blocky to flakey, argillaceous, trace very fine sand, trace carbonaceous fragments, minor pyrite. Trace medium grey hard calcareous siltstone. SANDSTONE (15-25%): white to light grey to light yellow, firm to hard, fine to medium, moderately well sorted, subangular to dominantly subrounded clear to smokey quartz, trace feldspar, trace muscovite and biotite flakes, slightly silty, minor clear to white siliceous cement, trace carbonaceous fragments, trace intergranular pyrite in parts. Poor visible porosity. Trace loose fine to medium sand. COAL (5%): dark grey to black, firm to hard, dirty. | 0.30, 2179/156/119/11/24/4/5 88/6/5/1/0 |
| 3295-3320 | SANDSTONE (5-100%): white to light grey to light yellow, firm to hard, fine to coarse, dominantly medium, moderately well sorted, subangular to dominantly subrounded clear to smokey quartz, Trace quartz granules, trace feldspar, trace muscovite and biotite flakes, slightly silty, minor clear to white siliceous cement, trace carbonaceous fragments, trace intergranular pyrite in parts. Poor visible porosity. Minor loose fine to medium sand. SILTSTONE (15-90%): medium to dark grey to brownish grey, firm to hard, blocky to flakey, argillaceous, trace very fine sand, trace carbonaceous fragments, minor pyrite. Trace medium grey hard calcareous siltstone. COAL (Tr-5%): dark grey to black, firm to hard, dirty. | 0.76, 5725/273/165/19/36/7/8 92/4/3/1/0 |
| 3320-3335 | SANDSTONE (80-100%): white to light grey to light yellow, loose, fine to granule, dominantly coarse to very coarse sand with up to 95% dusky yellow, medium to very coarse, strongly dolomite-siderite cemented aggregates at 3335m, poor to moderately sorted, subangular to dominantly subrounded clear to smokey quartz, trace feldspar, trace muscovite and biotite flakes, trace carbonaceous fragments. SILTSTONE (Tr-20%): medium to dark grey to brownish grey, firm to hard, blocky to flakey, argillaceous, trace very fine sand, trace carbonaceous fragments, minor pyrite. Trace medium grey hard calcareous siltstone. | 0.25, 2184/93/73/11/24/6/7 91/4/3/2/1 |
| 3335-3355 | SILTSTONE (45-95%): medium to dark grey to brownish grey, firm to hard, blocky to flakey, argillaceous, trace very fine sand, trace carbonaceous fragments, minor pyrite. Trace medium grey hard calcareous siltstone. SANDSTONE (5-55%): yellowish grey, very fine to medium, moderately to well sorted, moderately firm, silica-cemented aggregates, subrounded clear to smokey quartz, poor inferred porosity. Trace dusky yellow dolomite-siderite cemented aggregates. COAL (tr - 10%): dark grey to black, firm to hard, dirty. | 0.42, 2689/272/250/34/61/15/14 81/8/7/3/1 |
| 3355-3382 | SANDSTONE (Tr-60%): yellowish grey, very fine to medium lower, well sorted, moderately firm to hard, silica-cemented aggregates, subrounded clear to smokey quartz, trace carbonaceous fragments, poor inferred porosity. Minor loose fine to medium sand. SILTSTONE (30-70%): medium to dark grey to brownish grey, firm to hard, blocky to flakey, argillaceous, trace very fine sand, trace carbonaceous fragments, minor pyrite. COAL (10-15%, 50% at 3360m): dark grey to black, firm to hard, dirty. | 0.54, 3555/337/268/35/64/16/16 83/8/6/2/1 |
| 3382-3390 | SANDSTONE (30-70%): white to pale brownish grey fine to medium aggregates, moderately sorted, subangular to subrounded quartz in trace to common silty matrix, minor silica cement, minor pale yellow brown siderite or dolomite cement, firm to hard, common carbonaceous fragments and laminae, nil visible porosity. With minor loose fine to medium sand grains, trace quartz granules. SILTSTONE (30-70%): medium to dark grey to brownish grey, firm to hard, blocky to flakey, argillaceous, grading in part to hard very fine sandstone, trace carbonaceous fragments, minor microcrystalline pyrite masses. Trace dirty coal. | 0.42, 2435/203/168/26/46/14/13 84/7/6/2/1 |
| 3390-3400 | SILTSTONE (60-90%): medium to dark grey to brownish grey, firm to hard, blocky to flakey, argillaceous, grading in part to hard very fine sandstone, trace carbonaceous fragments, trace microcrystalline pyrite masses. SANDSTONE (5-30%): fine to medium aggregates and minor loose fine to granule quartz. COAL (tr-5%): black, hard, conchoidal fracture. | 0.55, 3521/314/240/34/65/17/16 84/7/6/2/1 |

| Depth m MDRT | Fluorescence | Cut | Residue ring / film |
| --- | --- | --- | --- |
| 3288-3295 | Trace to 2% dull greenish yellow pinpoint fluorescence in fine sandstone. | Moderately fast streaming bright blue white cut fluorescence. | Wide bright blue white fluorescing residual ring, no visible residue. |
| 3310-3355 | Trace to 2% dull yellow-green pinpoint fluorescence associated with well cemented medium sandstone | Very slow blooming dull blue-white cut fluorescence. | Dull faint blue-white fluorescing residual ring, no visible residue. |
| 3335-3355, 3365-3375 | Trace to 2% dull yellow-green pinpoint fluorescence associated with well cemented medium sandstone. | Very slow blooming dull blue-white cut fluorescence. | Dull faint blue-white fluorescing residual rings, no visible residue. |

In addition to above shows, the following rare component was noted:

| Depth m MDRT | Fluorescence | Cut | Residue ring / film |
| --- | --- | --- | --- |
| 3295, 3340, 3355, 3370, 3385, 3390 | Trace dull to bright greenish white live oil fluorescence on medium sandstone. | Very fast streaming bright blue green cut fluorescence | Wide dull green fluorescing residual ring, no visible residue. |

| (m MDRT) | Total Gas (%) | Methane (ppm) | Ethane (ppm) | Propane (ppm) | i-Butane (ppm) | n-Butane (ppm) | i-Pentane (ppm) | n-Pentane (ppm) | % Ratios (C1/2/3/4/5) | Type |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 3293.5 | 0.74 | 5805 | 301 | 206 | 17 | 39 | 6 | 6 | 91/5/3/1/0 | FMG |
| 3298.5 | 1.04 | 8167 | 388 | 227 | 23 | 43 | 7 | 8 | 92/4/3/1/0 | FMG |
| 3300.9* | 2.36 | 16879 | 771 | 406 | 41 | 70 | 12 | 12 | 93/4/2/1/0 | FMG |
| 3305.5 | 1.98 | 15416 | 714 | 391 | 42 | 70 | 13 | 13 | 93/4/2/1/0 | FMG |
| 3314.0 | 1.55 | 11238 | 444 | 240 | 29 | 52 | 11 | 11 | 93/4/2/1/0 | FMG |
| 3319.5 | 1.09 | 9240 | 343 | 178 | 23 | 42 | 9 | 10 | 93/4/2/1/0 | FMG |
| 3339.5* | 1.54 | 9404 | 930 | 850 | 114 | 184 | 42 | 36 | 81/8/7/3/1 | FMG |
| 3348.0* | 1.87 | 11849 | 1182 | 1006 | 131 | 203 | 44 | 37 | 82/8/7/2/1 | FMG |
| 3370.3* | 1.64 | 10582 | 1044 | 815 | 109 | 168 | 38 | 33 | 83/8/6/2/1 | FMG |
| 3378.8 | 1.36 | 9737 | 767 | 526 | 65 | 118 | 26 | 25 | 86/7/5/2/0 | FMG |
| 3387.5 | 1.23 | 7985 | 576 | 370 | 50 | 91 | 22 | 21 | 88/6/4/2/0 | FMG |
| 3391.3* | 2.84 | 17001 | 1510 | 1192 | 162 | 247 | 53 | 46 | 84/8/6/2/0 | FMG |
| 3398.4 | 1.13 | 8309 | 707 | 409 | 40 | 80 | 18 | 19 | 87/7/5/1/0 | FMG |

KEY: BG Background gas, CG Connection gas,   POG Pumps-off gas, TG Trip gas, STG Short trip gas, FMG Formation gas

* = isotube gas samples taken.

| From m MDRT | To m MDRT | Total or Rate (bbl) | Remarks |
| --- | --- | --- | --- |
|  |  |  | Normal surface losses. |

Run 4 MWD / LWD string as follows: Resistivity: 3.97m, ARC Gamma 4.02m, D&I (survey) 11.53m, Sonic 20.98m, SADN Density 26.93m, SADN Porosity 28.91m Using Powerpulse MWD. No RT SADN data available. RT Sonic failed at 3350m, battery was rerun from Run 3 but likely providing tool power so RM data should be available.

| Formation (Unit) | Prognosed MDRT SS, m | Actual MDRT TVDSS, m | Actual Thickness | Difference to Prog (TVDSS) | Basis Of Pick |
| --- | --- | --- | --- | --- | --- |
| Gippsland Limestone | 106 | -68 | 106.5 | -68 | 1803.4 | 0 | Sea-floor |
| Lakes Entrance | 1918.5 | -1880 | 1910 | -1871.4 | 189.8 | -8.6 | Slight increase in gamma, subtle change in cuttings |
| Latrobe Group: |  |  |  |  |  |  |  |
| Gurnard Formation | 2097.5 | -2059 | 2100 | -2061.2 | 27 | +2.2 | Greensand in cuttings |
| Kingfish Formation | 2132.5 | -2094 | 2127 | -2088.2 |  | -5.8 | Drill break, coarse quartz sand in cuttings |
| 54-5 Sand | 2513.5 | -2475 | 2537? | -2497.9 |  | +22.9 | Drill break, low gamma interval |
| 62 Sand | 2798.5 | -2760 | 2789? | -2749.9 |  | -10.1 | Drill break, coarse quartz sand in cuttings |
| Volador Fm 66.5 Sand | 2978.5 | -2940 | 3000? | -2960.9 |  | -20.9 | Change in cuttings |
| 67 Sand | 3218.5 | -3180 |  |  |  |  |  |
| 70 Sand | 3438.5 | -3400 |  |  |  |  |  |
| TD | 3501.5 | -3463 |  |  |  |  |  |

Commence drilling with NB4 at 08:00 hrs Sandstone aggregate cuttings better preserved than was observed with PDC bits. High mud temperature generating condensation in gas lines between BHI unit and shakers resulting in increased flow resistance, blowback of system regularly required to ensure flow maintained. Mud filtrate and filter cake samples supplied for resistivity measurement at 02:00 hrs, however the Schlumberger equipment on the rig to collect these measurements is unserviceable at present.

Geologists:  Simon Ward / Roman Leslie

# Text boxes

Lithology Summary:

Drilling Summary:

Oil Fluorescence Summary:

Gas Summary:

Fluid Loss:

MWD Summary:

Wellsite Formation Picks:

Comments: