| Stuart Petroleum Limited | BAZZARD-1 |
| --- | --- |
| Report Date: | 09 October 2008 | Bit Diameter: | 311.1 mm (12.25”) |
| Report Number: | 17 | Last Casing: | 399 mm (13-3/8”) @ 841 m |
| Spud Date: | 20 September 2008 | LOT: | 15.06 ppg at 853m |
| Days from Spud: | 18 | Mud Weight: | 10.0 |
| Current Activity (06:00 hours): | Running in hole with mule shoe to set plugs after laying out BHA at TD. | ECD: | 10.5 |
| Water Depth: | 68 m | Mud Type: | KCl / PHPA |
| Rotary Table: | 38.5 m above AHD. | Last Survey: | 3438.50m incl 1.3º |

| Time / Date | m MDRT | m TVDRT | Previous, m | Progress, m | Drill rate m/hr |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Minimum | Maximum | Average |
| 06:00 hrs, 09/10/08 | 3450 |  | 3406 | 44 |  |  |  |

| Depth m MDRT | Description | Gas Data (total gas in %; C1, C2, C3, iC4, nC4, iC5, nC5 in ppm), C1/2/3/4/5/ ratios indicated below. |
| --- | --- | --- |
| 3400-3425 | SANDSTONE (20-80%): white to pale brownish grey very fine to medium aggregates, dominantly fine, moderately sorted, subangular to subrounded quartz in trace to common white silty matrix, minor silica cement, minor pale yellow brown siderite or dolomite cement, firm to hard, common carbonaceous fragments and laminae, nil visible porosity. With common loose fine to medium sand grains. SILTSTONE (20-75%): medium to dark grey to brownish grey, firm to hard, blocky to flakey, argillaceous, grading in part to hard very fine sandstone, trace carbonaceous fragments, minor microcrystalline pyrite masses. Trace dirty coal. COAL (Tr-5%): black, dull, dirty. |  |
| 3425-3450 | SILTSTONE (60-95%): medium to dark grey to brownish grey, firm to hard, blocky to flakey, argillaceous, grading in part to hard very fine sandstone, trace carbonaceous fragments, minor microcrystalline pyrite masses. COAL (5-20%): black, dull, dirty. SANDSTONE (Tr-20%): white to pale brownish grey very fine to medium aggregates, moderately sorted, subangular to subrounded quartz in trace to common white silty matrix, minor silica cement, minor pale yellow brown siderite or dolomite cement, firm to hard, common carbonaceous fragments and laminae, nil visible porosity. With trace loose fine sand grains. |  |

| Depth m MDRT | Fluorescence | Cut | Residue ring / film |
| --- | --- | --- | --- |
| 3410-3425 | Trace to 2% dull yellow-green pinpoint fluorescence associated with well cemented medium sandstone. | Very slow blooming dull blue-white cut fluorescence. | Dull faint blue-white fluorescing residual rings, no visible residue |
| 3440-3445 | Trace to 2% dull yellow-green pinpoint fluorescence associated with well cemented medium sandstone. | Very slow blooming dull blue-white cut fluorescence. | Dull faint blue-white fluorescing residual rings, no visible residue |

| (m MDRT) | Total Gas (%) | Methane (ppm) | Ethane (ppm) | Propane (ppm) | i-Butane (ppm) | n-Butane (ppm) | i-Pentane (ppm) | n-Pentane (ppm) | % Ratios (C1/2/3/4/5) | Type |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 3410.0 | 2.07 | 10666 | 1000 | 696 | 81 | 127 | 28 | 26 | 84/8/6/2/0 | FMG |
| 3420.2* | 1.82 | 8482 | 971 | 725 | 93 | 147 | 32 | 29 | 81/9/7/2/1 | FMG |
| 3433.0* | 1.84 | 11162 | 1355 | 944 | 106 | 185 | 38 | 36 | 80/10/7/2/1 | FMG |
| 3442 | 1.06 | 6127 | 927 | 843 | 115 | 178 | 38 | 35 | 74/11/10/4/1 | FMG |
| 3445 | 1.65 | 10697 | 1087 | 547 | 57 | 100 | 23 | 23 | 85/9/5/1/0 | FMG |
| 3400-3425 | 0.68 | 4431 | 479 | 384 | 51 | 85 | 21 | 20 | 80/9/7/3/1 | BG |
| 3425-3450 | 0.65 | 3590 | 481 | 410 | 57 | 98 | 24 | 23 | 77/10/9/3/1 | BG |

KEY: BG Background gas, CG Connection gas,   POG Pumps-off gas, TG Trip gas, STG Short trip gas, FMG Formation gas

* = isotube gas samples taken.

| From m MDRT | To m MDRT | Total or Rate (bbl) | Remarks |
| --- | --- | --- | --- |
|  |  |  | Normal surface losses. |

Run 4 MWD / LWD string as follows: Resistivity: 3.97m, ARC Gamma 4.02m, D&I (survey) 11.53m, Sonic 20.98m, SADN Density 26.93m, SADN Porosity 28.91m Using Powerpulse MWD. No RT SADN data available.

| Formation (Unit) | Prognosed MDRT SS, m | Actual MDRT TVDSS, m | Actual Thickness | Difference to Prog (TVDSS) | Basis Of Pick |
| --- | --- | --- | --- | --- | --- |
| Gippsland Limestone | 106 | -68 | 106.5 | -68 | 1803.4 | 0 | Sea-floor |
| Lakes Entrance | 1918.5 | -1880 | 1910 | -1871.4 | 189.8 | -8.6 | Slight increase in gamma, subtle change in cuttings |
| Latrobe Group: |  |  |  |  |  |  |  |
| Gurnard Formation | 2097.5 | -2059 | 2100 | -2061.2 | 27 | +2.2 | Greensand in cuttings |
| Kingfish Formation | 2132.5 | -2094 | 2127 | -2088.2 |  | -5.8 | Drill break, coarse quartz sand in cuttings |
| 54-5 Sand | 2513.5 | -2475 | 2537? | -2497.9 |  | +22.9 | Drill break, low gamma interval |
| 62 Sand | 2798.5 | -2760 | 2789? | -2749.9 |  | -10.1 | Drill break, coarse quartz sand in cuttings |
| Volador Fm 66.5 Sand | 2978.5 | -2940 | 3000? | -2960.9 |  | -20.9 | Change in cuttings |
| 67 Sand | 3218.5 | -3180 |  |  |  |  |  |
| 70 Sand | 3438.5 | -3400 |  |  |  |  |  |
| TD | 3501.5 | -3463 | 3450 |  |  |  |  |

Final DGR for Bazzard-1, Simon Ward off rig 16:00 8 Oct. 08 TD 3450m at 13:15hrs

Geologists:  Simon Ward / Roman Leslie

# Text boxes

Lithology Summary:

Drilling Summary:

Oil Fluorescence Summary:

Gas Summary:

Fluid Loss:

MWD Summary:

Wellsite Formation Picks:

Comments: