| Stuart Petroleum Limited | BAZZARD-1 |
| --- | --- |
| Report Date: | 22 August 2008 | Bit Diameter: | 41 mm (16”) |
| Report Number: | 1 | Last Casing: | 760 mm (30”) @ 151 m, 20” shoe |
| Spud Date: | 20 August 2008 | LOT: | n/a |
| Days from Spud: | 2 | Mud Weight: | 8.6 ppg |
| Current Activity (0600 hours): | Drilling 406 mm (16”) hole | ECD: | 8.7 ppg |
| Water Depth: | 68 m | Mud Type: | Seawater / hivis sweeps |
| Rotary Table: | 38 m | Last Survey: | 195.13m / 0.92° incl / 244.6° azimuth |

| All depths in metres | m MDRT | m TVDRT | Previously | Progress | Drill rate m/hr |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Minimum | Maximum | Average |
| 0000 hours | 154 | 154 | 154 | 0 | - | - | - |
| 0600 hours | 258 | 258 | 154 | 104 | 8 | 96 | 81 |

| Depth m MDRT | Description | Gas Data (total gas in %; chrom data C1, C2, C3, iC4, nC4, iC5, nC5 in ppm) |
| --- | --- | --- |
|  | No new lithology drilled. | No gas data collected. |

| Depth m MDRT | Fluorescence | Cut | Residue ring / film |
| --- | --- | --- | --- |

| Background Gas / Gas Peaks |
| --- |
| (m MDRT) | Total Gas (%) | Methane (ppm) | Ethane (ppm) | Propane (ppm) | i-Butane (ppm) | n-Butane (ppm) | i-Pentane (ppm) | n-Pentane (ppm) | Type |

KEY: BG Background gas, CG Connection gas,   POG Pumps-off gas, TG Trip gas, STG Short trip gas, FMG Formation gas

| From m MDRT | To m MDRT | Total or Rate (bbl) | Remarks |
| --- | --- | --- | --- |

Sensor Offsets: gamma 5.35 m, D&I (survey) 6.00 m, sonic 14.99 m.

| Formation (Unit) | Prognosed m MDRT | Actual m MDRT | Basis Of Pick |
| --- | --- | --- | --- |
| Gippsland Limestone | 106 |  |  |
| Lakes Entrance | 1914 |  |  |
| La Trobe Group: |  |  |  |
| Gurnard Formation | 2104 |  |  |
| Kingfish Formation | 2130 |  |  |
| 51 Sand | 2217 |  |  |
| 52 Sand | 2340 |  |  |
| 53 Sand | 2513 |  |  |
| 62 Sand | 2932 |  |  |
| Volador Fm 66.5 Sand | 3234 |  |  |
| 67 Sand | 3435 |  |  |
| TD | 3501 |  |  |

WSG’s Simon Ward and Roman Leslie arrived on rig 22/09/08. Simon to work midnight to midday, Roman to work midday to midnight. All BHI systems operational. Details of sampling programme confirmed with BHI. Schlumberger wireline crew on board and checking tools. Schlumberger LWD/MWD tools fully operational when parts arrived from Sale today, commence RIH at 18:30hrs.

Geologists:  Simon Ward / Roman Leslie

# Text boxes

Lithology Summary:

Drilling Summary:

Oil Fluorescence Summary:

Gas Summary:

Fluid Loss:

MWD Summary:

Wellsite Formation Picks:

Comments: