| Stuart Petroleum Limited | BAZZARD-1 |
| --- | --- |
| Report Date: | 24 September 2008 | Bit Diameter: | 41 mm (16”) |
| Report Number: | 3 | Last Casing: | 760 mm (30”) @ 151 m, 20” shoe |
| Spud Date: | 20 September 2008 | LOT: | n/a |
| Days from Spud: | 4 | Mud Weight: | 8.6 ppg |
| Current Activity (06:00 hours): | Running 399mm (13-3/8”) casing. | ECD: | 8.7 ppg |
| Water Depth: | 68 m | Mud Type: | Seawater / hivis sweeps |
| Rotary Table: | 38.5 m | Last Survey: | 814.35m / 0.20° incl / 171.73° azimuth |

| Time / Date | m MDRT | m TVDRT | Previous, m | Progress, m | Drill rate m/hr |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Minimum | Maximum | Average |
| 00:00 hrs, 24/09/08 | 850 | 849.7 | 763 | 87 | 4.9 | 26.1 | 13.3 |
| 06:00 hrs, 25/09/08 | 850 | 849.7 | 820.8 | 29.2 | 6.8 | 21.8 | 14.1 |

| Depth m MDRT | Description | Gas Data (total gas in %; chrom data C1, C2, C3, iC4, nC4, iC5, nC5 in ppm) |
| --- | --- | --- |
|  | No samples collected, returns to texas deck. | No gas data collected. |

| Depth m MDRT | Fluorescence | Cut | Residue ring / film |
| --- | --- | --- | --- |

| Background Gas / Gas Peaks |
| --- |
| (m MDRT) | Total Gas (%) | Methane (ppm) | Ethane (ppm) | Propane (ppm) | i-Butane (ppm) | n-Butane (ppm) | i-Pentane (ppm) | n-Pentane (ppm) | Type |

KEY: BG Background gas, CG Connection gas,   POG Pumps-off gas, TG Trip gas, STG Short trip gas, FMG Formation gas

| From m MDRT | To m MDRT | Total or Rate (bbl) | Remarks |
| --- | --- | --- | --- |

Sensor Offsets: gamma 5.35 m, D&I (survey) 6.00 m, sonic 14.99 m.

| Formation (Unit) | Prognosed MDRT SS, m | Actual MDRT TVDSS, m | Actual Thickness | Difference to Prognosis | Basis Of Pick |
| --- | --- | --- | --- | --- | --- |
| Gippsland Limestone | 106.5 | -68 |  |  |  |  |  |
| Lakes Entrance | 1918.5 | -1880 |  |  |  |  |  |
| Latrobe Group: |  |  |  |  |  |  |  |
| Gurnard Formation | 2097.5 | -2059 |  |  |  |  |  |
| Kingfish Formation | 2132.5 | -2094 |  |  |  |  |  |
| 54-5 Sand | 2513.5 | -2475 |  |  |  |  |  |
| 62 Sand | 2798.5 | -2760 |  |  |  |  |  |
| Volador Fm 66.5 Sand | 2978.5 | -2940 |  |  |  |  |  |
| 67 Sand | 3218.5 | -3180 |  |  |  |  |  |
| 70 Sand | 3438.5 | -3400 |  |  |  |  |  |
| TD | 3501.5 | -3463 |  |  |  |  |  |

29.2m of drilling in the morning (820.8-850m). TD reached at 08.45 hrs.

Geologists:  Simon Ward / Roman Leslie

# Text boxes

Lithology Summary:

Drilling Summary:

Oil Fluorescence Summary:

Gas Summary:

Fluid Loss:

MWD Summary:

Wellsite Formation Picks:

Comments: