| Stuart Petroleum Limited | BAZZARD-1 |
| --- | --- |
| Report Date: | 27 September 2008 | Bit Diameter: | 311.1 mm (12.25”) |
| Report Number: | 6 | Last Casing: | 399 mm (13-3/8”) @ 841 m |
| Spud Date: | 20 September 2008 | LOT: | 15.06 ppg at 853m |
| Days from Spud: | 7 | Mud Weight: | 8.8 |
| Current Activity (06:00 hours): | Drilling 311 mm (12-1/4”) hole. | ECD: | 9.3 |
| Water Depth: | 68 m | Mud Type: | KCl / PHPA |
| Rotary Table: | 38.5 m above AHD. | Last Survey: | 1252.58m / 0.14° incl / 313.93° azimuth |

| Time / Date | m MDRT | m TVDRT | Previous, m | Progress, m | Drill rate m/hr |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Minimum | Maximum | Average |
| 00:00 hrs, 27/09/08 | 1088 | 1087.9 | 850 | 238 | 6.1 | 66.9 | 39.1 |
| 06:00 hrs, 28/09/08 | 1270 | 1269.9 | 850 | 420 | 1.5 | 67.7 | 40.0 |

| Depth m MDRT | Description | Gas Data (total gas in %; C1, C2, C3, iC4, nC4, iC5, nC5 in ppm) |
| --- | --- | --- |
| 850-1080 | CALCILUTITE (70-100%): light bluish grey-light olive grey with trace white to bluish white cuttings, subblocky-blocky, moderately soft to soft with rare hard (white cuttings), calcareous silt-mud, well sorted, minor clastic silt fraction, minor to rarely common clastic clay fraction, fine black (carbonaceous?) flecks and laminations, finely laminated, poor inferred porosity; with subordinate (interbedded?) CALCARENITE (0-30%): light olive-grey to greenish-grey and occasional yellowish-grey, subblocky to blocky aggregates, moderately hard to hard, very fine to medium grained, moderately sorted, semi translucent to opaque sub angular calcite grains, moderate to strong calcite cementation, rare skeletal fragments (echinoderms?), poor inferred porosity. | 0.31% av, 2953/0/4/1/1/0/0 |

| Depth m MDRT | Fluorescence | Cut | Residue ring / film |
| --- | --- | --- | --- |

| Background Gas / Gas Peaks |
| --- |
| (m MDRT) | Total Gas (%) | Methane (ppm) | Ethane (ppm) | Propane (ppm) | i-Butane (ppm) | n-Butane (ppm) | i-Pentane (ppm) | n-Pentane (ppm) | Type |
| 850-1088 | 0.01-0.60 | 2953 | 0 | 4 | 1 | 1 | 0 | 0 | BG |

KEY: BG Background gas, CG Connection gas,   POG Pumps-off gas, TG Trip gas, STG Short trip gas, FMG Formation gas

| From m MDRT | To m MDRT | Total or Rate (bbl) | Remarks |
| --- | --- | --- | --- |
|  |  |  | Normal surface fluid losses only. |

Run 2 MWD / LWD string as follows: Resistivity: 3.98m, ARC Gamma 4.03m, D&I (survey) 11.54m, Sonic 21.01m, SADN Density 25.51m, SADN Porosity 28.37m Density/porosity tool ceased sending real-time data at casing shoe, appears to be faulty connection in the tool data and power bus, the tool is recording to memory and running on the battery with c.3 days operation.

| Formation (Unit) | Prognosed MDRT SS, m | Actual MDRT TVDSS, m | Actual Thickness | Difference to Prog (TVDSS) | Basis Of Pick |
| --- | --- | --- | --- | --- | --- |
| Gippsland Limestone | 106 | -68 | 106.5 | -68 |  | 0 | Sea-floor |
| Lakes Entrance | 1918.5 | -1880 |  |  |  |  |  |
| Latrobe Group: |  |  |  |  |  |  |  |
| Gurnard Formation | 2097.5 | -2059 |  |  |  |  |  |
| Kingfish Formation | 2132.5 | -2094 |  |  |  |  |  |
| 54-5 Sand | 2513.5 | -2475 |  |  |  |  |  |
| 62 Sand | 2798.5 | -2760 |  |  |  |  |  |
| Volador Fm 66.5 Sand | 2978.5 | -2940 |  |  |  |  |  |
| 67 Sand | 3218.5 | -3180 |  |  |  |  |  |
| 70 Sand | 3438.5 | -3400 |  |  |  |  |  |
| TD | 3501.5 | -3463 |  |  |  |  |  |

Commence drilling cement with seawater at 10:00 hrs, drill to 853m at 13:10 hrs, displace to Gel mud, perform FIT, displace to KCl/ PHPA mud, drill ahead 311mm (12-1/4in) hole from 15:00 hrs. Good detection of LWD signal (except for Den/Por, see above). Data being transmitted by Interact. Sample interval 10m. All BHI equipment fully operational. All mudlog data being transmitted by WITS to SLB. SLB still to resolve BHI gas and lithology data transmission via Interact.

Geologists:  Simon Ward / Roman Leslie

# Text boxes

Lithology Summary:

Drilling Summary:

Oil Fluorescence Summary:

Gas Summary:

Fluid Loss:

MWD Summary:

Wellsite Formation Picks:

Comments: