| Stuart Petroleum Limited | BAZZARD-1 |
| --- | --- |
| Report Date: | 29 September 2008 | Bit Diameter: | 311.1 mm (12.25”) |
| Report Number: | 7 | Last Casing: | 399 mm (13-3/8”) @ 841 m |
| Spud Date: | 20 September 2008 | LOT: | 15.06 ppg at 853m |
| Days from Spud: | 9 | Mud Weight: | 9.3 |
| Current Activity (06:00 hours): | Drilling 311 mm (12-1/4”) hole. | ECD: | 9.7 |
| Water Depth: | 68 m | Mud Type: | KCl / PHPA |
| Rotary Table: | 38.5 m above AHD. | Last Survey: | 2018.76m inclination 2.3° azimuth 344.00° |

| Time / Date | m MDRT | m TVDRT | Previous, m | Progress, m | Drill rate m/hr |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Minimum | Maximum | Average |
| 06:00 hrs, 29/09/08 | 2082 | 2081.7 | 1270 | 812 | 10.0 | 81.5 | 53.7 |

| Depth m MDRT | Description | Gas Data (total gas in %; C1, C2, C3, iC4, nC4, iC5, nC5 in ppm), C1/2/3/4/5/ ratios indicated below. |
| --- | --- | --- |
| 1270-1370 | CALCAREOUS CLAYSTONE (80-95%): dark grey to dark olive grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately to highly calcareous, in parts grading to calcilutite. Trace forams. SILTSTONE (5-20%): medium grey to greenish grey, firm to hard, blocky, argillaceous, moderately calcareous. Trace black carbonaceous laminae. Trace crystalline calcite. | 0.38, 3623/1/9/1/1/1/0 100/0/0/0/0 |
| 1370-1430 | CALCAREOUS CLAYSTONE (80-95%): dark grey to dark olive grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately to highly calcareous, in parts grading to calcilutite. Trace forams. SILTSTONE (5-10%): medium grey to greenish grey, firm to hard, blocky, argillaceous, moderately calcareous. Trace black carbonaceous laminae. Trace crystalline calcite. Trace forams. Trace pyrite. LIMESTONE (5-10%): dark grey to clear to white to grey, soft to moderately hard to hard, crystalline to amorphous, trace shell fragments. | 0.37, 3462/3/11/2/1/1/0 99/0/1/0/0 |
| 1430-1490 | CALCAREOUS CLAYSTONE (95-100%): medium light grey to dark grey to dark olive grey, soft to moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately calcareous, commonly grading to calcilutite. Trace forams. SILTSTONE (0-5%): medium grey to greenish grey, firm to hard, blocky, argillaceous, moderately calcareous. Trace black carbonaceous laminae. Trace crystalline calcite. | 0.35, 3326/5/12/2/1/1/0 99/0/1/0/0 |
| 1490-1730 | CALCAREOUS CLAYSTONE (40-100%): medium light grey to dark grey to dark olive grey, soft to moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately to highly calcareous, commonly grading to calcilutite. Trace forams. Trace to ~1% pyrite. SILTSTONE (tr-60%): medium grey to greenish grey, firm to hard, blocky, argillaceous, moderately calcareous. Trace black carbonaceous laminae. Trace crystalline calcite. Trace pyrite. LIMESTONE (tr-15%): white to greyish yellow to dark grey, hard to very hard, microcrystaline to crystalline to amorphous. CALCARENITE (0-15%): light olive grey to greenish grey to greyish yellow, subblocky aggregates, moderately hard, fine-grained (lower-upper), moderately sorted, semi translucent to opaque sub angular calcite, calcite cemented, poor inferred porosity. | 0.33, 2907/11/20/5/3/3/0 99/0/1/0/0 |
| 1730-1850 | CALCAREOUS CLAYSTONE (75-95%): medium light grey to medium grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately to highly calcareous, commonly grading to calcilutite. Trace forams. SILTSTONE (5-25%): medium grey to greenish grey, firm to hard, blocky, argillaceous, moderately to strongly calcareous. Trace black carbonaceous laminae. | 0.29, 2386/10/19/5/3/3/1 98/1/1/0/0 |
| 1850-1910 | CALCAREOUS CLAYSTONE (80-90%): medium light grey to medium grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately to highly calcareous, commonly grading to calcilutite. Trace forams. SILTSTONE (10%): medium grey to greenish grey, firm to hard, blocky, argillaceous, moderately to strongly calcareous. Trace black carbonaceous laminae. CALCARENITE (tr-10%): white to pale grey to greenish-grey, subblocky, soft / amorphous to hard, fine-grained (lower), moderately sorted, opaque sub angular to subrounded calcite, strongly calcite cemented in hard fraction, trace to common (at 1860m) dark green fine to medium grained glauconite, poor inferred porosity. | 0.24, 2080/10/16/5/3/3/1 98/1/1/0/0 |
| 1910-1970 | LAKES ENTRANCE FORMATION: CLAYSTONE (70-90%): light to medium grey to slightly brownish grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately to highly calcareous, grading in parts to calcilutite. Trace forams. SILTSTONE (10%): medium grey to greenish grey, firm to hard, blocky, argillaceous, moderately to highly calcareous. Trace black carbonaceous laminae. Trace pyrite. CALCARENITE (10-20% from 1940-1960m): light olive-grey to greenish-grey, subblocky aggregates, moderately hard, very fine-grained (lower), moderately sorted, semi translucent to opaque sub angular calcite, calcite cemented, poor inferred porosity. | 0.17, 1238/7/10/3/1/2/0 98/1/1/0/00 |
| 1970-2060 | CALCILUTITE (50-60%): light olive grey to light grey, soft to firm, subblocky, common clastic silt and clay. CLAYSTONE (35-45%): medium light grey to medium grey, moderately firm, subblocky to blocky, slightly silty, trace mica flakes, trace carbonaceous flakes, moderately to highly calcareous. Trace forams. SILTSTONE (5-10%): medium grey to greenish grey, firm to hard, blocky, argillaceous, moderately to highly calcareous. Trace black carbonaceous laminae. | 0.15, 1052/12/11/3/1/1/0 97/2/1/0/0 |

| Depth m MDRT | Fluorescence | Cut | Residue ring / film |
| --- | --- | --- | --- |

| (m MDRT) | Total Gas (%) | Methane (ppm) | Ethane (ppm) | Propane (ppm) | i-Butane (ppm) | n-Butane (ppm) | i-Pentane (ppm) | n-Pentane (ppm) | % Ratios (C1/2/3/4/5) | Type |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1270-1910 | 0.33 | 2934 | 8 | 16 | 4 | 2 | 2 | tr | 99/0/1/0/0 | BG |
| 1910-2060 | 0.15 | 1103 | 11 | 11 | 3 | 1 | 1 | tr | 98/1/1/0/0 | BG |

KEY: BG Background gas, CG Connection gas,   POG Pumps-off gas, TG Trip gas, STG Short trip gas, FMG Formation gas

| From m MDRT | To m MDRT | Total or Rate (bbl) | Remarks |
| --- | --- | --- | --- |
|  |  |  | Normal surface fluid losses only. |

Run 2 MWD / LWD string as follows: Resistivity: 3.98m, ARC Gamma 4.03m, D&I (survey) 11.54m, Sonic 21.01m, SADN Density 25.51m, SADN Porosity 28.37m LWD RT data quality poor in places due to faulty upper standpipe pressure sensor which will be changed out at the next trip. System reset 1960-1968m, brief RT data gap. Resistivity RT curves absent from Interact and RT display below 1955m, available from 2060m. RT Gamma data missing 2025-2055m, RT Sonic data missing 2010-2037m. Den/Por data in memory only.

| Formation (Unit) | Prognosed MDRT SS, m | Actual MDRT TVDSS, m | Actual Thickness | Difference to Prog (TVDSS) | Basis Of Pick |
| --- | --- | --- | --- | --- | --- |
| Gippsland Limestone | 106 | -68 | 106.5 | -68 | 1803.4 | 0 | Sea-floor |
| Lakes Entrance | 1918.5 | -1880 | 1910 | -1871.4 |  | -8.6 (i.e. high) | Slight increase in gamma, subtle change in cuttings |
| Latrobe Group: |  |  |  |  |  |  |  |
| Gurnard Formation | 2097.5 | -2059 |  |  |  |  |  |
| Kingfish Formation | 2132.5 | -2094 |  |  |  |  |  |
| 54-5 Sand | 2513.5 | -2475 |  |  |  |  |  |
| 62 Sand | 2798.5 | -2760 |  |  |  |  |  |
| Volador Fm 66.5 Sand | 2978.5 | -2940 |  |  |  |  |  |
| 67 Sand | 3218.5 | -3180 |  |  |  |  |  |
| 70 Sand | 3438.5 | -3400 |  |  |  |  |  |
| TD | 3501.5 | -3463 |  |  |  |  |  |

Gas readings diminishing as mud weight increased to 9.3 ppg (previously 8.9 ppg at 06:00 hrs 28 Sept). Sized calcium carbonate and Barablok (asphaltic material) added to mud from 1915m. Lakes Entrance Fm recognised at 1910 mAH from subtle change in cuttings (slight colour change, slight apparent decrease in overall calcite content), coincident with 10-20api increase in gamma baseline.

Geologists:  Simon Ward / Roman Leslie

# Text boxes

Lithology Summary:

Drilling Summary:

Oil Fluorescence Summary:

Gas Summary:

Fluid Loss:

MWD Summary:

Wellsite Formation Picks:

Comments: