PETRO TECH PTY. LTD. A.C.N. (009 116 429) Boola Boola No.2 PEP 166

DAILY GEOLOGICAL REPORT No. 1 Date: 1-06-2007

Depth: 0m Progress: 0m Days from Spud: 0

Rig: CENTURY RIG No.11 GL(AHD): 40.0m Drilling Rep: Lou DeVattimo RT: (datum) 45.2m Geologist: David Horner Last Casing: 13⅜" at 15m

0600 hrs Update: Boola Boola No.2 was spudded at 0030hrs, 2nd June, 2007 with 12¼" hole and gel spud mud. Drill ahead with 12¼" hole to 79m. Lithology (spud-69m) is a massive Sandstone (100%) light orange, very fine to pebble, dominantly very coarse, subangular to subrounded, poorly sorted, no visible cement, trace orange brown argillaceous matrix, clear to opaque quartz grains often with orange iron oxide staining, trace green grey cherty lithics, trace black coal detritus, unconsolidated, very good inferred porosity, no oil fluorescence. Top LaTrobe Group at 69m RKB.

Comments: 13⅜" was set to 15m RKB prior to rig mobilization. Prepare to spud Boola Boola No.2.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
|  | No new formation drilled. |  |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Haunted Hill Formation LaTrobe Group Strzelecki Group Rintouls Creek Sandstone | 5.2 60 565 1065 | 5.2 | +40 | 0 |
| Tyers Conglomerate | 1265 |  |  |  |
| Basement | 1465 |  |  |  |
| Total Depth | 1500 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
|  | No new formation drilled. |