PETRO TECH PTY. LTD. A.C.N. (009 116 429) Boola Boola No.2 PEP 166

DAILY GEOLOGICAL REPORT No. 22 Date: 22-06-2007

Depth: 1706m Progress: 75m Days from Spud: 21

Rig: CENTURY RIG No.11 GL(AHD): 40.0m Drilling Rep: Lou DeVattimo RT: (datum) 45.2m Geologist: David Horner Last Casing: 9⅝" at 572m

0600 hrs Update: Drill ahead with 8½" hole at 1731m. Current lithology Strzelecki Shale (50%) laminated and thinly interbedded with tight siliceous very fine Sandstone (50%), background gas 0.25 units (C1 100%).

Comments: Drill ahead with 8½" hole to 1706m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1631-1706 | Strzelecki Group - No Show | TG 0.1-0.3u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Haunted Hill Formation LaTrobe Group - Yallourn Formation LaTrobe Group - Morwell 1 Formation LaTrobe Group - Morewell 2 Formation | 5.2 60 100 350 | 5.2 69 110 370 | +40 -24 -65 -325 | 0 9 Low 10 Low 20 Low |
| LaTrobe Group - Sub-Morewell 2 Fm | 555 | 522 | -477 | 33 High |
| LaTrobe Group - Basal Conglomerate | - | 553 | -508 | - |
| Strzelecki Group | 565 | 582 | -537 | 17 Low |
| Rintouls Creek Sandstone | 1065 |  |  |  |
| Tyers Conglomerate | 1265 |  |  |  |
| Basement | 1465 |  |  |  |
| Total Depth | 1500 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1631-1706 | STRZELECKI GROUP Shale (90%) laminated with Sandstone (10%). SANDSTONE: off white to light brown grey, very fine, subangular to subrounded, well sorted, very strong silica cement, abundant white siliceous matrix, quartzose with common altered feldspar grains, trace black carbonaceous material, trace to common clear to white quartz veins, very hard, no visual porosity, no oil fluorescence. SHALE: medium grey to grey black, slightly to very silty, moderately to dominantly very carbonaceous, trace to common clear to white quartz veins, common slickensides, common micromica, hard, fissile. |