PETRO TECH PTY. LTD. A.C.N. (009 116 429) Boola Boola No.2 PEP 166

DAILY GEOLOGICAL REPORT No. 30 Date: 30-06-2007

Depth: 1887m Progress: 0m Days from Spud: 29

Rig: CENTURY RIG No.11 GL(AHD): 40.0m Drilling Rep: Dave Hair RT: (datum) 45.2m Geologist: David Horner Last Casing: 9⅝" at 572m

0600 hrs Update: Prepare for drill string backoff.

Comments: Continue to work stuck pipe, unable to free pipe, run free point indicator.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
|  | No new formation drilled. |  |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Haunted Hill Formation LaTrobe Group - Yallourn Formation LaTrobe Group - Morwell 1 Formation LaTrobe Group - Morewell 2 Formation | 5.2 60 100 350 | 5.2 69 110 370 | +40 -24 -65 -325 | 0 9 Low 10 Low 20 Low |
| LaTrobe Group - Sub-Morewell 2 Fm | 555 | 522 | -477 | 33 High |
| LaTrobe Group - Basal Conglomerate | - | 553 | -508 | - |
| Strzelecki Group | 565 | 582 | -537 | 17 Low |
| Rintouls Creek Sandstone | 1065 | - | - | - |
| Tyers Conglomerate | 1265 | - | - | - |
| Basement | 1465 | - | - | - |
| Total Depth | 1500 | 1887 | -1842 | 387 Low |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
|  | No new formation drilled. |