LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Boola Boola-2 | REPORT No. : | 22 | DFS: | 21 | DATE : | 22-06-07 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 1706.00m | LAST DEPTH : | 1631.00m | 24 HR PROGRESS: | 75.00m | PTD : | 1700 m |
| TOTAL FUEL : | 11500 | FUEL USAGE : | 3900 | DAYCOST : $ | 49,654 | CUM. COST : $ | 2,086,521 |
| 0600 OPS : | 0-0 - Drill 81/2 hole 1693 to 1731m |
| Next 24 Hrs Op | Drill – Wiper Trip – Drill ahead |
| Site Personnel: | Dave Hair - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 8 | 7 Re-run |  | Drilling | 23 |  | Density | 1.128 | S.G. |
| Size (mm) | 216 | 216 |  | Tripping | 0 |  | Viscosity | 34 | Sec |
| Make | Reed | Reed |  | Surveys | .5 |  | Water Loss | 19.4 | Cc |
| Type | TD43AP | TD 51AP |  | Rigged up BOP |  |  | pH | 8.5 | Strip |
| IADC Code | 4-3-7 | 5-1-7 |  | Slip cut Line |  |  | Filter Cake | 1 | 32 nd |
| Serial Number | EM2047 | JK2076 |  | Circulate Sample |  |  | PV / YP | 7/10 | Cp/lb/100’ |
| Nozzles (32) | 12-12-12 | 12-12-12 |  | Casing |  |  | Gels | 8/12 | S/m |
| Depth in (m) | 1594 | 1415 |  | F.I.T |  |  | Sand | tr | % Vol |
| Depth out (m) |  | 1594 |  | Surveys |  |  | Solids | 7.2 | % Vol |
| Total Metres | 112 so far | 179 |  | Circulate & Condition |  |  | Oil |  | % Vol |
| Hours | 39 so far | 60 |  | Rig Service | .5 |  | K+ | 5,250 | Mg/l |
| WOB (kg) | 15 | 14 |  | Pick up BHA |  |  | Chlorides | 7800 | Mg/l |
| RPM | 90 | 80 |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition | in | 6-3-BT-M-E-2-LT-8-PR |  | Repair rig |  |  | KCL | 1.0 | % by wt |
| Impact Force | 562 | 565 |  | Wait On Cement |  |  | Daily Cost $ | 1343.30 |
| Jet Velocity | 334 | 334 |  | Test BOPs |  |  | Cum Cost $ | 27069.7 |
| B.H.A.: | 216mm Bit-Bit Sub-NMDC-1 x 6-1/4 DC-STB-15 x 6-1/4 DC-JARS-1 x 6-1/4 DC-4 HWDP - |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 30 | ° at | 1486 | m |  | Type | Amount |
| 0000 | 1000 | Drill 81/2 hole 1631m to 1659m |  | 25 | ° at | 1581 | m |  | Biocide |  |
| 1000 | 1030 | Rig Service |  | 15 | ° at | 1694 | m |  | Sodium Sulphite |  |
| 1030 | 2330 | Drill 81/2 hole 1659m to 1706m |  | 20 | ° at | 1131 | m |  | Pac - L | 4 |
| 2330 | 2400 | Deviation Survey @ 1694 – 15deg - Az 257 |  | 23½ | ° at | 1186 | m |  | Barite |  |
|  |  |  |  | 24 | ° at | 1206 | m |  | Xanthum gum | 2 |
|  |  |  |  | 26 | ° at | 1281 | m |  | PHPA/ KCL |  |
|  |  |  |  | 31 | ° at | 1354 | m |  | Caustic Soda |  |
|  |  |  |  | PUMP 1 |  | PUMP 2 |
|  |  |  |  | Liner | 108 | mm |  | Liner | 108 | mm |
|  |  |  |  | Pressure | 10,000 | kPa |  | Pressure | 10,000 | KPa |
|  |  |  |  | A.V. DP | 163 | f/min |  | A.V. DP |  | f/min |
|  |  |  |  | A.V. DC | 255 | f/min |  | A.V. DC |  | f/min |
|  |  |  |  | SPM | 85 |  | SPM | 85 |
|  |  | 1 loads of water used today Total 35 |  | GPM | 173 |  | GPM | 173 |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton | 50% Excess |  | Size | 244 | mm |
|  |  |  |  | Class Bulk | 506 |  | Weight | 52.48 | Kg/m |
|  |  |  |  | % | NF6 Lead | 0.015g/sk |  | Grade | K-55 |  |
|  |  |  |  | % | Econolite Lead | 0.580g/sk |  | Connection | BTC |  |
|  |  | Held pre-tour safety and job meetings |  | % | NF6 Tail | 0.006g/sk |  | Joints | 47 |  |
|  |  |  |  | % | HR-6L Tail | 0.025g/sk |  | Length | 466.14 | m |
| Days since | LTA | 391 |  | Av. Wt Lead/Tail | 12.5p/g /15.6p/g |  | Depth | 572 m from RKB | m |

,66