LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 10 Date: 19-10-2005

Depth: 956m Progress: 72m Days from Spud: 10

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 244mm at 258m

0600 hrs Update: Drill ahead with 216mm hole at 992m. Lithology Sandstone (90%) with minor interbedded Claystone (10%), background gas trace to 1 unit - no shows.

Comments: Drill ahead with 216mm hole to 947m, survey = 2.5 degrees, POOH for new bit, trip gas 1 unit, drill ahead with 216mm hole.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 884-956 | Strzelecki Formation - No Show | TG tr-2u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 10

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 884-956 | STRZELECKI FORMATION Sandstone (80%) with minor thinly interbedded and laminated Claystone (20%). SANDSTONE: light to medium green grey, very fine to coarse, dominantly medium, subangular to subrounded, moderately sorted, moderate silica and weak calcareous cements, common to abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, common quartz grains, trace coarse brown mica flakes, trace to rarely abundant black coaly detritus, hard, very poor to poor visual porosity, no oil fluorescence. CLAYSTONE: medium grey to medium brown grey to medium brown to medium green grey, very silty, occasionally very finely arenaceous with altered lithic grains, trace black carbonaceous flecks, trace to rarely abundant black coal detritus, trace micromica, firm, slightly subfissile. |