LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 11 Date: 20-10-2005

Depth: 1082m Progress: 126m Days from Spud: 11

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 244mm at 258m

0600 hrs Update: Drill ahead with 216mm hole 1100m, circulate, survey, wiper trip - prepare to POOH to log and run casing. Lithology: Sandstone (50%) laminated and thinly interbedded with Claystone (50%), background gas 0.3 units.

Comments: Drill ahead with 216mm hole to 1082m. Carbide at 1042m = 10 units, hole 14% overgauge.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 956-1082 | Strzelecki Formation - No Show The Coal at 1050m has no fluorescence but gives a weak to moderately bright very pale yellow white crush cut - this most likely signifies the section at this depth is in the oil generation level of maturity. | TG tr-1.5u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 11

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 956-1082 | STRZELECKI FORMATION Sandstone (80%) with minor thinly interbedded and laminated Claystone (20%) and minor laminae of Coal (trace) at 1050m.. SANDSTONE: light to medium green grey, very fine to coarse, dominantly medium, subangular to subrounded, moderately sorted, moderate silica and moderate to strong calcareous cements, common to abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, common quartz grains, trace black coaly detritus, hard, poor visual porosity, no oil fluorescence. CLAYSTONE: off white to medium brown to medium green grey, moderately to very silty, very finely arenaceous with altered lithic grains in part, trace black carbonaceous flecks, trace black coal detritus, trace micromica, moderately hard, subfissile. COAL: black, subvitreous, angular to subconchoidal fracture - cleated, clean, hard, brittle. CUT: The coal at 1050m has no fluorescence but gives a weak to moderately bright very pale yellow white crush cut. |