LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 16 Date: 25-10-2005

Depth: 1147m Progress: 47m Days from Spud: 16

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 178mm at 1097m

0600 hrs Update: Drill ahead with 156mm hole at 1178m. Current lithology: Sandstone (100%) fine grained. Background gas trace-1 unit (C1 100%).

Comments: Continue RIH, shut down rig for 6 hours due to inebriated crew, continue RIH, drill out shoe track and new hole to 1103m, perform FIT (no leak off) to 600PSI with 9.7 ppg mud (EMW = 13 ppg), drill ahead with 156mm hole to 1147m. Carbide at 1112m = 35 units.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1100-1147 | Strzelecki Formation - No Show The coal has no fluorescence but gives a weak to moderately bright very pale yellow white crush cut. | TG tr-1u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 16

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1100-1147 | STRZELECKI FORMATION Sandstone (70%) interbedded and laminated with Claystone (30%) and in part minor laminated Coal (trace). SANDSTONE: light to medium green grey, very fine to medium, dominantly fine to medium, subangular to subrounded, moderately sorted, moderate silica and moderate calcareous cements, abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, trace quartz grains, trace black coaly detritus, hard, very poor visual porosity, no oil fluorescence. CLAYSTONE: medium grey to medium green grey to medium brown grey, moderately silty, occasionally very finely arenaceous with altered lithic grains, trace black carbonaceous flecks, trace to common black coal detritus, trace micromica, moderately hard, subfissile. COAL: black, subvitreous lustre, blocky to subconchoidal fracture, clean to moderately argillaceous, hard, brittle. CUT: The coal has no fluorescence but gives a weak to moderately bright very pale yellow white crush cut. |