LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 19 Date: 28-10-2005

Depth: 1385m Progress: 117m Days from Spud: 19

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 178mm at 1097m

0600 hrs Update: Drill ahead with 156mm hole to 1397m, survey. Lithology: sandstone (90%) interbedded and laminated with claystone (10%) and minor coal (trace), background gas trace-2 unts (C1 100%). Cutting samples below 1385m indicate the presence of significant fracturing and hot water mineralization (well bore may be re-entering the main fault zone or a parasitic fault?

Comments: Drill ahead with 156mm hole to 1282m, survey, drill ahead with 156mm hole to 1385m. Cutting samples would indicate the well bore exited the main fault plane at about 1273m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1268-1302 | Strzelecki Formation - No Show The Coal below 1293m has no fluorescence but gives a weak dull light yellow crush cut, indicative of this section being in the oil generation window of maturity - note: the coal present in the faulted section drilled had nil to extremely weak oil cut, this is most probably due to hydrothermal 'cooking' by migrating hot water along the fault plane. | TG tr-2u C1 100% |
| 1302-1385 | Strzelecki Formation - No Show The coal has no fluorescence but gives a weak dull light yellow crush cut. | TG 1-2u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 19

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1268-1273 | STRZELECKI FORMATION Sandstone (60%) interbedded and laminated with Claystone (40%). SANDSTONE: light to medium green grey, very fine to occasionally medium, dominantly medium, subangular to subrounded, moderately sorted, strong silica and calcareous cements, common white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace orange brown and black lithic grains, trace quartz grains, trace black coaly material, trace veining infilled by a soft light brown soapy mineral and trace brick red mineral, trace crystalline calcite, hard, no visual porosity, no oil fluorescence. CLAYSTONE: light to dark grey, often very silty, occasionally very finely arenaceous with altered lithic grains, trace black carbonaceous flecks, common black coal detritus, trace micromica, trace slickensided surfaces, trace veining infilled by a soft light brown soapy mineral and trace brick red mineral, trace crystalline calcite, moderately hard, subfissile. |
| 1273-1302 | STRZELECKI FORMATION Sandstone (50%) interbedded and laminated with Claystone (50%) and minor Coal (trace). SANDSTONE: light to medium green grey, very fine to occasionally medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica and weak to strong calcareous cements, abundant white argillaceous matrix, abundant altered feldspar, common grey green lithic grains, trace orange brown and black lithic grains, trace quartz grains, common black coaly detritus, hard, no visual porosity, no oil fluorescence. CLAYSTONE: medium to dark grey to medium green grey, very silty in part, occasionally very finely arenaceous with altered lithic grains, trace black carbonaceous flecks, common black coal detritus, trace micromica, moderately hard, subfissile. COAL: black to very dark grey, subvitreous lustre, platy to subconchoidal fracture - slickensided, clean to often very argillaceous, hard, brittle. The Coal below 1293m has no fluorescence but gives a weak dull light yellow crush cut. |
| 1302-1385 | STRZELECKI FORMATION Sandstone (70%) interbedded and laminated with Claystone (30%) and minor Coal (trace). SANDSTONE: light to medium green grey, very fine to medium, dominantly fine, subangular to subrounded, moderately sorted, moderate silica and calcareous cements, abundant white argillaceous matrix, abundant altered feldspar, common grey green lithics, trace orange brown and black lithic, common quartz grains, trace black coaly detritus, moderately hard, very poor visual porosity, no oil fluorescence. CLAYSTONE: light to medium grey to medium brown grey, very silty in part, very finely arenaceous with altered feldspars in part, trace black carbonaceous flecks, trace black coal detritus, trace micromica, moderately hard, subfissile. COAL: black to very dark brown grey, earthy to subvitreous lustre, platy to blocky to subconchoidal fracture, clean to dominantly very argillaceous, hard, brittle - the coal has no fluorescence but gives a very weak dull light yellow crush cut. |