LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 27 Date: 5-11-2005

Depth: 1898m Progress: 49m Days from Spud: 27

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 178mm at 1097m

0600 hrs Update: Finish casing survey, wait on Haliburton cementers.

Comments: Drill ahead with 156mm hole to 1891m, Survey at 1890m = 7.9°, BHT 61.8°, drill ahead to 1898m, POOH for suspected hole in 178mm casing, run casing survey, establish hole in 178mm casing at 127m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1849-1898 | Strzelecki Formation - No Show | TG tr-2u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 27

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1849-1898 | STRZELECKI FORMATION Sandstone (80%) interbedded and laminated with and in part grading to Claystone (20%) with minor Coal (trace). SANDSTONE: light to medium green grey, very fine to occasionally medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica and weak calcareous cements, abundant white argillaceous matrix - matrix supported, abundant altered feldspar, common grey green lithics, rare orange brown and black lithics, trace quartz grains, common black coal detritus, hard, no visual porosity, no oil fluorescence. CLAYSTONE: light to medium grey to medium brown grey, very silty in part, very finely arenaceous with altered feldspars grains in part, slightly calcareous where arenaceous, trace black carbonaceous flecks, common black coal detritus, trace micromica, moderately hard, subfissile. COAL: black to dark brown grey, earthy where argillaceous, subvitreous where clean, platy to subconchoidal fracture, very argillaceous in part, hard, brittle. CUT: The coal has no fluorescence but gives a weak dull pale yellow crush cut. |