LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 29 Date: 7-11-2005

Depth: 1963m Progress: 65m Days from Spud: 29

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 178mm at 1097m

0600 hrs Update: Drill ahead with 156mm hole to 1974m, POOH due to low ROP.

Comments: Drill out cement plugs, RIH, drill ahead with 156mm hole to 1963m. Trip gas trace C1.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1898-1963 | Strzelecki Formation - No Show | TG tr-1u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 29

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1898-1963 | STRZELECKI FORMATION Sandstone (80%) interbedded and laminated with Claystone (20%) and minor Coal (trace). SANDSTONE: light to medium green grey, very fine to medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica and weak calcareous cements, abundant white argillaceous matrix - matrix supported, abundant altered feldspar, common grey green lithics, rare orange brown and black lithics, trace quartz grains, trace to common black coal detritus, hard, no visual porosity, no oil fluorescence. CLAYSTONE: light to medium dark grey to medium brown grey, very silty in part - grades to siltstone, very finely arenaceous with altered feldspars grains in part, slightly calcareous where arenaceous, trace black carbonaceous flecks, trace black coal detritus, common micromica, moderately hard, subfissile. COAL: black to dark brown grey, earthy where argillaceous, subvitreous where clean, platy to subconchoidal fracture, very argillaceous in part, hard, brittle. The coal has no fluorescence but gives a very weak dull pale yellow crush cut. |