LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 2 Date: 11-10-05

Depth: 71m Progress: 26m Days from Spud: 2

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 340mm at 12m

0600 hrs Update: Pump 34bbl cement plug, wait on cement.

Comments: Pump high viscosity LCM pills to try and cure total loss of circulation, drill ahead with no returns to surface 45-71m, POOH, RIH open ended and begin pumping 34bbl cement plug.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 45-71 | LaTrobe Formation - Drilled with no returns to surface. | TG 0u |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 | +73 | 0 |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 2

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 45-71 | Drilled with no returns to surface. Lithology interpreted from drill rate to be LaTrobe Coal from 44-66m, with LaTrobe Sandstone from 66-71m. |