LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 30 Date: 8-11-2005

Depth: 1974m Progress: 11m Days from Spud: 30

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 178mm at 1097m

0600 hrs Update: RIH with new bit prior to drilling ahead.

Comments: Drill ahead with 156mm hole to 1974m, POOH, bit missing 1 cone, RIH with reverse circulation junk basket, POOH with junk basket, recovered lost cone, make up and RIH with new bit.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1963-1974 | Strzelecki Formation - No Show | TG tr-1u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 30

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1963-1974 | STRZELECKI FORMATION Sandstone (80%) interbedded and laminated with Claystone (20%). SANDSTONE: light to medium green grey, very fine to occasionally medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica and weak calcareous cements, abundant white argillaceous matrix - matrix supported, abundant altered feldspar, common grey green lithics, rare orange brown and black lithics, trace quartz grains, trace to common black coal detritus, hard, no visual porosity, no oil fluorescence. CLAYSTONE: off white to medium dark grey to medium brown grey, very silty in part - grades to siltstone, very finely arenaceous with altered feldspars grains in part, slightly calcareous where arenaceous, trace black carbonaceous flecks, common black coal detritus, common micromica, moderately hard, subfissile. |