LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 35 Date: 13-11-2005

Depth: 2271m Progress: 78m Days from Spud: 35

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 178mm at 1097m

0600 hrs Update: POOH at 2271m due to high torque, bit missing one cone, wait on fishing tools.

Comments: RIH with new 6" (152mm) bit, trip gas trace, drill ahead with 152mm hole to 2271m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 2193-2271 | Strzelecki Formation - No Show Maximum gas 2 units from coal at 2254m. | TG tr-2u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 35

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 2193-2243 | STRZELECKI FORMATION Claystone (90%) laminated with Sandstone (10%). SANDSTONE: light to medium green grey, trace light brown and very calcareous, very fine, subangular to subrounded, moderately sorted, strong silica and weak calcareous cements, abundant white argillaceous matrix - matrix supported, abundant altered feldspar grains, common grey green lithics, rare orange brown and black lithics, trace quartz grains, trace brick red mineral, trace black coal detritus, hard, no visual porosity, no oil fluorescence. CLAYSTONE: light to dark grey to medium brown grey, often very silty - grades to siltstone, very finely arenaceous with altered feldspars grains in part, slightly calcareous where arenaceous, moderately carbonaceous in part, common black coal detritus, common micromica, hard, subfissile. |
| 2243-2271 | STRZELECKI FORMATION Massive Sandstone (100%) with minor laminated Claystone (Trace). SANDSTONE: light to medium green grey, very fine to medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica and moderate calcareous cements, abundant white argillaceous matrix - matrix supported, abundant altered feldspar grains, common grey green lithics, rare orange brown and black lithics, trace quartz grains, common black coal detritus, very hard, no visual porosity, no oil fluorescence. CLAYSTONE: light to dark grey to medium brown grey, often very silty - grades to siltstone, very finely arenaceous with altered feldspars grains in part, slightly calcareous where arenaceous, moderately carbonaceous in part, common black coal detritus, common micromica, hard, subfissile. |