LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 38 Date: 16-11-2005

Depth: 2323m Progress: 35m Days from Spud: 38

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 178mm at 1097m

0600 hrs Update: POOH for new bit.

Comments: Drill ahead with 152mm hole to 2323m, POOH due to low ROP.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 2288-2323 | Strzelecki Formation - No Show | TG tr-0.5u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 38

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 2288-2323 | STRZELECKI FORMATION Claystone (70%) with laminated and grading to Sandstone (30%). SANDSTONE: light to medium green grey, silty to fine, dominantly fine, subangular to subrounded, moderately sorted, very strong silica and moderate calcareous cements, abundant white argillaceous matrix, abundant altered feldspar grains, common grey green lithics, rare orange brown and black lithics, trace quartz grains, trace black coal detritus, trace calcite lined fractures, very hard, no visual porosity, no oil fluorescence. CLAYSTONE: off white to dark grey to medium brown grey, often very silty - grades to siltstone, often very finely arenaceouswith altered feldspars grains grades to sandstone, slightly calcareous where arenaceous, moderately carbonaceous in part, common black coal detritus, common micromica, trace calcite lined fractures, common brick red vein infill in part, hard, subfissile. |