LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 39 Date: 17-11-2005

Depth: 2341m Progress: 18m Days from Spud: 39

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 178mm at 1097m

0600 hrs Update: Circulate hole clean, POOH, rig up Baker Atlas for electric logs.

Comments: POOH due to low ROP, RIH with new bit, trip gas 0.3 units, drill ahead with 152mm hole to 2341m. Reached 2341m at 2400hrs, 17th November, 2005.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 2323-2341 | Strzelecki Formation - No Show | TG tr-0.4u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 39

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 2323-2341 | STRZELECKI FORMATION Claystone (70%) with laminated and grading to Sandstone (30%). SANDSTONE: light to medium green grey, silty to fine, dominantly very fine, subangular to subrounded, moderately sorted, very strong silica and moderate calcareous cements, abundant white argillaceous matrix, abundant altered feldspar grains, common grey green lithics, rare orange brown and black lithics, trace quartz grains, trace black coal detritus, trace to common calcite lined fractures, very hard, no visual porosity, no oil fluorescence. CLAYSTONE: off white to dark grey to medium brown grey, often very silty - grades to siltstone, often very finely arenaceous with altered feldspars grains - grades to sandstone, slightly calcareous where arenaceous, moderately carbonaceous in part, trace black coal detritus, common micromica, trace to common calcite lined fractures, hard, subfissile. |