LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 3 Date: 12-10-05

Depth: 71m Progress: 0m Days from Spud: 3

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 340mm at 12m

0600 hrs Update: Pull conductor, open hole out to 17.5" (444mm) in preparation for running 13.375" (340mm) casing.

Comments: Pump 34bbl cement plug, wait on cement, annulus not holding, pump 40bbl cement plug No.2, WOC, annulus holding, drill out to 43m, lose returns, cleanout blind to 71m, POOH, prepare to pull conductor.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
|  | No new formation drilled |  |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 | +73 | 0 |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 3

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
|  | No new formation drilled. |