LAKES OIL N.L. CUTTINGS DESCRIPTIONS WELL NAME: BOUNDARY CREEK No.2 DATE: 10-10-05 GEOLOGIST: David Horner PAGE: 1

| Interval (m) | % | Description |
| --- | --- | --- |
| 12-30 | 100 | SANDSTONE: light orange, very fine to pebble, dominantly very coarse, subangular to rounded, poorly sorted, trace orange brown argillaceous matrix, no visible cement, clear to opaque quartz grains occasionally with yellow brown iron oxide staining, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 30-44 | 100 | SANDSTONE: very light orange, very fine to very coarse, dominantly coarse, subangular to rounded, poorly sorted, no visible matrix, no visible cement, clear to opaque quartz grains occasionally with light yellow staining, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 44-71 | N.R. | Total loss of circulation - probable coal. |
| 71-90 | 100 | SANDSTONE: very light grey, fine to pebble, dominantly very coarse, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 90-100 | 100 | SANDSTONE: very light grey, fine to pebble, dominantly granular, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 100-120 | 100 | SANDSTONE: very light grey, fine to pebble, dominantly very coarse, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 120-130 | 100 | SANDSTONE: very light grey, very fine to pebble, dominantly very coarse, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 130-150 | 100 | SANDSTONE: very light grey, very fine to pebble, dominantly granular, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 150-160 | Trace | CLAYSTONE: medium brown, trace black coal detritus, very soft, very dispersive, non fissile. |
|  | 100 | SANDSTONE: very light grey, very fine to pebble, dominantly very coarse, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, common black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 160-170 | 100 | SANDSTONE: very light grey, very fine to pebble, dominantly very coarse, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 170-180 | 100 | SANDSTONE: very light grey, very fine to pebble, dominantly granular, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 180-185 | Trace | CLAYSTONE: medium brown, trace black coal detritus, trace pyrite, very soft, very dispersive, non fissile. |
|  | 100 | SANDSTONE: very light grey, very fine to pebble, dominantly very coarse, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, trace pyrite, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 185-195 | 100 | SANDSTONE: very light grey, very fine to pebble, dominantly granular, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, trace pyrite, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 195-215 | Trace | CLAYSTONE: light grey to medium brown, trace black coal detritus, trace pyrite, very soft, very dispersive, non fissile. |
|  | 100 | SANDSTONE: very light grey, very fine to pebble, dominantly granular, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, trace pyrite, unconsolidated, very good inferred porosity, no oil fluorescence |
| 215-220 | 100 | SANDSTONE: very light grey, very fine to pebble, dominantly very coarse, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, trace pyrite, unconsolidated, very good inferred porosity, no oil fluorescence. |