LAKES OIL N.L. CUTTINGS DESCRIPTIONS WELL NAME: BOUNDARY CREEK No.2 DATE: 10-10-05 GEOLOGIST: David Horner PAGE: 1

| Interval (m) | % | Description |
| --- | --- | --- |
| 12-30 | 100 | SANDSTONE: light orange, very fine to pebble, dominantly very coarse, subangular to rounded, poorly sorted, trace orange brown argillaceous matrix, no visible cement, clear to opaque quartz grains occasionally with yellow brown iron oxide staining, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 30-44 | 100 | SANDSTONE: very light orange, very fine to very coarse, dominantly coarse, subangular to rounded, poorly sorted, no visible matrix, no visible cement, clear to opaque quartz grains occasionally with light yellow staining, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 44-71 | N.R. | Total loss of circulation - probable coal. |
| 71-90 | 100 | SANDSTONE: very light grey, fine to pebble, dominantly very coarse, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 90-100 | 100 | SANDSTONE: very light grey, fine to pebble, dominantly granular, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 100-120 | 100 | SANDSTONE: very light grey, fine to pebble, dominantly very coarse, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 120-130 | 100 | SANDSTONE: very light grey, very fine to pebble, dominantly very coarse, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 130-150 | 100 | SANDSTONE: very light grey, very fine to pebble, dominantly granular, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 150-160 | Trace | CLAYSTONE: medium brown, trace black coal detritus, very soft, very dispersive, non fissile. |
|  | 100 | SANDSTONE: very light grey, very fine to pebble, dominantly very coarse, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, common black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 160-170 | 100 | SANDSTONE: very light grey, very fine to pebble, dominantly very coarse, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 170-180 | 100 | SANDSTONE: very light grey, very fine to pebble, dominantly granular, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 180-185 | Trace | CLAYSTONE: medium brown, trace black coal detritus, trace pyrite, very soft, very dispersive, non fissile. |
|  | 100 | SANDSTONE: very light grey, very fine to pebble, dominantly very coarse, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, trace pyrite, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 185-195 | 100 | SANDSTONE: very light grey, very fine to pebble, dominantly granular, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, trace pyrite, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 195-215 | Trace | CLAYSTONE: light grey to medium brown, trace black coal detritus, trace pyrite, very soft, very dispersive, non fissile. |
|  | 100 | SANDSTONE: very light grey, very fine to pebble, dominantly granular, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, trace pyrite, unconsolidated, very good inferred porosity, no oil fluorescence |
| 215-225 | 100 | SANDSTONE: very light grey, very fine to pebble, dominantly very coarse, angular to subrounded, very poorly sorted, no visible matrix, no visible cement, opaque to milky quartz grains, trace grey cherty lithics, trace black coaly detritus, trace pyrite, unconsolidated, very good inferred porosity, no oil fluorescence. |
| 225-230 | 100 | SANDSTONE: grains as for 215-225m. intermixed with abundant off white altered feldspar grains and common altered grey green and brown lithic grains, trace black coal detritus, unconsolidated, good inferred porosity, no oil fluorescence. |
| 230-235 | 10 | CLAYSTONE: medium grey to medium brown grey, moderately to very silty, trace black coal detritus, trace pyrite, very soft, very dispersive, non fissile. |
|  | 90 | SANDSTONE: as for 225-230m. |
| 235-245 | 30 | CLAYSTONE: light grey to medium green grey, moderately silty, trace black carbonaceous flecks, trace pyrite, soft, very dispersive, non fissile. |
|  | 70 | SANDSTONE: light to medium grey to medium green grey, very fine to coarse, dominantly medium, subangular to subrounded, moderately sorted, weak silica cement, common white argillaceous matrix, abundant altered feldspar and grey green and brown lithics, common quartz grains, trace black carbonaceous material, friable, poor to fair visual porosity, no oil fluorescnce. |
| 245-255 | 40 | CLAYSTONE: light grey to medium green grey to medium brown grey, moderately silty, trace black carbonaceous flecks, trace pyrite, soft, very dispersive, non fissile. |
|  | 60 | SANDSTONE: light to medium grey to medium green grey, very fine to coarse, dominantly medium to coarse, subangular to subrounded, moderately sorted, weak silica cement, common to abundant white argillaceous matrix, abundant altered feldspar and grey green and brown lithic grains, common quartz grains, trace black carbonaceous material, friable, poor to fair visual porosity, no oil fluorescnce. |
| 255-261 | 50 | CLAYSTONE: as for 245-255m. |
|  | 50 | SANDSTONE: light to medium grey to medium green grey, very fine to coarse, dominantly medium, subangular to subrounded, moderately sorted, weak silica cement, common to abundant white argillaceous matrix, abundant altered feldspar and grey green and brown lithic grains, common quartz grains, trace black carbonaceous material, friable, poor visual porosity, no oil fluorescnce. |