LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 7 Date: 16-10-2005

Depth: 509m Progress: 248m Days from Spud: 7

Rig: HUNT RIG No.2 GL(AHD): 74.0m Drilling Rep: Lou DeVattimo RT: (datum) 77.65m Geologist: David Horner Last Casing: 244mm at 258m

0600 hrs Update: Drill ahead with 216mm hole at 580m. Lithology: (509-580) Sandstone (50%) interbedded and laminated with Claystone (50%). Current lithology: Sandstone (100%) with fair visual porosity. Background gas trace to 1 unit (C1 100%), no shows.

Comments: Pressure test BOP's, make up and RIH 8.5" (216mm) drilling assembly, tag cement at 249m, drill ahead with 216mm hole to 264m, perform leak off test to 175 PSI with 8.55 lb/gal mud (EMW = 12.45 ppg), drill ahead with 216mm hole to 509m. Carbide at 277m = 170 units.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 261-360 | Strzelecki Formation - No Show | TG tr-1u C1 100% |
| 360-509 | Strzelecki Formation - No Show | TG tr-0.5u C1 100% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| LaTrobe Group Strzelecki Formation T.D. | 4.7 197 2500 | 4.7 227 | +73 -149 | 0 30 Low |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) BOUNDARY CREEK No.2 PEP 157

DAILY GEOLOGICAL REPORT No. 7

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 261-360 | STRZELECKI FORMATION Sandstone (80%) interbedded and laminated with Claystone (20%). SANDSTONE: light to medium green grey, very fine to coarse, dominantly medium, subangular to subrounded, moderately sorted, weak silica cement, abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace brown and black lithic grains, common quartz grains, trace black carbonaceous material, rare pyrite, friable, fair visual porosity, no oil fluorescnce. CLAYSTONE: light to medium grey to medium green grey, occasionally medium brown grey, moderately silty, trace black carbonaceous flecks, rare pyrite, soft, moderately dispersive, non fissile. |
| 360-509 | STRZELECKI FORMATION Sandstone (90%) interbedded and laminated with Claystone (10%). SANDSTONE: light to medium green grey, very fine to very coarse, dominantly coarse, subangular to subrounded, moderately sorted, weak silica and calcareous cements, common to abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace brown and black lithic grains, common quartz grains, trace coarse brown mica flakes, trace black carbonaceous material, trace pyrite, trace vein calcite in part, friable, poor to good dominantly fair visual porosity, no oil fluorescnce. CLAYSTONE: light to medium grey to medium green grey to medium brown grey, very silty, occasionally very finely arenaceous with altered lithic grains, trace black carbonaceous flecks, trace vein calcite, trace pyrite, soft, slightly dispersive, non fissile. |