LAKES OIL N.L. SIDE WALL CORE DESCRIPTIONS

WELL NAME: Boundary Creek No.2 DATE: 22-10-2005/20-11-2005 GEOLOGIST: David Horner PAGE: 1

| SWC No. | DEPTH (m) | REC'D (mm) | DESCRIPTION |
| --- | --- | --- | --- |

COMMENTS: Cores cut with rotary sidewall coring tool. Run #1 Cut 21, Recovered 21, Run #2 Cut 4 Recovered 4, Run #3 Cut xx, Recovered xx. Core numbers 1-18 are in good condition, core number is 19 crumbly, cores 20 & 25 are in good condition. All cores are wrapped in gladwrap, then alfoil, numbered on the alfoil and finally sealed in candle wax.

| 1 | 1080.0 | 39 | CLAYSTONE: medium dark grey, moderately carbonaceous, trace micromica, hard. |
| --- | --- | --- | --- |
| 2 | 1051.0 | 42 | COAL: black, fibrous to blocky fracture, earthy to subvitreous, hard, brittle. |
| 3 | 1020.0 | 24 | SANDSTONE: medium green grey, fine to medium, lithic, non calcareous, hard, very poor visual porosity, no oil fluorescence. |
| 4 | 1004.0 | 39 | CLAYSTONE: medium grey, very silty, hard. |
| 5 | 975.5 | 38 | SANDSTONE: medium green grey, fine to medium, lithic, common black coal detritus, non calcareous, hard, very poor visual porosity, no oil fluorescence. |
| 6 | 938.5 | 46 | SANDSTONE: medium green grey, fine to medium, lithic, slightly calcareous, moderately hard, poor visual porosity, no oil fluorescence. |
| 7 | 908.0 | 48 | SANDSTONE: medium green grey, fine to coarse, lithic, common black coal detritus, slightly calcareous, moderately hard, poor visual porosity, no oil fluorescence. |
| 8 | 860.0 | 41 | SANDSTONE: medium green grey, fine to medium, lithic, slightly calcareous, moderately hard, poor visual porosity, no oil fluorescence. |
| 9 | 774.5 | 42 | SANDSTONE: medium green grey, very fine to medium, lithic, slightly calcareous, moderately hard, poor visual porosity, no oil fluorescence. |
| 10 | 747.5 | 46 | CLAYSTONE: medium brown grey, very silty, trace black coal flecks, moderately hard. |
| 11 | 702.0 | 19 | SANDSTONE: medium green grey, very fine to coarse, lithic, slightly calcareous, moderately hard, poor visual porosity, no oil fluorescence. |
| 12 | 658.0 | 43 | SANDSTONE: medium green grey, very fine to medium, lithic, slightly calcareous, moderately hard, poor visual porosity, no oil fluorescence. |
| 13 | 638.0 | 33 | CLAYSTONE: medium brown grey, very silty, common black carbonaceous detritus, moderately hard. |
| 14 | 575.0 | 45 | SANDSTONE: medium green grey, fine to medium, lithic, non calcareous, moderately hard, poor visual porosity, no oil fluorescence. |
| 15 | 570.5 | 44 | SANDSTONE: medium green grey, fine to medium, lithic, non calcareous, friable to moderately hard, poor visual porosity, no oil fluorescence. |
| 16 | 495.0 | 41 | SANDSTONE: medium green grey, fine to coarse, lithic, slightly calcareous, friable to moderately hard, poor to fair visual porosity, no oil fluorescence. |
| 17 | 430.0 | 42 | SILTSTONE: medium brown, very finely arenaceous, trace black carbonaceous specks, firm. |
| 18 | 405.0 | 43 | SANDSTONE: medium green grey, fine to medium, lithic, common black coal detritus, slightly calcareous, friable, fair visual porosity, no oil fluorescence. |
| 19 | 354.0 | 38 | SANDSTONE: medium green grey, fine to medium, lithic, moderately calcareous, friable, poor to fair visual porosity, no oil fluorescence. |
| 20 | 320.0 | 32 | CLAYSTONE: medium dark grey, trace black carbonaceous flecks, firm. |
| 21 | 274.0 | 39 | SANDSTONE: medium green grey, fine to medium, lithic, slightly calcareous, friable, poor to fair visual porosity, no oil fluorescence. |
| 22 | 1166.0 | 45 | SANDSTONE: medium green grey, very fine to dominantly fine, lithic, slightly calcareous, trace black coaly material, hard, very poor visual porosity, no oil fluorescence. |
| 23 | 1168.0 | 39 | SANDSTONE: medium green grey, fine grained, lithic, slightly calcareous, common black coal detritus, hard, very poor visual porosity, no oil fluorescence. |
| 24 | 1172.0 | 44 | SANDSTONE: medium green grey, very fine to medium, dominantly fine, lithic, slightly calcareous, trace black coaly material, hard, very poor visual porosity, no oil fluorescence. |
| 25 | 1180.0 | 43 | SANDSTONE: medium green grey, very fine to occasionally medium, dominantly fine, lithic, slightly calcareous, trace black coaly material, hard, very poor visual porosity, no oil fluorescence. |
| 26 | 1184.0 | 37 | SANDSTONE: medium green grey, very fine to dominantly fine, lithic, strong silica and weak calcareous cements, hard, very poor visual porosity, no oil fluorescence. |
| 27 | 1213.0 | 43 | SANDSTONE: medium green grey, very fine to medium, dominantly fine, lithic, strong silica and weak calcareous cements, hard, very poor visual porosity, no oil fluorescence. |
| 28 | 1219.5 | 43 | SANDSTONE: medium green grey, very fine to medium, dominantly fine, lithic, strong silica cement, hard, very poor visual porosity, no oil fluorescence. |
| 29 | 1285.0 | 44 | SANDSTONE: medium green grey, very fine to medium, dominantly medium, lithic, strong silica and weak calcareous cements, trace black coal detritus, hard, very poor visual porosity, no oil fluorescence. |
| 30 | 1374.0 | 46 | CLAYSTONE: medium dark grey, slightly silty, slightly carbonacous, non calcareous, trace micromica, hard, subfissile. |
| 31 | 1400.5 | 45 | SANDSTONE: medium green grey, very fine to medium, dominantly fine to medium, lithic, strong silica and weak calcareous cements, trace black coal detritus, hard, no visual porosity, no oil fluorescence. |
| 32 | 1514.0 | 39 | SANDSTONE: medium green grey, fine graned, lithic, strong silica and weak calcareous cements, hard, no visual porosity, no oil fluorescence. |
| 33 | 1643.0 | 45 | SANDSTONE: medium green grey, very fine to medium, dominantly fine, lithic, very strong silica cement, common black coal detritus, very hard, no visual porosity, no oil fluorescence. |
| 34 | 1722.0 | 41 | SANDSTONE: medium green grey, very fine to medium, dominantly fine, lithic, very strong silica cement, trace black coal detritus, very hard, no visual porosity, no oil fluorescence. |
| 35 | 1732.0 | 42 | SANDSTONE: medium green grey, very fine to medium, dominantly fine, lithic, very strong silica cement, trace black coal detritus, very hard, no visual porosity, no oil fluorescence. |
| 36 | 1760.0 | 41 | SANDSTONE: medium green grey, very fine to fine, dominantly fine, lithic, very strong silica cement, very hard, no visual porosity, no oil fluorescence. |
| 37 | 1880.0 | 0 | No Recovery. |
| 38 | 2069.0 | 44 | COAL: black, subvitreous, conchoidal fracture, hard, brittle, laminated with: SANDSTONE: medium green grey, very fine, lithic, very strong silica cement, very hard, no visual porosity, no oil fluorescence. The Coal has extremely weak dull pale yellow white crush cut. |
| 39 | 2131.0 | 43 | SANDSTONE: medium green grey, very fine to fine, dominantly fine, lithic, very strong silica cement, very hard, no visual porosity, no oil fluorescence. |
| 40 | 2230.0 | 0 | No Recovery |
| 41 | 2310.0 | 38 | CLAYSTONE: dark grey, slightly silty, very carbonacous, non calcareous, common micromica, hard, subfissile. |