LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Boundary creek-2 | REPORT No. : | 22 | DFS: | 21 | DATE : | 31 Oct-05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 1526m | LAST DEPTH : | 1456m | 24 HR PROGRESS : | 70m | PTD : | 2500m |
| TOTAL FUEL : | 5,200 | FUEL USAGE : | 2,050 |  | 28,955 | CUM. COST : $ | 1,315,540 |
| 0600 OPS : | Drilling 156mm hole at 1548m |
| Next 24 hr OPS: | Drill ahead |
| Site Personnel: | Lakes 3 A.M.C 1- Mud logger 2- Hunt Energy 19 |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | Run 9 Bit 6 Rerun | Run 10 Bit7 Rerun |  | Drilling | 16.50 |  | Density | 9.25 | ppg |
| Size (mm) | 156 | 156mm |  | Tripping | 4.50 |  | Viscosity | 39 | Sec |
| Make | Reed | Varel |  | Surveys | 1.00 |  | PV @ Deg C | 14 | Deg C |
| Type | SL43HP | M-322 |  | Reaming |  |  | YP lbs/100 ft 2 | 5 | Lbs/100ft |
| IADC Code | 4-3-7 | Medium PDC |  | Slip and cut block line | 1.50 |  | API Filtrate | 6.6 | m/30min |
| Serial Number | JK 4699 | MSK-56G1 |  | Circulate and clean hole | 0.50 |  | Gels lbs/100 ft 2 | 1 / 2 / 3 |  |
| Nozzles (32) | 13-14-16 | 14-14-14 |  | Cement casing |  |  | Cake 32nds/ in | 1 |  |
| Depth in (m) | 1396 | 1456 |  | Rig repair |  |  | Sand | 0.20 | % Vol |
| Depth out (m) | 1456 |  |  | Off payroll |  |  | Solids | 6.8 | % Vol |
| Total Metres | 204 | 70 |  | Run Casing |  |  | Hardness Ca mg/l | 60 |  |
| Hours | 61 | 16.50 |  | Rig Service |  |  | KCL Concentration | 1.42 | % by wt |
| WOB (kg) | 7000 | 7000 |  | Test BOP |  |  | Chlorides | 8,900 | Mg/l |
| RPM | 100 | 100 |  | Drill out Cmt |  |  | Methyl Blue | 7.00 | Ppb equiv |
| Condition |  |  |  | Logging |  |  | K+ | 7,500 | Mg/l |
| Impact Force | 166lb/ft | 162lb/ft |  | W.0.C |  |  | Daily Cost $ | 1,928 |
| Jet Velocity | 150ft/sec | 155ft/sec |  | Install BOP |  |  | Cum Cost $ | 35,215 |
| B.H.A.: | Bit- Bit sub 2 x 4-3/4inch drill collars- stabilizer -11 x 4-3/4inch drill collars-Jars-2 x 4-3/4 inch drill collars -4 x Hevi-Wate drillpipe |
|  | BHA length 185.75m Weight below Jars 22,000lbs |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 7.00 | ° at | 1282m | m |  | Type | Amount |
| 00:00 | 00:30 | Tripped out |  | 8.00 | ° at | 1346m | m |  | Defoamer | 3 |
| 00:30 | 01:30 | Changed Bit and stabilizer position |  | 8.00 | ° at | 1387m | m |  | AMC Pac-R / L | 3 / 3 |
| 01:30 | 03:00 | Slipped and cut Blockline |  | 8.50 | ° at | 1415m | m |  | Caustic | 1 |
| 03:00 | 06:00 | Tripped in hole to 1456m |  | 8.50 | ° at | 1452m | m |  | AMC Biocide | 1 |
| 06:00 | 15:30 | Drilled 156mm hole from 1456m to 1491m |  | 9.00 | ° at | 1489m | m |  | Potassium chloride | 8 |
| 15:30 | 16:00 | Circulated for survey |  |  | ° at |  | m |  | Soium Bicarbonate | 1 |
| 16:00 | 17:00 | Ran survey on wireline at 1489m |  |  | ° at |  | m |  | Sodium sulphite | 2 |
| 17;00 | 24:00 | Drilled 156mm hole from 1491m to 1526m |  |  |  |  |
|  |  |  |  | PUMP 1 |  | PUMP 2 |
|  |  |  |  | Liner | 140 | mm |  | Liner | 140 | mm |
|  |  | Drilled through fault for the third time 1502m to 1512 |  | Pressure | 8,000 | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP | 221 | ft/min |  | A.V. DP |  | m/min |
|  |  |  |  | A.V. DC | 323 | ft/min |  | A.V. DC |  | m/min |
|  |  |  |  | SPM | 44 |  | SPM |  |
|  |  |  |  | GPM | 218 |  | GPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  | Control drilling wt on bit to drop angle on bottom |  | Sacks |  |  | Size | 178mm |  |
|  |  |  |  | Class |  |  | Weight | 38.69 | Kg/m |
|  |  |  |  |  |  |  |  | Grade | N-80 |  |
|  |  |  |  |  |  |  |  | Connection | Buttress |  |
|  | JSA | Slipped and cut Block line- Greased crown |  |  |  |  |  | Joints | 92 |  |
|  |  | Surveys |  |  |  |  |  | Length |  | m |
| Days since | LTA | 362 |  |  |  |  | Shoe | 1097 | m |

,66