LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Boundary creek-2 | REPORT No. : | 24 | DFS: | 23 | DATE : | 2- Nov-05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 1643m | LAST DEPTH : | 1581m | 24 HR PROGRESS : | 62m | PTD : | 2500m |
| TOTAL FUEL : | 9,350 | FUEL USAGE : | 2,050 |  | 28,285 | CUM. COST : $ | 1,378,772 |
| 0600 OPS : | Tripped in hole with new Bit –Pick up the Kelly |
| Next 24 hr OPS: | Drill ahead |
| Site Personnel: | Lakes 3 A.M.C 1- Mud logger 2- Hunt Energy 19 |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | Run 10 Bit 7 Rerun | Run 11 |  | Drilling | 21.50 |  | Density | 9.25 | ppg |
| Size (mm) | 156 | 156mm |  | Tripping | 1.50 |  | Viscosity | 40 | Sec |
| Make | Varel | REED |  | Surveys |  |  | PV @ Deg C | 14 | Deg C |
| Type | M-322 | SL43HP |  | Reaming |  |  | YP lbs/100 ft 2 | 9 | Lbs/100ft |
| IADC Code | Medium PDC | 4-3-7 |  | Slip and cut block line |  |  | API Filtrate | 6.4 | m/30min |
| Serial Number | JK 4699 | JK4700 |  | Circulate and clean hole | 0.50 |  | Gels lbs/100 ft 2 | 2 / 3 / 4 |  |
| Nozzles (32) | 14-14-14 | 13-16-16 |  | Cement casing |  |  | Cake 32nds/ in | 1 |  |
| Depth in (m) | 1396 | 1581 |  | Rig repair | 0.50 |  | Sand | 0.25 | % Vol |
| Depth out (m) | 1456 | 1643 |  | Off payroll |  |  | Solids | 6.6 | % Vol |
| Total Metres | 277m this hole | 62 |  | Run Casing |  |  | Hardness Ca mg/l | 70 |  |
| Hours | 78 | 21.50 |  | Rig Service |  |  | KCL Concentration | 1.75 | % by wt |
| WOB (kg) | 6000 | 8000 |  | Test BOP |  |  | Chlorides | 9,800 | Mg/l |
| RPM | 100 | 100 |  | Drill out Cmt |  |  | Methyl Blue | 7.5 | Ppb equiv |
| Condition | Worn |  |  | Logging |  |  | K+ | 9,300 | Mg/l |
| Impact Force | 162lb/ft |  |  | W.0.C |  |  | Daily Cost $ | 1,458 |
| Jet Velocity | 155ft/sec |  |  | Install BOP |  |  | Cum Cost $ | 38,636 |
| B.H.A.: | Bit- Bit sub 2 x 4-3/4inch drill collars- stabilizer -11 x 4-3/4inch drill collars-Jars-2 x 4-3/4 inch drill collars -4 x Hevi-Wate drillpipe |
|  | BHA length 185.75m Weight below Jars 22,000lbs |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 7.00 | ° at | 1282m | m |  | Type | Amount |
| 00:00 | 00;30 | Drilling 156mm hole from 1581m to 1582m |  | 8.00 | ° at | 1346m | m |  | Defoamer | 1 |
| 00:30 | 01:00 | Changed out washpipe on Swivel |  | 8.00 | ° at | 1387m | m |  | AMC Pac-R | 4 |
| 01:00 | 10:00 | Drilled 156mm hole from 1582m to 1643m |  | 8.50 | ° at | 1415m | m |  | Caustic - Barite | 1 - 14 |
| 10:00 | 10:30 | Pumped pill prior trip out due to slow drill rate |  | 8.50 | ° at | 1452m | m |  | Xanthum Gum | 1 |
| 10:30 | 24:00 | Trip out for Bit change |  | 9.00 | ° at | 1489m | m |  | Potassium chloride | 8 |
|  |  |  |  | 9.50 | ° at | 1575m | m |  | Cepac-R | 1 |
|  |  |  |  |  | ° at |  | m |  | Sodium sulphite | 1 |
|  |  |  |  | PUMP 1 |  | PUMP 2 |
|  |  | Slow drilling rate from 13:00hrs |  | Liner | 140 | mm |  | Liner | 140 | mm |
|  |  |  |  | Pressure | 8,000 | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP | 221 | ft/min |  | A.V. DP |  | m/min |
|  |  |  |  | A.V. DC | 323 | ft/min |  | A.V. DC |  | m/min |
|  |  |  |  | SPM | 44 |  | SPM |  |
|  |  |  |  | GPM | 218 |  | GPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks |  |  | Size | 178mm |  |
|  |  |  |  | Class |  |  | Weight | 38.69 | Kg/m |
|  |  |  |  |  |  |  |  | Grade | N-80 |  |
|  |  |  |  |  |  |  |  | Connection | Buttress |  |
|  | JSA | Cleaning drill collars |  |  |  |  |  | Joints | 92 |  |
|  |  | Working in the Sub-base area |  |  |  |  |  | Length |  | m |
| Days since | LTA | 364 |  |  |  |  | Shoe | 1097 | m |

,66