LAKES OIL N.L.

DAILY DRILLING REPORT

| WELL: Boundary Creek-2 | REPORT No.: 28 | DATE: 06-10-05 |
| --- | --- | --- |
| DFS: 27 | 2400 DEPTH: 1898 | Last Depth: 1898 |
| 24hr Progress: 0 | PTD: 2500 | Total Fuel: 7,550 |
| Fuel Usage: 1,250 | Daily Cost: | Cum Cost: |
| 0600hrs Operation: Run in hole to continue Drilling 156mm hole |
| Next 24hr Operation: Drill ahead |
| Site Personnel: Lakes 3-AMC 1-Higgins 2-Hunt 18-SDS 3 |

| HOURLY OPERATIONS SUMMARY (000-2400hrs) | OPERATIONS BREAKDOWN |
| --- | --- |
| FROM | TO | OPERATION |  |  |
| 00:00 | 01:00 | Rigged down SGS loggers | Drilling |  |
| 01:00 | 07:30 | Wait on Halliburton Cementer | Tripping | 2.50 |
| 07:30 |  | Tripped in hole with open pipe | Surveys |  |
|  | 08:00 | to 220m to set cement plug | Reaming |  |
| 08:00 | 09:30 | Set cement plug accross 220-180m | Slip & Cut Block Line |  |
| 09:30 | 14:30 | Wait on cement to set in hole | Circulate & Clean Hole |  |
| 14:30 | 15:00 | Tagged top cement at 180m 7K weight | Cement Casing |  |
| 15:00 | 15:30 | Tripped out with pipe | Rig Repair |  |
| 15:30 |  | Halliburton cemented from surface | Surveys |  |
|  |  | to 121m down 244mm casing and | Run Casing |  |
|  | 16:30 | inside the 178mm casing 121-110m | Rig Service |  |
| 16:30 | 20:30 | Wait on Cement to set in annulus | Test BOP’s |  |
| 20:30 |  | Tripped in hole tagged top cement at | Drill Out Cement | 2.50 |
|  | 21:30 | 90m inside the 178mm casing | Logging | 1 |
| 21:30 | 24:00 | Drilled cement from 90m - 110m | W.O.C. | 9.00 |
|  |  |  | Cement Plug | 2.50 |
|  | JSA | Laying out drill collars | Wait on Cementer | 6.50 |
|  |  | Kick indications |  |  |
|  | 368 | Days Since Last LTA: |  |  |

| BIT INFORMATION | MUD PROPERTIES |
| --- | --- |
| Bit Number | 8 Run-12 |  | Density (ppg) | 9.20 |
| Size (mm) | 156 |  | Viscosity (Sec) | 40 |
| Make | Reed |  | PV @ Degree C | 15 |
| Type | SL51HP |  | YP (lbs/100ft2) | 10 |
| IADC Code | 4-3-7 |  | API Filtrate (ml/30min) | 7.00 |
| Serial Number | HP5998 |  | Gels (lbs/100ft2) | 1 / 2 / 2 |
| Nozzles (x32) | 16-16-13 |  | Filter Cake (32nds inch) | 1/- |
| Depth In (m) | 1643 |  | Sand (% Vol) | 0.10 |
| Depth Out (m) | 1898 |  | Solids (% Vol) | 6.3 |
| Total Metres | 251 |  | Hardness (Ca mg/l) | 80 |
| Hours | 50.5 |  | KCl (% by wt) | 1.08 |
| WOB (kg) | 7000 |  | Chlorides (Mg/l) | 8,600 |
| RPM | 100 |  | Methyl Blue (ppg eq) | 6.00 |
| Condition | 2-2-RG-G-E | I-N0-HP | Potassium (Mg/l) | 5,700 |
| Impact Force | 118lb/ft |  | Daily Cost ($) | 795 |
| Jet Velocity | 122 ft/sec |  | Cumulative Cost ($) | 45,105 |

LAKES OIL N.L.

DAILY DRILLING REPORT NO.                       PAGE: 2

| CEMENT DATA | LAST CASING | CHEMICALS USED |
| --- | --- | --- |
| Sacks |  | Size | 178 mm | Starlose | 2 |
| Class |  | Weight | 38.69 | Xanthum Gum XCD | 1 |
|  |  | Grade | N-80 | Defoamer | 2 |
|  |  | Connection | Buttress | Calcium | 3 |
|  |  | Joints | 92 | Potassium Chloride | 2 |
|  |  | Length | 1092.15m |  |  |
|  |  | Shoe | 1097.00 | Sodium Bicarbonate | 4 |
|  |  |  |  | Sodium Sulphite | 1 |

| SURVEYS | PUMP No.1 | PUMP No.2 |
| --- | --- | --- |
| 7.00 deg at | 1282 m | Liner | 140mm | Liner |  |
| 8.00 deg at | 1346 m | Stroke | 16 inch | Stroke |  |
| 8.00 deg at | 1387 m | Pressure | 8970kpa | Pressure |  |
| 8.50 deg at | 1415 m | A.V. DP | 192 ft/min | A.V. DP |  |
| 8.50 deg at | 1452 m | A.V. DC | 281 ft/min | A.V. DC |  |
| 9.00 deg at | 1489m m | SPM | 40 | SPM |  |
| 9.50 deg at | 1575 m | GPM | 198 | GPM |  |
| 7.9 deg at | 1880 m |  |  |  |  |
| deg at | m |  |  |  |  |

BHA: Bit-Bit sub- 2 x 4-3/4 Drill collars-Stabilizer-11 x 4-3/4 Drill collars-Jar-2 x 4-3/4 Drill collars

COMMENTS:

REPORT BY: Lou De-Vattimo