LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Boundary creek-2 | REPORT No. : | 3 | DFS: | 2 | DATE : | 12-Oct-05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 71.00m | LAST DEPTH : | 71.00m | 24 HR PROGRESS : | .00m | PTD : | 2500m |
| TOTAL FUEL : | 12,400 | FUEL USAGE : | 750 | DAYCOST : $ | 26,243 | CUM. COST : $ | 265,370 |
| 0600 OPS : | Open out hole from 311mm to 444mm depth at 06:00hrs 58 m |
| Next 24 hr OPS: | Open hole to 444mm to 71meters from RKB then run 70m of 340mm Casing to isolate the loss circulation zone at 43 meters |
| Site Personnel: | Lakes 3- A.M.C 1- Mud logger 2- Hunt Energy 20 |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 1 Re-Run |  |  | Drilling |  |  | Density | Spud mud | ppg |
| Size (mm) | 311 |  |  | Tripping | 7.50 |  | Viscosity |  | Sec |
| Make | BBL |  |  | Surveys |  |  | PV @ Deg C |  | Deg C |
| Type | M-22 |  |  | Rigging up |  |  | YP lbs/100 ft 2 |  | Lbs/100ft |
| IADC Code | 1-1-7 |  |  | Slip and cut block line |  |  | API Filtrate |  | m/30min |
| Serial Number | 6093062 |  |  | Circulate and clean hole |  |  | Gels lbs/100 ft 2 |  |  |
| Nozzles (32) | 18-18-18 |  |  | Cement casing |  |  | Cake 32nds/ in |  |  |
| Depth in (m) | 15.00 |  |  | Rig repair |  |  | Sand |  | % Vol |
| Depth out (m) |  |  |  | Surveys |  |  | Solids |  | % Vol |
| Total Metres | 56 |  |  | Run Casing |  |  | Hardness Ca mg/l |  |  |
| Hours | 5 |  |  | Rig Service |  |  | KCL Concentration |  | % by wt |
| WOB (kg) | 1000 |  |  | Pulled conductor pipe | 2.00 |  | Chlorides |  | Mg/l |
| RPM | 60 |  |  | Drill out Cmt | 1.00 |  | Methyl Blue |  | Ppb equiv |
| Condition |  |  |  | Logging |  |  | K+ |  | Mg/l |
| Impact Force | 21lb/ft |  |  | W.0.C | 12.00 |  | Daily Cost $ | 836 |
| Jet Velocity | 45ft/sec |  |  | Cement plug | 0.50 |  | Cum Cost $ | 4,632 |
| B.H.A.: |  |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  |  | ° at |  | m |  | Type | Amount |
| 00:00 | 07:00 | Wait on cement plug # 1 to set at loss circ zone |  |  | ° at |  | m |  | Ausgel | 82 |
| 07:00 | 07:30 | Tagged cement at 43m |  |  | ° at |  | m |  |  |  |
| 07:30 |  | Attempted to circulate no returns loss circulation |  |  | ° at |  | m |  |  |  |
|  | 09:00 | still evident – rigged up Halliburton |  |  | ° at |  | m |  |  |  |
| 09:00 | 09:30 | Set cement pug # 2 34bbls of slurry |  |  | ° at |  | m |  |  |  |
| 09:30 | 14:30 | Wait on cement plug # 2 to set |  |  | ° at |  | m |  |  |  |
| 14:30 | 16:30 | R.I.H to 40m and tagged cement with 311mm bit |  |  | ° at | 1713 | m |  |  |  |
| 16;30 |  | Drilled out cement from 40m to 71m lost mud returns |  |  |  |  |
|  | 17:30 | at 43m |  | PUMP 1 |  | PUMP 2 |
| 17:30 | 21:30 | Pulled out of hole layed out drilling assembly |  | Liner | 140 | mm |  | Liner | 140 | mm |
| 21:30 | 23:30 | Pulled the conductor pipe and layed out same |  | Pressure | 700 | kPa |  | Pressure | 10,500 | KPa |
| 23:30 | 24:00 | Made up 17-1/2 inch ( 444mm ) Bit |  | A.V. DP |  | m/min |  | A.V. DP |  | m/min |
|  |  |  |  | A.V. DC |  | m/min |  | A.V. DC |  | m/min |
|  |  |  |  | SPM |  |  | SPM |  |
|  |  | Due to loss circulation problems at 43m the hole size |  | GPM |  |  | GPM |  |
|  |  | From surface to 71m will be reamed out to 444mm |  |  |  |  |
|  |  | and 340mm Casing will be set and cemented so |  | CEMENT DATA |  | LAST CASING |
|  |  | as to isolate the loss circulation zone , as two attempts |  | Sacks | 330 |  | Size | 340mm |  |
|  |  | to seal off with cement and loss circulation material |  | Class | A |  | Weight | 71.43 | Kg/m |
|  |  | did not work |  |  | Econolite | 88gals |  | Grade | K-55 |  |
|  |  |  |  |  | Calcium chloride | 150lbs |  | Connection | Buttress |  |
|  |  |  |  |  | Defoamer | 3 gals |  | Joints | 1 |  |
|  |  |  |  |  |  |  |  | Length | 12.00 | m |
| Days since | LTA | 344 |  |  |  |  | Shoe |  | m |

,66