LAKES OIL N.L.

DAILY DRILLING REPORT

| WELL: Boundary Crk-2 | REPORT No.: 30 | DATE: 08-11-05 |
| --- | --- | --- |
| DFS: 29 | 2400 DEPTH: 1974 | Last Depth: 1963 |
| 24hr Progress: 11 | PTD: 2500 | Total Fuel: 4,800 |
| Fuel Usage: 2000 | Daily Cost: 33,457 | Cum Cost: 1,580,177 |
| 0600hrs Operation: Drilling 156mm hole at 1974m |
| Next 24hr Operation: Drill ahead with 156mm Bit |
| Site Personnel: Lakes 3-AMC 1-Higgins 2-Hunt 19 |

| HOURLY OPERATIONS SUMMARY (000-2400hrs) | OPERATIONS BREAKDOWN |
| --- | --- |
| FROM | TO | OPERATION |  |  |
| 00:00 | 04:00 | Drilled 156mm hole 1963m to 1974m | Drilling | 4.00 |
| 04:00 | 04:30 | Circulated | Tripping | 14.00 |
| 04:30 | 05:30 | Ran survey at 1956m | Surveys | 1.00 |
| 05:30 | 10:00 | Tripped out for Bit change | Reaming |  |
| 10:00 | 10:30 | Serviced the Rig | Slip & Cut Block Line |  |
| 10:30 | 11:30 | Wait on Baker oil tool overshot | Circulate & Clean Hole | 2.00 |
| 11:30 | 12:00 | Made up tool to fish Bit cone | Cement Casing |  |
| 12:00 | 17:00 | Tripped in hole to 1974m | Rig Repair |  |
| 17:00 | 17:30 | Picked up Kelly | Surveys | 1.00 |
| 17:30 | 18:00 | Circulated then dropped ball | Run Casing |  |
| 18:00 | 18:30 | Washed over Fish - ( lost cone ) | Rig Service | 0.50 |
| 18:30 | 22:00 | Tripped out | Test BOP’s |  |
| 22:00 | 24:00 | Made up New Bit and BHA | Drill Out Cement |  |
|  |  |  | Logging |  |
|  |  |  | W.O.C. |  |
|  |  |  | Cement Plug |  |
|  | JSA | Laying out the drilling jars | Wait on Cementer |  |
|  |  | Tripping out of hole | Made up fishing tools | 1.50 |
|  | 370 | Days Since Last LTA: |  |  |

| BIT INFORMATION | MUD PROPERTIES |
| --- | --- |
| Bit Number | 8 Run-12 | 13 Rerun-8 | Density (ppg) | 9.50 |
| Size (mm) | 156 | 156 | Viscosity (Sec) | 44 |
| Make | Reed | Reed | PV @ Degree C | 16 |
| Type | SL51HP | SL43HP | YP (lbs/100ft2) | 15 |
| IADC Code | 5-3-7 | 4-3-7 | API Filtrate (ml/30min) | 7.4 |
| Serial Number | HP5998 | JK4700 | Gels (lbs/100ft2) | 3 / 4 / 6 |
| Nozzles (x32) | 16-16-13 | 16-16-13 | Filter Cake (32nds inch) | 1/- |
| Depth In (m) | 1643 | 1898 | Sand (% Vol) | 0.20 / 0.20 |
| Depth Out (m) | 1898 | 1974 | Solids (% Vol) | 8.7 |
| Total Metres | 251 | 138 | Hardness (Ca mg/l) | 200 |
| Hours | 50.5 | 39 total 2 runs | KCl (% by wt) | 1.50 |
| WOB (kg) | 7000 | 8000 | Chlorides (Mg/l) | 9,400 |
| RPM | 100 | 90 | Methyl Blue (ppg eq) | 8.5 |
| Condition | 2-2-RG-G-E | Lost cone | Potassium (Mg/l) | 8,000 |
| Impact Force | 118lb/ft | 117lb/ft | Daily Cost ($) | 362 |
| Jet Velocity | 122 ft/sec | 122ft/sec | Cumulative Cost ($) | 46,761 |

LAKES OIL N.L.

DAILY DRILLING REPORT NO. 29                 PAGE: 2

| CEMENT DATA | LAST CASING | CHEMICALS USED |
| --- | --- | --- |
| Sacks |  | Size | 178 mm | Starlose |  |
| Class |  | Weight | 38.69 | Xanthum Gum XCD |  |
|  |  | Grade | N-80 | Defoamer |  |
|  |  | Connection | Buttress | Sodium sulphite | 1` |
|  |  | Joints | 92 | Potassium Chloride | 10 |
|  |  | Length | 1092.15m | AMC Biocide |  |
|  |  | Shoe | 1097.00 | Sodium Bicarbonate |  |
|  |  |  |  | Baracarb-20 | 3 |
|  |  |  |  | Barite | 20 |

| SURVEYS | PUMP No.1 | PUMP No.2 |
| --- | --- | --- |
| 7.00 deg at | 1282 m | Liner | 140mm | Liner |  |
| 8.00 deg at | 1346 m | Stroke | 16 inch | Stroke |  |
| 8.00 deg at | 1387 m | Pressure | 8970kpa | Pressure |  |
| 8.50 deg at | 1415 m | A.V. DP | 192 ft/min | A.V. DP |  |
| 8.50 deg at | 1452 m | A.V. DC | 281 ft/min | A.V. DC |  |
| 9.00 deg at | 1489m m | SPM | 40 | SPM |  |
| 9.50 deg at | 1575 m | GPM | 198 | GPM |  |
| 7.9 deg at | 1880 m |  |  |  |  |
| 8.00 deg at | 1956 m |  |  |  |  |

BHA: Bit-Bit sub- 2 x 4-3/4 Drill collars-Stabilizer-11 x 4-3/4 Drill collars-Jar-2 x 4-3/4 Drill collars

COMMENTS: Pulled bit because of slow drill rate and excessive torque which caused lost cone

REPORT BY: Lou De-Vattimo