LAKES OIL N.L.

DAILY DRILLING REPORT

| WELL: Boundary Crk-2 | REPORT No.: 31 | DATE: 09-11-05 |
| --- | --- | --- |
| DFS: 30 | 2400 DEPTH: 2041 | Last Depth: 1974 |
| 24hr Progress: 67m | PTD: 2500 | Total Fuel: 3,900 |
| Fuel Usage: 900 | Daily Cost: 27,887 | Cum Cost: 1,612,346 |
| 0600hrs Operation: Drilling 156mm hole at 2065m |
| Next 24hr Operation: Drill ahead with 156mm Bit |
| Site Personnel: Lakes 3-AMC 1-Higgins 2-Hunt 19 |

| HOURLY OPERATIONS SUMMARY (000-2400hrs) | OPERATIONS BREAKDOWN |
| --- | --- |
| FROM | TO | OPERATION |  |  |
| 00:00 | 03:00 | Tripped in hole to 1089m with Bit | Drilling | 17.50 |
| 03:300 | 03:30 | Slipped and cut Block line | Tripping | 5.50 |
| 03:30 | 06:00 | Tripped in hole to 1973m | Surveys |  |
| 06:00 | 06:30 | Circulated and washed to bottom 1974 | Reaming |  |
| 06:30 | 24:00 | Drilled 156mm hole 1974m to 2041m | Slip & Cut Block Line | 0.50 |
|  |  |  | Circulate & Clean Hole | 0.50 |
|  |  |  | Cement Casing |  |
|  |  |  | Rig Repair |  |
|  |  |  | Surveys |  |
|  |  | Changed out Drilling Jars | Run Casing |  |
|  |  |  | Rig Service |  |
|  |  |  | Test BOP’s |  |
|  |  |  | Drill Out Cement |  |
|  |  |  | Logging |  |
|  |  |  | W.O.C. |  |
|  |  |  | Cement Plug |  |
|  | JSA | New crew man inducted | Wait on Cementer |  |
|  |  | Using the fork lift stinger | Made up fishing tools |  |
|  | 371 | Days Since Last LTA: |  |  |

| BIT INFORMATION | MUD PROPERTIES |
| --- | --- |
| Bit Number |  | 14 Bit # 9 | Density (ppg) | 9.40 |
| Size (mm) |  | 156 | Viscosity (Sec) | 39 |
| Make |  | Reed | PV @ Degree C | 11 |
| Type |  | SL51HP | YP (lbs/100ft2) | 10 |
| IADC Code |  | 5-1-7 | API Filtrate (ml/30min) | 7.4 |
| Serial Number |  | HP5997 | Gels (lbs/100ft2) | 2 / 3 /3 |
| Nozzles (x32) |  | 13-14-16 | Filter Cake (32nds inch) | 1/- |
| Depth In (m) |  | 1974 | Sand (% Vol) | 0.20 / 0.30 |
| Depth Out (m) |  |  | Solids (% Vol) | 7.9 |
| Total Metres |  | 67 | Hardness (Ca mg/l) | 180 |
| Hours |  | 17.50 | KCl (% by wt) | 1.58 |
| WOB (kg) |  | 8000 | Chlorides (Mg/l) | 9,200 |
| RPM |  | 90 | Methyl Blue (ppg eq) | 8.5 |
| Condition |  | In hole | Potassium (Mg/l) | 8,400 |
| Impact Force |  | 116ft/lb | Daily Cost ($) | 1,010 |
| Jet Velocity |  | 127ft/sec | Cumulative Cost ($) | 47,771 |

LAKES OIL N.L.

DAILY DRILLING REPORT NO. 30                 PAGE: 2

| CEMENT DATA | LAST CASING | CHEMICALS USED |
| --- | --- | --- |
| Sacks |  | Size | 178 mm | Starlose | 2 |
| Class |  | Weight | 38.69 | Xanthum Gum XCD | 1 |
|  |  | Grade | N-80 | Defoamer | 1 |
|  |  | Connection | Buttress | Citric acid | 1` |
|  |  | Joints | 92 | Potassium Chloride | 10 |
|  |  | Length | 1092.15m | AMC Biocide | 1 |
|  |  | Shoe | 1097.00 | Cepac-R | 4 |
|  |  |  |  | Sodium Bicarbonate | 1 |
|  |  |  |  | Sodium Sulphite | 1 |

| SURVEYS | PUMP No.1 | PUMP No.2 |
| --- | --- | --- |
| 7.00 deg at | 1282 m | Liner | 140mm | Liner |  |
| 8.00 deg at | 1346 m | Stroke | 16 inch | Stroke |  |
| 8.00 deg at | 1387 m | Pressure | 8970kpa | Pressure |  |
| 8.50 deg at | 1415 m | A.V. DP | 192 ft/min | A.V. DP |  |
| 8.50 deg at | 1452 m | A.V. DC | 281 ft/min | A.V. DC |  |
| 9.00 deg at | 1489m m | SPM | 40 | SPM |  |
| 9.50 deg at | 1575 m | GPM | 198 | GPM |  |
| 7.9 deg at | 1880 m |  |  |  |  |
| 8.00 deg at | 1956 m |  |  |  |  |

BHA: Bit-Bit sub- 2 x 4-3/4 Drill collars-Stabilizer-11 x 4-3/4 Drill collars-Jar-2 x 4-3/4 Drill collars

COMMENTS: Drilling parameters suggest that no junk obstruction on bottom when drilling commenced

REPORT BY: Lou De-Vattimo