LAKES OIL N.L.

DAILY DRILLING REPORT

| WELL: Boundary Crk-2 | REPORT No.: 32 | DATE: 10-11-05 |
| --- | --- | --- |
| DFS: 31 | 2400 DEPTH: 2135 | Last Depth: 2041 |
| 24hr Progress: 94m | PTD: 2500 | Total Fuel: 11,300 |
| Fuel Usage: 2,600 | Daily Cost: 27,777 | Cum Cost: 1,640,163 |
| 0600hrs Operation: Drilling 156mm hole at 2154m |
| Next 24hr Operation: Drill ahead with 156mm Bit - Trip out for Bit change |
| Site Personnel: Lakes 3-AMC 1-Higgins 2-Hunt 17 |

| HOURLY OPERATIONS SUMMARY (000-2400hrs) | OPERATIONS BREAKDOWN |
| --- | --- |
| FROM | TO | OPERATION |  |  |
| 00:00 | 24:00 | Drilled 156mm hole 2041m to 2135m | Drilling | 24.00 |
|  |  |  | Tripping |  |
|  |  |  | Surveys |  |
|  |  |  | Reaming |  |
|  |  |  | Slip & Cut Block Line |  |
|  |  |  | Circulate & Clean Hole |  |
|  |  |  | Cement Casing |  |
|  |  |  | Rig Repair |  |
|  |  |  | Surveys |  |
|  |  |  | Run Casing |  |
|  |  |  | Rig Service |  |
|  |  |  | Test BOP’s |  |
|  |  |  | Drill Out Cement |  |
|  |  |  | Logging |  |
|  |  |  | W.O.C. |  |
|  |  |  | Cement Plug |  |
|  | JSA | Handling drill pipe bins | Wait on Cementer |  |
|  |  | Using the fork lift stinger | Made up fishing tools |  |
|  | 372 | Days Since Last LTA: |  |  |

| BIT INFORMATION | MUD PROPERTIES |
| --- | --- |
| Bit Number |  | 14 Bit # 9 | Density (ppg) | 9.50 |
| Size (mm) |  | 156 | Viscosity (Sec) | 43 |
| Make |  | Reed | PV @ Degree C | 18 |
| Type |  | SL51HP | YP (lbs/100ft2) | 10 |
| IADC Code |  | 5-1-7 | API Filtrate (ml/30min) | 7.0 |
| Serial Number |  | HP5997 | Gels (lbs/100ft2) | 2 / 4 / 6 |
| Nozzles (x32) |  | 13-14-16 | Filter Cake (32nds inch) | 1/- |
| Depth In (m) |  | 1974 | Sand (% Vol) | 0.15 / 0.40 |
| Depth Out (m) |  |  | Solids (% Vol) | 8.7 |
| Total Metres |  | 161 to date | Hardness (Ca mg/l) | 360 |
| Hours |  | 41.50 | KCl (% by wt) | 1.75 |
| WOB (kg) |  | 8000 | Chlorides (Mg/l) | 10,000 |
| RPM |  | 90 | Methyl Blue (ppg eq) | 8.5 |
| Condition |  | In hole | Potassium (Mg/l) | 9,300 |
| Impact Force |  | 116ft/lb | Daily Cost ($) | 895 |
| Jet Velocity |  | 127ft/sec | Cumulative Cost ($) | 48,666 |

LAKES OIL N.L.

DAILY DRILLING REPORT NO. 31                 PAGE: 2

| CEMENT DATA | LAST CASING | CHEMICALS USED |
| --- | --- | --- |
| Sacks |  | Size | 178 mm | Starlose | 4 |
| Class |  | Weight | 38.69 | Xanthum Gum XCD | 1 |
|  |  | Grade | N-80 | Defoamer |  |
|  |  | Connection | Buttress | Citric acid |  |
|  |  | Joints | 92 | Potassium Chloride | 6 |
|  |  | Length | 1092.15m | AMC Biocide | 1 |
|  |  | Shoe | 1097.00 | Cepac-R | 6 |
|  |  |  |  | Sodium Bicarbonate | 3 |
|  |  |  |  | Sodium Sulphite | 1 |

| SURVEYS | PUMP No.1 | PUMP No.2 |
| --- | --- | --- |
| 7.00 deg at | 1282 m | Liner | 140mm | Liner |  |
| 8.00 deg at | 1346 m | Stroke | 16 inch | Stroke |  |
| 8.00 deg at | 1387 m | Pressure | 8970kpa | Pressure |  |
| 8.50 deg at | 1415 m | A.V. DP | 192 ft/min | A.V. DP |  |
| 8.50 deg at | 1452 m | A.V. DC | 281 ft/min | A.V. DC |  |
| 9.00 deg at | 1489m m | SPM | 40 | SPM |  |
| 9.50 deg at | 1575 m | GPM | 198 | GPM |  |
| 7.9 deg at | 1880 m |  |  |  |  |
| 8.00 deg at | 1956 m |  |  |  |  |

BHA: Bit-Bit sub- 2 x 4-3/4 Drill collars-Stabilizer-11 x 4-3/4 Drill collars-Jar-2 x 4-3/4 Drill collars

COMMENTS:

REPORT BY: Lou De-Vattimo