LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Boundary creek-2 | REPORT No. : | 5 | DFS: | 4 | DATE : | 14-Oct-05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 261m | LAST DEPTH : | 132m | 24 HR PROGRESS : | 149m | PTD : | 2500m |
| TOTAL FUEL : | 10,700 | FUEL USAGE : | 1000 |  |  | CUM. COST : $ |  |
| 0600 OPS : | Make up the Casing bowl to Casing |
| Next 24 hr OPS: | Install and test the Blowout preventors then make up the 216mm drilling assembly |
| Site Personnel: | Lakes 3- A.M.C 1- Mud logger 2- Hunt Energy 20 |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 1 Re-Run |  |  | Drilling | 9.50 |  | Density | Spud mud | ppg |
| Size (mm) | 311 |  |  | Tripping | 2.50 |  | Viscosity |  | Sec |
| Make | BBL |  |  | Surveys |  |  | PV @ Deg C |  | Deg C |
| Type | M-22 |  |  | Reaming |  |  | YP lbs/100 ft 2 |  | Lbs/100ft |
| IADC Code | 1-1-7 |  |  | Slip and cut block line |  |  | API Filtrate |  | m/30min |
| Serial Number | 6093062 |  |  | Circulate and clean hole | 1.00 |  | Gels lbs/100 ft 2 |  |  |
| Nozzles (32) | 18-18-18 |  |  | Cement casing | 1.50 |  | Cake 32nds/ in |  |  |
| Depth in (m) | 15.00 |  |  | Rig repair |  |  | Sand |  | % Vol |
| Depth out (m) | 261m |  |  | Surveys | 1.00 |  | Solids |  | % Vol |
| Total Metres | 246m |  |  | Run Casing | 6.00 |  | Hardness Ca mg/l |  |  |
| Hours | 16.5 |  |  | Rig Service |  |  | KCL Concentration |  | % by wt |
| WOB (kg) | 1000 |  |  | Make up conductor pipe |  |  | Chlorides |  | Mg/l |
| RPM | 80 |  |  | Drill out Cmt |  |  | Methyl Blue |  | Ppb equiv |
| Condition | 4-4-NO-A-2-2-2-1-0 |  |  | Logging |  |  | K+ |  | Mg/l |
| Impact Force | lb/ft |  |  | W.0.C | 2.50 |  | Daily Cost $ | 306 |
| Jet Velocity | ft/sec |  |  | Cement plug |  |  | Cum Cost $ | 5,845 |
| B.H.A.: | Bit- Bit sub- 2 X 8inch drill collars- crossover sub – 8 x 6-1/2 inch drill collars |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 0.25 | ° at | 218m | m |  | Type | Amount |
| 00:00 | 09:30 | Drilled 311mm hole from 132m to 261m |  |  | ° at |  | m |  | Ausgel | 30 |
| 09:30 | 10:30 | Circulated hole clean |  |  | ° at |  | m |  |  |  |
| 10;30 | 11:30 | Wiper tripped and ran survey |  |  | ° at |  | m |  |  |  |
| 11:30 | 14:00 | Tripped out for casing , layed out 2 eight inch collars |  |  | ° at |  | m |  |  |  |
| 14:00 | 19:00 | Ran 21 jnts of 244mm casing |  |  | ° at |  | m |  |  |  |
| 19:00 | 20:00 | Rigged up Halliburton then circulated |  |  | ° at |  | m |  |  |  |
| 20:00 | 21:30 | Held meeting then cemented the Casing |  |  | ° at |  | m |  |  |  |
| 21:30 | 24:00 | Wait on cement |  |  |  |  |
|  |  |  |  | PUMP 1 |  | PUMP 2 |
|  |  | Hook load with casing 29,000lbs |  | Liner | 140 | mm |  | Liner | 140 | mm |
|  |  | Displaced cement with water |  | Pressure | 1000 | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP |  | m/min |  | A.V. DP |  | m/min |
|  |  |  |  | A.V. DC |  | m/min |  | A.V. DC |  | m/min |
|  |  |  |  | SPM | 50 |  | SPM |  |
|  |  |  |  | GPM | 250 |  | GPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks | 40 |  | Size | 244mm |  |
|  |  |  |  | Class |  |  | Weight | 53.57 | Kg/m |
|  |  |  |  |  |  |  |  | Grade | K-55 |  |
|  |  |  |  |  |  |  |  | Connection | Buttress |  |
|  | JSA | Mousehole connections |  |  |  |  |  | Joints | 21 |  |
|  |  | Running casing |  |  |  |  |  | Length | 253 | m |
| Days since | LTA | 346 |  |  |  |  | Shoe | 258 | m |

,66