LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Boundary creek-2 | REPORT No. : | 8 | DFS: | 7 | DATE : | 17-Oct-05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 743m | LAST DEPTH : | 509m | 24 HR PROGRESS : | 234m | PTD : | 2500m |
| TOTAL FUEL : | 10,300 | FUEL USAGE : | 1800 |  | 37,055 | CUM. COST : $ | 489,819 |
| 0600 OPS : | Drilling 216mm hole at 788 m |
| Next 24 hr OPS: | Drill to 800m– Survey -Wiper trip to 600m-Continue drilling to 1100m |
| Site Personnel: | Lakes 4- A.M.C 1- Mud logger 2- Hunt Energy 21- Atlas loggers 3 |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 2 Re run |  |  | Drilling | 21.50 |  | Density | 9.15 | ppg |
| Size (mm) | 216mm |  |  | Tripping | 2.00 |  | Viscosity | 37 | Sec |
| Make | Reed |  |  | Surveys |  |  | PV @ Deg C | 9 | Deg C |
| Type | ETH 11 |  |  | Reaming |  |  | YP lbs/100 ft 2 | 8 | Lbs/100ft |
| IADC Code | 1-1-7 |  |  | Slip and cut block line |  |  | API Filtrate | 6.2 | m/30min |
| Serial Number | MX-8867 |  |  | Circulate and clean hole | 0.50 |  | Gels lbs/100 ft 2 | 1/2/2 |  |
| Nozzles (32) | 13-13-13 |  |  | Cement casing |  |  | Cake 32nds/ in | <1 |  |
| Depth in (m) | 261 |  |  | Rig repair |  |  | Sand | 0.75 / 0 .15 | % Vol |
| Depth out (m) |  |  |  | Surveys |  |  | Solids | 6.6 | % Vol |
| Total Metres | 482 |  |  | Run Casing |  |  | Hardness Ca mg/l | 700 |  |
| Hours | 38 |  |  | Rig Service |  |  | KCL Concentration | 2.08 | % by wt |
| WOB (kg) | 6000 |  |  | Test BOP |  |  | Chlorides | 11,000 | Mg/l |
| RPM | 90 |  |  | Drill out Cmt |  |  | Methyl Blue | 10.00 | Ppb equiv |
| Condition |  |  |  | Logging |  |  | K+ | 11,100 | Mg/l |
| Impact Force | 418 |  |  | W.0.C |  |  | Daily Cost $ | 4,298 |
| Jet Velocity | 270 |  |  | Cement plug |  |  | Cum Cost $ | 15,344 |
| B.H.A.: | Bit- Bit sub- 2 x 6-1/4inch drill collars- stabilizer -6 x 6-1/4inch drill collars -4 x Hevi-Wate drillpipe |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 0.25 | ° at | 218m | m |  | Type | Amount |
| 00:00 | 08:30 | Drilled 216mm hole from 509m to 600m |  | 1.50 | ° at | 600m | m |  | Starlose / Barite | 7 / 10 |
| 08:30 | 09:00 | Circulated and ran survey at 600m |  |  | ° at |  | m |  | AMC Defoamer | 7 |
| 09:00 | 10:00 | Wiper tripped to shoe at 261m |  |  | ° at |  | m |  | AMC PAC-R | 5 |
| 10:00 | 11:00 | Tripped back to bottom - hole good |  |  | ° at |  | m |  | Sodium Sulphite | 2 |
| 11:00 | 24:00 | Drilled 216mm hole from 600m to 609m |  |  | ° at |  | m |  | Potassium chloride | 42 |
|  |  |  |  |  | ° at |  | m |  | Calcium Chloride | 11 |
|  |  |  |  |  | ° at |  | m |  | Biocide / XCD | 1 / 3 |
|  |  |  |  | PUMP 1 |  | PUMP 2 |
|  |  |  |  | Liner | 140 | mm |  | Liner | 140 | mm |
|  |  |  |  | Pressure | 7,700 | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP | 154 | m/min |  | A.V. DP |  | m/min |
|  |  |  |  | A.V. DC | 241 | m/min |  | A.V. DC |  | m/min |
|  |  |  |  | SPM | 66 |  | SPM |  |
|  |  | One load of 3-1/2inch drill pipe arrived from Perth |  | GPM | 327 |  | GPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks |  |  | Size | 244mm |  |
|  |  |  |  | Class |  |  | Weight | 53.57 | Kg/m |
|  |  |  |  |  |  |  |  | Grade | K-55 |  |
|  |  |  |  |  |  |  |  | Connection | Buttress |  |
|  | JSA | Make up the drill string-making connections |  |  |  |  |  | Joints | 21 |  |
|  |  |  |  |  |  |  |  | Length | 253 | m |
| Days since | LTA | 349 |  |  |  |  | Shoe | 258 | m |

,66