LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Boundary creek-2 | REPORT No. : | 15 | DFS: | 14 | DATE : | 24 Oct-05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 1100m | LAST DEPTH : | 1100m | 24 HR PROGRESS : | 0m | PTD : | 2500m |
| TOTAL FUEL : | 7,600 | FUEL USAGE : | 1,000 |  | 177,232 | CUM. COST : $ | 1,085,231 |
| 0600 OPS : | Nil operation from 02:30 hrs until 08:00 hrs crew change |
| Next 24 hr OPS: | Continue picking up drill pipe and tripping in hole with 156mm drilling assembly |
| Site Personnel: | Lakes 3 A.M.C 1- Mud logger 2- Hunt Energy 18 |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 6 |  |  | Drilling |  |  | Density | 9.55 | ppg |
| Size (mm) | 156 |  |  | Tripping | 4.00 |  | Viscosity | 44 | Sec |
| Make | Reed |  |  | Surveys |  |  | PV @ Deg C | 14 | Deg C |
| Type | SL43HP |  |  | Reaming |  |  | YP lbs/100 ft 2 | 7 | Lbs/100ft |
| IADC Code | 4-3-7 |  |  | Slip and cut block line |  |  | API Filtrate |  | m/30min |
| Serial Number | JK 4699 |  |  | Circulate and clean hole |  |  | Gels lbs/100 ft 2 |  |  |
| Nozzles (32) | 13-14-16 |  |  | Cement casing |  |  | Cake 32nds/ in | 1/- |  |
| Depth in (m) | 1100 |  |  | Rig repair |  |  | Sand | 0.15 | % Vol |
| Depth out (m) |  |  |  | Surveys |  |  | Solids | 0.1 | % Vol |
| Total Metres |  |  |  | Run Casing |  |  | Hardness Ca mg/l | 9.1 |  |
| Hours |  |  |  | Rig Service |  |  | KCL Concentration | 1.25 | % by wt |
| WOB (kg) |  |  |  | Test BOP | 6.00 |  | Chlorides | 9,000 | Mg/l |
| RPM |  |  |  | Drill out Cmt |  |  | Methyl Blue | 10.8 | Ppb equiv |
| Condition |  |  |  | Logging |  |  | K+ | 6,600 | Mg/l |
| Impact Force |  |  |  | W.0.C |  |  | Daily Cost $ | 0 |
| Jet Velocity |  |  |  | Install BOP | 14.00 |  | Cum Cost $ | 25,654 |
| B.H.A.: | Bit- Near bit stab- 2 x 4-3/4inch drill collars- stabilizer -12 x 4-3/4inch drill collars-Jars-2 x 4-3/4 inch drill collars -4 x Hevi-Wate drillpipe |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 0.25 | ° at | 218m | m |  | Type | Amount |
| 00:00 |  | Completed installation of wellhead equipment and |  | 1.50 | ° at | 600m | m |  | Defoamer / Biocide |  |
|  |  | B.O.P – changed out the pipe rams to 3-1/2inch and |  | 2.00 | ° at | 797m | m |  |  |  |
|  | 13:00 | Function tested the BOP lines |  | 2.50 | ° at | 938m | m |  | AMC PAC-L / R |  |
| 13:00 | 14:00 | Energized the “ X “ bushing with 14,000kpa |  | 3.00 | ° at | 1096m | m |  | Starlose |  |
| 14:00 | 20:00 | Tested the BOP and choke manifold |  |  | ° at |  | m |  | Potassium chloride |  |
| 20:00 |  | Made up 156mm bit and picking up the drilling |  |  | ° at |  | m |  | Soium Bicarbonate |  |
|  | 24:00 | assembly - bit at 338m |  |  | ° at |  | m |  | Sodium sulphite |  |
|  |  |  |  | PUMP 1 |  | PUMP 2 |
|  |  |  |  | Liner | 140 | mm |  | Liner | 140 | mm |
|  |  |  |  | Pressure |  | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP |  | m/min |  | A.V. DP |  | m/min |
|  |  |  |  | A.V. DC |  | m/min |  | A.V. DC |  | m/min |
|  |  | Atlas loggers departed 23-10-05 |  | SPM |  |  | SPM |  |
|  |  | One atlas logger on site |  | GPM |  |  | GPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks |  |  | Size | 178mm |  |
|  |  |  |  | Class |  |  | Weight | 38.69 | Kg/m |
|  |  |  |  |  |  |  |  | Grade | N-80 |  |
|  |  |  |  |  |  |  |  | Connection | Buttress |  |
|  | JSA | Hazards around confined space areas / Pressure tsests |  |  |  |  |  | Joints | 92 |  |
|  |  |  |  |  |  |  |  | Length |  | m |
| Days since | LTA | 356 |  |  |  |  | Shoe | 1097 | m |

,66