|  | LAKES OIL N.L. (A.C.N. 004 247 214) | Registered Office: Level 11, 500 Collins Street, Melbourne, Vic. 3000 | P.O. Box 300, Collins St. West Melbourne, Vic. 8007 Phone: (03) 9629 1566 Fax: (03) 9629 1624 |
| --- | --- | --- | --- |

# Boundary Creek-2 Wellsite

# via Longford

October 20th 2005

# Boundary Creek-2 Daily Report # 10 – October 20th 2005

24 Hour Progress

At 6am this morning the contractor was drilling ahead in 216mm hole at a depth of 992m having drilled 81m during the past 24 hours. A survey was run at 947m showing the deviation of the hole was 2.5º and bit#2 was then tripped from the hole and replaced with bit#3 due to decreasing drill rate. Bit#3 was then tripped into the hole to 947m and drilling recommenced. The formation is predominantly sandstone (80%) with increasing clay content over the last 70m with some coals present associated with slightly increased gas levels (1-2 units). Background gas has ranged from trace-1 unit and no oil fluorescence has been observed during the past 24 hours.

Next 24 Hours

Continue drilling 216mm hole to the intermediate casing point at approximately 1100m.

Tim O’Brien

Lakes Oil