WELL NAME: CRC No.1 PERMIT: PPL 13 DAILY GEOLOGICAL REPORT No. 10 DATE: 24/02/2007

Depth: 1247m Progress: 2m Days from Spud: 10

Rig: Century Rig No.11 GL(AHD): 44.8m Drilling Rep: Kevin Murphy/Brian Assels RT: (datum) 50.0m Geologist: David Horner Last Casing: 194mm at 512m

0600 hrs Update: Core ahead at 1257m. Current lithology (Interpreted from drill rate: Claystone 60% grading to, interbedded and laminated with Sandstone 40%), background gas 0.001-0.003%.

Comments: Make up and RIH with coring assembly, Cut Core No.2 1245.0-1246.0m (cut 1.0m), POOH due to low coring rate and high pump pressure, no recovery, service core barrel, RIH for Core No.3. Cut Core No3 from 1246.0m to 1247m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1245-1247 | Paaratte Formation - No Show | TG 0.001-0.002% C1 100% C2+ 0 |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Port Campbell Limestone Gellibrand Marl Clifton Formation Narrawaturk Marl Mepunga Formation Dilwyn Formation Pember Mudstone Pebble Point Formation | 5.2 125 462 476 550 635 879 936 | 5.2 122 457 474 551 633 878 939 | 44.8 -72 -407 -424 -501 -583 -828 -889 | 0 3 High 5 High 2 High 1 Low 2 High 1 High 3 Low |
| Massacre Shale | 995 | 1002 | -952 | 7 Low |
| Timboon Sandstone | 1016 | 1022 | -972 | 6 Low |
| Paaratte Formation | 1129 | 1128 | -1078 | 1 High |
| Skull Creek Formation | 1521 |  |  |  |
| Nullawarre Formation | 1712 |  |  |  |
| Belfast Mudstone | 1715 |  |  |  |
| Flaxmans Formation | 2026 |  |  |  |
| Waarre Formation Unit "C" | 2045 |  |  |  |
| Waarre Formation Unit "B" | 2075 |  |  |  |
| Waarre Formation Unit "A" | 2091 |  |  |  |
| Eumeralla Formation | 2131 |  |  |  |
| Total Depth | 2250 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1245-1247 | PAARATTE FORMATION Massive Claystone (100%). CLAYSTONE: medium to dark grey to medium to dark brown grey to dark green grey, moderately to very silty, often very fine to finely arenaceous, trace fine black coaly detritus, trace pyrite, trace micromica, soft, non fissile. |