WELL NAME: CRC No.1 PERMIT: PPL 13 DAILY GEOLOGICAL REPORT No. 12 DATE: 26/02/2007

Depth: 1526m Progress: 203m Days from Spud: 12

Rig: Century Rig No.11 GL(AHD): 44.8m Drilling Rep: Kevin Murphy/Brian Assels RT: (datum) 50.0m Geologist: David Horner Last Casing: 194mm at 512m

0600 hrs Update: Drill ahead with 171mm hole at 1586m. Top of Skull Creek Formation at 1528m (7m Low). Current Lithology Skull Creek Claystone (100%), background gas 0.003% (C1 100%).

Comments: Drill ahead with 171mm hole to 1526m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1323-1503 | Paaratte Formation - No Show | TG 0.001-0.003% C1 100% C2 Trace C3+ 0 |
| 1503-1507 | Paaratte Formation - Oil Show From 1503-1507m the sandstone has 20% moderately bright patchy very pale yellow white fluorescence giving a weak milky white crush cut, thin ring residue. No gas or drill rate increase was noted across this interval. The cutting samples are very poor quality due to disaggregation by the drilling action of the PDC drill bit and subsequent encapsulation by the PHPA in the mud system. The best assessment is for this to be a light gravity mobile crude oil contained within tight very fine grained feldspathic sand lenses with insufficient porosity/permeability for economic oil recovery. Attention however should be paid to this interval during electric log evaluation. | TG 0.001-0.002% C1 100% C2+ 0 |
| 1507-1528 | Paaratte Formation - No Show | TG 0.001-0.002% C1 100% C2+ 0 |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Port Campbell Limestone Gellibrand Marl Clifton Formation Narrawaturk Marl Mepunga Formation Dilwyn Formation Pember Mudstone Pebble Point Formation | 5.2 125 462 476 550 635 879 936 | 5.2 122 457 474 551 633 878 939 | 44.8 -72 -407 -424 -501 -583 -828 -889 | 0 3 High 5 High 2 High 1 Low 2 High 1 High 3 Low |
| Massacre Shale | 995 | 1002 | -952 | 7 Low |
| Timboon Sandstone | 1016 | 1022 | -972 | 6 Low |
| Paaratte Formation | 1129 | 1128 | -1078 | 1 High |
| Skull Creek Formation | 1521 | 1528 | -1478 | 7 Low |
| Nullawarre Formation | 1712 |  |  |  |
| Belfast Mudstone | 1715 |  |  |  |
| Flaxmans Formation | 2026 |  |  |  |
| Waarre Formation Unit "C" | 2045 |  |  |  |
| Waarre Formation Unit "B" | 2075 |  |  |  |
| Waarre Formation Unit "A" | 2091 |  |  |  |
| Eumeralla Formation | 2131 |  |  |  |
| Total Depth | 2250 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1323-1450 | PAARATTE FORMATION Claystone (50%) interbedded with and grading to Sandstone (50%). CLAYSTONE: light to dark grey to medium to dark brown grey, moderately to very silty, often very finely to finely arenaceous, trace to abundant dispersed medium to pebble sized quartz grains, trace black coaly detritus, trace pyrite, trace micromica, firm, non fissile. SANDSTONE: off white to medium grey, very fine to pebble quartz grains, dominantly very fine, occasionally dominantly very coarse, angular to rounded, very poorly sorted, weak silica cement, abundant off white to medium grey argillaceous and silt matrix, clear to opaque quartz grains, trace black coaly detritus, trace biotite flakes. trace pyrite, friable, very poor to occasionally good inferred porosity, no oil fluorescence. |
| 1450-1528 | PAARATTE FORMATION Claystone (70%) interbedded with and grading to Sandstone (30%). CLAYSTONE: light to dark grey to medium brown grey, moderately to very silty, often very finely arenaceous, rare medium to pebble rounded quartz grains, trace black coaly detritus, trace pyrite, trace micromica, firm, non fissile. SANDSTONE: off white to medium grey, very fine to rarely fine, trace dispersed medium to very coarse quartz grains, angular to rounded, poorly sorted, weak silica cement, abundant off white argillaceous matrix, clear to opaque quartz grains, abundant altered feldspar grains, trace black coaly detritus, friable, very poor inferred porosity. FLUORESCENCE: from 1503-1507m the sandstone has 20% moderately bright patchy very pale yellow white fluorescence giving a weak milky white crush cut, thin ring residue. |