WELL NAME: CRC No.1 PERMIT: PPL 13 DAILY GEOLOGICAL REPORT No. 18 DATE: 04/03/2007

Depth: 2033m Progress: 129m Days from Spud: 18

Rig: Century Rig No.11 GL(AHD): 44.8m Drilling Rep: Kevin Murphy/Brian Assels RT: (datum) 50.0m Geologist: David Horner Last Casing: 194mm at 512m

0600 hrs Update: RIH with 60ft core barrel for Core No.5.

Comments: RIH, trip gas 0.14%, drill ahead with 171mm hole to 2033m, circulate sample, survey 0.75 degrees at 86 degress AZ., POOH for Core No.5.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1904-2020 | Belfast Mudstone - No Show | TG 0.05-0.19% C1 92% C2 7% C3 1% C4+ 0 |
| 2020-2033 | Flaxmans Formation - No Show | TG 0.05-0.10% C1 89.5% C2 7% C3 3% C4 0.5% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Port Campbell Limestone Gellibrand Marl Clifton Formation Narrawaturk Marl Mepunga Formation Dilwyn Formation Pember Mudstone Pebble Point Formation | 5.2 125 462 476 550 635 879 936 | 5.2 122 457 474 551 633 878 939 | 44.8 -72 -407 -424 -501 -583 -828 -889 | 0 3 High 5 High 2 High 1 Low 2 High 1 High 3 Low |
| Massacre Shale | 995 | 1002 | -952 | 7 Low |
| Timboon Sandstone | 1016 | 1022 | -972 | 6 Low |
| Paaratte Formation | 1129 | 1128 | -1078 | 1 High |
| Skull Creek Formation | 1521 | 1528 | -1478 | 7 Low |
| Nullawarre Formation | 1712 | n/p | n/p | n/p |
| Belfast Mudstone | 1715 | 1728 | -1678 | 13 Low |
| Flaxmans Formation | 2026 | 2020 | -1970 | 6 High |
| Waarre Formation Unit "C" | 2045 |  |  |  |
| Waarre Formation Unit "B" | 2075 |  |  |  |
| Waarre Formation Unit "A" | 2091 |  |  |  |
| Eumeralla Formation | 2131 |  |  |  |
| Total Depth | 2250 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1904-2020 | BELFAST MUDSTONE Massive Claystone (100%). CLAYSTONE: dark grey, slightly silty, moderately carbonaceous, common to abundant dark green glauconite, rare Inoceramus in part, trace to rarely common pyrite, trace to common mediumbrown cryptocrystalline dolomite, rare calcite, common micromica, moderately hard, slightly subfissile. |
| 2020-2033 | FLAXMANS FORMATION Claystone (100%). CLAYSTONE: medium grey to medium to dark brown grey to medium brown, moderately silty, nil to rarely abundant very fine altered feldspar and quartz grains, trace glauconite, slightly calcareous in part, trace pyrite, trace micromica, moderately hard, slightly subfissile. |