WELL NAME: CRC No.1 PERMIT: PPL 13 DAILY GEOLOGICAL REPORT No. 1 DATE: 15/02/2007

Depth: 216m Progress: 216m Days from Spud: 1

Rig: Century Rig No.11 GL(AHD): 44.8m Drilling Rep: Kevin Murphy/Brian Assels RT: (datum) 50.0m Geologist: David Horner Last Casing: 406 at 15.2m

0600 hrs Update: Drill ahead with 251mm hole to 312m. Current lithology 100% MARL: medium green grey to rarely medium brown grey, occasionally medium to dark grey, abundant fossil fragments including bryozoa, forams, bivalves, gastropods, sponge spicules and echinoid spines, very soft, sticky, non fissile, background gas 0.001-0.003% (C1 100%).

Comments: Spud CRC No.1 at 1100hrs on 15th February 2007, drill ahead with 251mm hole to 216m. Survey at 131m = 0.25 degrees.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 15.2-122 | Port Campbell Limestone - No Show | TG 0.001-0.002% C1 100% C2+ 0 |
| 122-216 | Gellibrand Marl - No Show | TG 0.001-0.003% C1 100% C2+ 0 |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Port Campbell Limestone Gellibrand Marl Clifton Formation Narrawaturk Marl Mepunga Formation Dilwyn Formation Pember Mudstone Pebble Point Formation | 5.2 125 462 476 550 635 884 946 | 5.2 122 | 44.8 -72 | 0 3 High |
| Massacre Shale | 1004 |  |  |  |
| Timboon Sandstone | 1026 |  |  |  |
| Paaratte Formation | 1139 |  |  |  |
| Skull Creek Formation | 1551 |  |  |  |
| Nullawarre Formation | 1732 |  |  |  |
| Belfast Mudstone | 1740 |  |  |  |
| Flaxmans Formation | 2026 |  |  |  |
| Waarre Formation Unit "C" | 2045 |  |  |  |
| Waarre Formation Unit "B" | 2075 |  |  |  |
| Waarre Formation Unit "A" | 2091 |  |  |  |
| Eumeralla Formation | 2131 |  |  |  |
| Total Depth | 2250 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 15.2-122 | PORT CAMPBELL LIMESTONE Massive Calcarenite (100%). CALCARENITE: light grey, yellow orange at top, very fine to medium, dominantly fine grained, abundant fossil fragments including bryozoa, echinoid spines, sponge spicules, gastropods, bivalves and forams - occasionally infilled with glauconite, trace black lithics, trace glauconite, rare medium grey marl, moderate calcareous cement, poor visual porosity, friable to moderately hard, grading with depth to: CALCARENITE: light grey, very fine to fine, dominantly very fine, slightly to moderately argillaceous, trace fossil fragments including bryozoa, echinoid spines, sponge spicules, gastropods, bivalves and forams, trace black lithics, trace glauconite, trace medium grey marl, moderate calcareous cement, poor visual porosity, friable to moderately hard. |
| 122-216 | GELLIBRAND MARL Massive Marl (100%). MARL: medium green grey to medium brown grey, occasionally medium to dark grey, abundant fossil fragments including bryozoa, forams, bivalves, gastropods, sponge spicules and echinoid spines, rare glauconite, rare pyrite, rare black coaly detritus, very soft, sticky, non fissile. |