WELL NAME: CRC No.1 PERMIT: PPL 13 DAILY GEOLOGICAL REPORT No. 20 DATE: 06/03/2007

Depth: 2051m Progress: 13m Days from Spud: 20

Rig: Century Rig No.11 GL(AHD): 44.8m Drilling Rep: Kevin Murphy/Brian Assels RT: (datum) 50.0m Geologist: David Horner Last Casing: 194mm at 512m

0600 hrs Update: POOH, recover Core No.5, cut 2033.0-2051.0m (18.0m), recovered 2044.41-2051.00m (6.59m), 37% recovery. (Core sections missing from top, middle and bottom). Make up 80ft core barrel, RIH for Core No.6.

Comments: Cut Core No.5, 2033.0-2051.0m, cut 18.0m, POOH.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 2038-2050 | Flaxmans Formation - Gas Show The sandstones within the Flaxmans Formation appear to be gas saturated. However, due to the abundance of white kaolin matrix visually appear to have insufficient porosity/permeability for significant gas flow rates. | TG 0.02-0.22% C1 91% C2 6% C3 2% C4 1% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Port Campbell Limestone Gellibrand Marl Clifton Formation Narrawaturk Marl Mepunga Formation Dilwyn Formation Pember Mudstone Pebble Point Formation | 5.2 125 462 476 550 635 879 936 | 5.2 122 457 474 551 633 878 939 | 44.8 -72 -407 -424 -501 -583 -828 -889 | 0 3 High 5 High 2 High 1 Low 2 High 1 High 3 Low |
| Massacre Shale | 995 | 1002 | -952 | 7 Low |
| Timboon Sandstone | 1016 | 1022 | -972 | 6 Low |
| Paaratte Formation | 1129 | 1128 | -1078 | 1 High |
| Skull Creek Formation | 1521 | 1528 | -1478 | 7 Low |
| Nullawarre Formation | 1712 | n/p | n/p | n/p |
| Belfast Mudstone | 1715 | 1728 | -1678 | 13 Low |
| Flaxmans Formation | 2026 | 2020 | -1970 | 6 High |
| Waarre Formation Unit "C" | 2045 |  |  |  |
| Waarre Formation Unit "B" | 2075 |  |  |  |
| Waarre Formation Unit "A" | 2091 |  |  |  |
| Eumeralla Formation | 2131 |  |  |  |
| Total Depth | 2250 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 2038-2050 | FLAXMANS FORMATION Claystone (80%) with interbedded Sandstone (20%). CLAYSTONE: light to dark grey to medium to dark brown grey to occasionally medium brown, moderately silty, abundant very fine altered feldspar and quartz grains in part, trace glauconite, slightly calcareous in part, trace pyrite, trace micromica, moderately hard, slightly subfissile. SANDSTONE: off white, very fine to fine, trace to common medium to very coarse grains, dominantly very fine, subangular to surounded, moderately sorted, weak silica cement, abundant white argillaceous matrix, quartzose with abundant altered feldspar grains, trace black carbonaceous specks, friable, poor visual porosity, no oil fluorescence. |