WELL NAME: CRC No.1 PERMIT: PPL 13 DAILY GEOLOGICAL REPORT No. 25 DATE: 11/03/2007

Depth: 2249m Progress: 0m Days from Spud: 25

Rig: Century Rig No.11 GL(AHD): 44.8m Drilling Rep: Kevin Murphy/Roy Dunne RT: (datum) 50.0m Geologist: David Horner Last Casing: 194mm at 512m

0600 hrs Update: Continue to run Schlumber logs: Run#5 CMR-ECS.

Comments: Continue to run Schlumber Logs: Run#4 MDT (samples), Run#5 CMR-ECS.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
|  | No new formation drilled. |  |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Port Campbell Limestone Gellibrand Marl Clifton Formation Narrawaturk Marl Mepunga Formation Dilwyn Formation Pember Mudstone Pebble Point Formation | 5.2 125 462 476 550 635 879 936 | 5.2 122 457 474 551 633 878 939 | 44.8 -72 -407 -424 -501 -583 -828 -889 | 0 3 High 5 High 2 High 1 Low 2 High 1 High 3 Low |
| Massacre Shale | 995 | 1002 | -952 | 7 Low |
| Timboon Sandstone | 1016 | 1022 | -972 | 6 Low |
| Paaratte Formation | 1129 | 1128 | -1078 | 1 High |
| Skull Creek Formation | 1521 | 1528 | -1478 | 7 Low |
| Nullawarre Formation | 1712 | n/p | n/p | n/p |
| Belfast Mudstone | 1715 | 1728 | -1678 | 13 Low |
| Flaxmans Formation | 2026 | 2020 | -1970 | 6 High |
| Waarre Formation Unit "C" | 2045 | 2053.5 | -2003.5 | 8.5 Low |
| Waarre Formation Unit "B" | 2075 | 2084 | -2034 | 9 Low |
| Waarre Formation Unit "A" | 2091 | 2103 | -2053 | 12 Low |
| Eumeralla Formation | 2131 | 2140 | -2090 | 9 Low |
| Total Depth | 2250 | 2249 | -2199 | 1 High |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
|  | No new formation drilled. |