WELL NAME: CRC No.1 PERMIT: PPL 13 DAILY GEOLOGICAL REPORT No. 22 DATE: 08/03/2007

Depth: 2249m Progress: 173.5m Days from Spud: 22

Rig: Century Rig No.11 GL(AHD): 44.8m Drilling Rep: Kevin Murphy/Brian Assels RT: (datum) 50.0m Geologist: David Horner Last Casing: 194mm at 512m

0600 hrs Update: Work tight hole.

Comments: RIH with 4 blade PDC bit, drill ahead with 171mm hole to 2249m, POOH to log.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 2075.5-2084 | Waarre Formation Unit "C" - No Show | TG 0.02-0.43% C1 90% C2 6% C3 3% C4 1% C5 trace |
| 2084-2103 | Waarre Formation Unit "B" - No Show | TG 0.02-0.12% C1 90% C2 7% C3 2% C4 1% |
| 2103-2140 | Waarre Formation Unit "A" - Gas Show The Waarre sandstones appear to have some gas saturation but from cutting samples appear to have insufficient porosity/permeability to achieve significant gas flow rates. | TG 0.05-0.46% C1 92% C2 5% C3 2% C4 1% C5 trace |
| 2140-2249 | Eumeralla Formation - Gas Shows The Eumeralla appears to contain some gas saturation, however this has very limited porosity/permeabilty - too low for significant flow rates. | TG 0.01-0.24% C1 95% C2 4% C3 1% C4 trace |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Port Campbell Limestone Gellibrand Marl Clifton Formation Narrawaturk Marl Mepunga Formation Dilwyn Formation Pember Mudstone Pebble Point Formation | 5.2 125 462 476 550 635 879 936 | 5.2 122 457 474 551 633 878 939 | 44.8 -72 -407 -424 -501 -583 -828 -889 | 0 3 High 5 High 2 High 1 Low 2 High 1 High 3 Low |
| Massacre Shale | 995 | 1002 | -952 | 7 Low |
| Timboon Sandstone | 1016 | 1022 | -972 | 6 Low |
| Paaratte Formation | 1129 | 1128 | -1078 | 1 High |
| Skull Creek Formation | 1521 | 1528 | -1478 | 7 Low |
| Nullawarre Formation | 1712 | n/p | n/p | n/p |
| Belfast Mudstone | 1715 | 1728 | -1678 | 13 Low |
| Flaxmans Formation | 2026 | 2020 | -1970 | 6 High |
| Waarre Formation Unit "C" | 2045 | 2053.5 | -2003.5 | 8.5 Low |
| Waarre Formation Unit "B" | 2075 | 2084 | -2034 | 9 Low |
| Waarre Formation Unit "A" | 2091 | 2103 | -2053 | 12 Low |
| Eumeralla Formation | 2131 | 2140 | -2090 | 9 Low |
| Total Depth | 2250 | 2249 | -2199 | 1 High |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 2075.5-2084 | WAARRE FORMATION UNIT "C" Sandstone (90%) with minor interbedded Claystone (10%) and minor laminations of Coal (trace). SANDSTONE: light grey, very fine to pebble, dominantly very coarse, angular to subrounded, very poorly sorted, weak silica cement, trace to common off white argillaceous matrix, clear to opaque quartz grains, trace black coaly detritus and laminae, friable, good visual porosity, no oil fluorescence. CLAYSTONE: very dark grey, slightly silty, very carbonaceous, trace slickensides, common micromica, moderately hard, slightly subfissile. COAL: very dark grey to black, slightly to dominantly very argillaceous, trace micromica, common slickensides, soft to firm. |
| 2084-2103 | WAARRE FORMATION UNIT "B" Claystone (80%) interlaminated and thinly interbedded with Sandstone (20%). CLAYSTONE: medium to dark grey to dark brown grey, very silty, often very finely arenaceous with quartz and altered feldspar grains, slightly to moderately carbonaceous, common black carbonaceous flecks and coaly detritus, trace pyrite, common micromica, moderately hard, slightly subfissile. SANDSTONE: off white to light grey, very fine to fine, dominantly very fine, angular to subrounded, moderately sorted, moderate silica cement, common to abundant white argillaceous matrix, quartzose with common altered feldspar grains, trace black carbonaceous specks and detritus, moderately hard, very poor visual porosity, no oil fluorescence. |
| 2103-2140 | WAARRE FORMATION UNIT "A" Sandstone (90%) interlaminated and thinly interbedded with Claystone (10%). SANDSTONE: off white to light grey, very fine to fine, common medium to very coarse grains, dominantly fine, angular to subrounded, moderately sorted, moderate silica cement, abundant white argillaceous matrix, quartzose with abundant altered feldspar grains, trace black carbonaceous specks and detritus, trace pyrite, moderately hard, very poor to poor visual porosity, no oil fluorescence. CLAYSTONE: medium to dark grey to medium brown grey, very silty, often very finely arenaceous with quartz and altered feldspar grains, slightly carbonaceous, common black carbonaceous flecks and coaly detritus, trace pyrite, common micromica, moderately hard, slightly subfissile. |
| 2140-2249 | EUMERALLA FORMATION Sandstone (90%) weathered at top becoming fresher with depth with interbedded Claystone (10%). SANDSTONE: light to medium green grey, very fine to medium, dominantly fine, subangular to subrounded, moderately to well sorted, moderate silica and occasional weak calcareous cement, abundant white argillaceous matrix, abundant altered feldspar and grey green lithic grains, trace red brown lithics, trace to common quartz grains, trace black carbonaceous detritus, friable, very poor visual porosity, no oil fluorescence. CLAYSTONE: medium green grey to medium brown grey, trace black carbonaceous flecks, soft, non fissile. |