| WELL: | Childers Cove-1 | REPORT No.: | 1 | DAYS FROM SPUD: | 1 | DATE: | 19/09/05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0000hrs Depth: | 84 | Last Depth: | spud | 24 HR PROGRESS: | 84 | PTD: | 2536.0mRT(1) |
| 0600 OPS: | 20/09/05 –176m – drilling ahead 12 ½” top hole in the Port Campbell Limestone, possibly the Gellibrand Marl (awaiting for more lagged sample for confirmation). |
| REMARKS: | Childers Cove-1 spudded at 1800hrs on the 19th of October, 2005. |

| PRIMARY OBJECTIVES: | Prognosed | SECONDARY OBJECTIVES: | Prognosed |
| --- | --- | --- | --- |
| Flaxman/Waarre Formation | 2349.0 m R.T. |  |  |
| Spud Date: | 18:00hrs 19/09/05 | Surface Latitude: | 38°29’31.96” | T.D. = |  | Metres R.T. |
| TD Reached Date: |  | Surface Longitude: | 142°44’46.66” | G.L. = | 46.2 | Metres ASL |
| Rig release Date: |  | Surface E (MGA94): | 0 652 295.0 | R.T. = | 51.5 | Metres ASL |
| Rig | Century Rig-7 | Surface N (MGA94): | 5 738 126.0 |  |  |
| Nearby Wells / Facilities are | 244mm Casing Shoe = |  | Metres R.T. |
|  | 178mm Casing Shoe = |  | Metres R.T. |

| Fm. Tops | Wellsite | Wellsite | Prognosed Depth | Diff | H/L |  | Sub-Sea Depth Comparisons |
| --- | --- | --- | --- | --- | --- | --- | --- |
| (* Geophysical Picks) | (mRT) | (mSS) | (mRT) | (mSS) |  |  |  | P-1ST1 | Diff | H/L |
| Port Campbell Limestone | 5.3 | 46.2 | 5.3 | 46.2 |  |  |  | 5.3 |  |  |
| Gellibrand Marl |  |  | 144.5 | -93.0 |  |  |  | -149.2 |  |  |
| Clifton Formation |  |  | 562.5 | -511.0 |  |  |  | -526.8 |  |  |
| Narrawaturk Marl |  |  | 592.5 | -541.0 |  |  |  | -546.2 |  |  |
| Mepunga Formation |  |  | 661.5 | -610.0 |  |  |  | -664.0 |  |  |
| Dilwyn Formation |  |  | 750.5 | -699.0 |  |  |  | -717.4 |  |  |
| Pember Mudstone |  |  | 1136.5 | -1085.0 |  |  |  | -936.3 |  |  |
| Pebble Point Formation |  |  | 1195.5 | -1144.0 |  |  |  | -1021.1 |  |  |
| Paaratte Formation |  |  | 1285.5 | -1234.0 |  |  |  | -1175.2 |  |  |  |  |  |  |  |  |  |
| Skull Creek Mudstone |  |  | 1756.5 | -1705.0 |  |  |  | -1643.7 |  |  |
| Nullawarre Green |  |  | 1922.5 | -1871.0 |  |  |  | -1740.2 |  |  |
| Belfast Mudstone |  |  | 2028.5 | -1977.0 |  |  |  | -1757.0 |  |  |
| Top Amplitudes |  |  | 2345.5 | -2294.0 |  |  |  | -1965.8 |  |  |
| Base Amplitudes |  |  | 2482.5 | -2431.0 |  |  |  | - |  |  |
| TD CDL-7 (shallow) |  |  | 2532.5 | -2481.0 |  |  |  | - |  |  |
| Eumeralla Formation |  |  | 2703.5 | -2652.0 |  |  |  | -2028.2 |  |  |
| TD CDL-7 (success case) |  |  | 2743.5 | -2692.0 |  |  |  | - |  |  |

Tops are wellsite picks

| Interval | ROP (ave) | Lithology Description |
| --- | --- | --- |
| Spud | - | 176.0 | 0.3-5.4 (1.5) | Massive LIMESTONE with minor MARL at later depths. LIMESTONE, off white, yellowish grey, pale olive, minor medium light grey, sparitic, micritic, common to abundant shell and coral fragments, trace green lithics, trace pyrite nodules, crystalline, microcrystalline in part, unconsolidated, friable to moderately hard. MARL, light to occasional medium grey, common shell and coral fragments, trace pyrite nodules, soft to dispersive, amorphous. |
| Gas | Units: | Nil | Composition (%): | - | / | - | / | - | / | - | / | - |
| Show Details / %CO2 | Nil |